Purpose of This Procedure

The objective is to determine and document the radionuclide composition of silt, soil, or sediment around selected air and water discharge points at Fermi National Accelerator Laboratory (Fermilab). Sample sites are selected according to their proximity to discharge points and site boundaries.

Materials/Pre-requisites Needed

# Special Precautions

- Contact the appropriate Radiation Safety Officer (RSO) for access to sampling locations within controlled areas.

- Every effort should be made to select sampling plots and individual sample cuts that are as homogeneous as possible. Avoid tilled areas or areas with unusual wind or water influence.

- Avoid sample cross-contamination and personal contamination during sampling by using accepted decontamination protocol. Wash sampling tools with Liqui-Nox® and water then thoroughly rinse with distilled water after each use.

- Wear disposable latex or Nitrile™ gloves while sampling to avoid contact with sample media and change gloves between each sample site.

- To prevent mold growth and decay of organic matter following collection, store the samples in the Environmental Sample Refrigerator at Site 39.

Equipment

##### WH7E

Surface Waters, Soil, Silt, & Vegetation Field Logbook

Fermilab Chain-of-Custody (COC) Form EP 002

Sample Identification (SID) Labels

Site 39

250ml Poly Bottles

Soil Corer (1-inch)

Stainless Steel Mixing Bowl, Spoon, and Spatula

Brush

5 Gallon Carboy with Liqui-Nox® and Tap Water

5 Gallon Carboy with Distilled Water

Disposable Latex or Nitrile™ Gloves

KayDry® Wipes

Waterproof Boots or Hip-Waders

Main Control Room

Rad Fence Key (only when needed)

References

- ASTM Designation: C 998-83, Standard Method for Sampling Surface Soil for Radionuclides, August 1983.

- ASTM Designation: C 999-83, Standard Method for Soil Sample Preparation for the Determination of Radionuclides, August 1983.

- ASTM Designation: D 420-87, Standard Guide for Investigating and Sampling Soil and Rock, October 1987.

- ASTM Designation: D 5088-90, Standard Practice for Decontamination of Field Equipment Used at Nonradioactive Waste Sites, 1990.

- DOE/EP-0023, A Guide For: Environmental Radiological Surveillance At U. S. Department of Energy Installations, Revised July 1981.

- EML HASL-300, HASL Procedures Manual, 27th Edition, Chapter 2, Section 2.4 and 2.5, Revised Feb. 1992.

- The Hazardous Waste Consultant, Soil Sampling and Analysis – Practices and Pitfalls, November/December 1992.

RESPONSIBILITIES

The sampling and analysis of soil is a useful approach to determine the accumulated concentrations of long-lived radionuclides deposited onto the ground or within sediments. Samples of selected on-site air and effluent discharge points at Fermilab are collected annually (MI-65 Stacks: North, South, East, West are sampled quarterly) for analysis of radionuclide accumulation within the soil/sediment medium. Sites are determined on the basis of annual water and air discharges, and the accelerator run schedule. Appendix A lists the current sampling locations including one background sample (Site 12). This location was chosen due to its distance from possible areas of influence. Appendix B provides maps of sample locations and Appendix C presents digital images of the actual sample points.

Factors necessary to provide meaningful information regarding terrestrial radionuclide concentrations include the location, time, frequency, size, and integrity (prior to analysis) of the sample. Additionally, samples must be representative of the area from which data is desired, and since soil is considered a heterogeneous medium, multi-point sampling (compositing) is necessary. A sample area should be vegetated and relatively undisturbed with uniform surroundings (topographical, meteorological, and climatological). All of the sites sampled for this study occur in either remote or limited access areas and are similarly influenced by climate. The ventilation stack locations are situated on the sloped sides or tops of the beamline berms and surrounded by various grasses, weeds, or ground cover plants such as Crown Vetch. The sumps discharge into drainage ditches vegetated with various grasses and cattails. Creek boundary locations are sampled midstream and are not influenced by the presence of vegetation.

Analyses are for accelerator-produced isotopes that undergo gamma decay (Be-7, Na-22, Ca-45, Mn-54, and Co-60) for all sites, plus tritium (H-3) (beta decay) for the ventilation stack discharge sites. If detected, activities of K-40 and Cs-137 are also reported; however, these are found regionally and are not the result of accelerator operations (K-40 is commonly found in fertilizers and Cs-137 in the environment is the result of nuclear bomb testing). Creeks and ditches are sampled for H-3 on a regular basis throughout the year so it is not necessary during soil/sediment sampling. All samples are submitted to the Radionuclide Analysis Facility (RAF) for analysis. H-3 activities of moisture leached from the ventilation stack soil samples are reported in pCi/ml, while soil gamma data are reported in pCi/g dry weight.

## DETAILED PROCEDURE

- Collect all sub-samples:

Soil - Ventilation Stack and Background Locations

  - Insert the soil corer into the soil, twist and remove.

  - Use the spatula to transfer the top 5cm of the core into the stainless steel bowl.

  - Repeat to collect 10-15 sub-samples over an area of about 1m2.

##### Sediment - Creek and Sump Discharge Locations

- Collect a spoonful of the top 5cm of sediment in the immediate vicinity of the discharge pipe.

- Place the sediment into the stainless steel bowl.

- Repeat to collect 10 sub-samples over an area of about 1m2.

Note: Fewer cores are required if using a larger corer; however, a minimum of 10 cores is required under all circumstances.

  - Thoroughly mix and pulverize the sub-samples with the spoon, discarding rocks, roots, and vegetation (if possible), and composite into the 250ml sample bottle. Discard any excess soil/sediment in the location it was collected.

  - Wipe the sample bottle clean and label it with a SID and sample type.

  - Complete the COC and field logbook.

- Clean all of the sample equipment using Liqui-Nox® soap and water then thoroughly rinse with distilled water and dry with a KayDry® before proceeding to the next sample area.

- Complete a RAF Work Request and relinquish custody of the samples to RAF personnel. After they sign the COC, make a copy for the EP Group file on WH7E.

- Store the samples in the Environmental Sample Refrigerator at Site 39. Place the original COC in the plastic jacket on the outside of the refrigerator door.

- Return the COC copy to the EP Group file on WH7E for storage until analytical results are received.

## Appendix A

Sample Site Characteristics for Annual Soil/Silt/Sediment Sampling

(Locations determined annually)

_________________________________________________________________________________________

#### Site	Site Type	Discharge Type	Sample Point

_________________________________________________________________________________________

Kress	Creek	N/A	Upstream Boundary

Kress	Creek	Water	Transfer Ditch

Ferry	Creek	Water	Spillway

Indian	Creek	Water	Spillway

M01 SP5	Sump Discharge	Water	Discharge Pipe

N01 SP7	Sump Discharge	Water	Discharge Pipe

AP0	Ventilation Stack	Air	Stack

M01	Ventilation Stack	Air	Stack

M05	Ventilation Stack	Air	Stack

MI-12A	Ventilation Stack	Air	Stack

Q409	Ventilation Stack	Air	Stack

Site 12	Background	N/A	Farm Well

MI-65 N,S,E,W	       Ventilation Stack	                Air		    Stack

_________________________________________________________________________________________

## Appendix B

Sample Location Maps

## Appendix C

Sample Location Digital Images

Kress Creek Upstream Boundary - Turnoff from Fabyan Parkway. View is easterly.

Kress Creek Upstream Boundary - Sample from east bank near Fabyan Parkway viaduct. View is westerly.

Kress Creek Transfer Ditch - General location. View is southerly.

Kress Creek Transfer Ditch - Sample from center of ditch. View is northerly.

Ferry Creek Spillway - Sample around spillway from A.E. Sea. View is westerly.

Indian Creek Spillway - Sample from bank of Swan Lake Channel near spillway. View is to westerly.

M01 SP5 Discharge - Sample at the concrete discharge pipe located on the east side of the Meson berm downstream of MS1 Service Building. View is southwesterly.

N01 SP7 Discharge - Sample at the corrugated metal discharge pipe on west side of Neutrino berm downstream of NS1 Service Building. View is southeasterly

.

AP0 Stack - Sample taken around the base of the stack. View is southeasterly.

M01 Stack - Collect sample from around base of the stack located on the east side of Meson Berm upstream of M01 Service Building. View is northerly.

M05 Stack - Access road on West side of Meson Berm. Stack is located on top of berm. View is northerly.

M05 Stack - Collect sample from around the base of stack located on top of Meson Berm south of the Meson Detector Building. View is northerly.

MI-12A Stack - Collect sample from around concrete base of stack. View is southerly.

Q409 Stack - Collect sample from around base of stack located on Main Injector Berm  east of MI-40 Service Building. View is easterly.

Site 12 (Background) - Collect sample from around the base of Well 12. View is southerly.