## Slide 1: New experimental station at ATLAS
October 5, 2021
Matt Hendricks
ATLAS Operations Manager

## Slide 2: outline
ATLAS orientation
New experimental station at ATLAS
Hazards
Hazard mitigation
Questions

## Slide 3: Overview
DOE National User Facility for low energy nuclear physics research
3 distinct accelerator sections
  50 superconducting resonators, total voltage of 52MV
Typical 1 to 500 pnA range currents, higher possible for some species
H through U stable isotopes available, some radioactive species too
CARIBU – radioactive isotopes via 252Cf source to either:
  ATLAS
  1 of 4 stopped target stations; 1 in assembly stage
6 accelerated target stations
  1 new target stations in assembly stage
New experiment every week on average;
  24/7 operation ~40 weeks/year
  26 FTEs operations side
Quick stats:

## Slide 4: Credited controls
Shielding
Beam Current Monitor
  Redundant passive pickups, stops beam when above threshold
ARIS (ATLAS Radiation Interlock System)
  Permits personnel access to areas with accelerated beam only if:
    Dose rate < 5mrem/hr
    Accumulated dose < 20 mrem/8 hr (rolling)
  Talk on this system by J. Clark - tomorrow
NARIS (New ATLAS Radiation Interlock System)
  CARIBU’s interlock system
  Cannot stop radiation, only warn that levels are above threshold

## Slide 5
Source to target maximum length: ~130m

## Slide 6: New target area motivation
Nuclear astrophysics question
  Improved understanding of the r-process
  Occurs in neutron rich nuclei
AREA126
208Pb + 9Be at 1 GeV/u
(fragmentation reaction with best cross-sections for N = 126)
136Xe + 198Pt at 10 MeV/u
(best multi-nucleon transfer (MNT) reaction)

## Slide 7: Multi-nucleon transfer
198Pt (target)
136Xe (projectile)

## Slide 8: Multi-nucleon transfer
Neutron donation
+6 neutrons
204Pt (target)
130Xe (projectile)
-6 neutrons
neutron
proton

## Slide 9: Multi-nucleon transfer
204Pt (target-like)
130Xe (projectile-like)

## Slide 10: Separation
Cooler-Buncher
Separated cooling and bunching sections, simplified electrode construction, optimized injection optics
Gas Catcher
Takes a continuous, isotopically mixed, low energy beam
Bunched, isotopically pure, low-emittance beam
Multi-Reflection – Time Of Flight
Mass Resolution in excess of 105
Deliver isotopically pure beams to experiments
beam dump

## Slide 11: Tight fit
Very cramped space for 2-dimensional installation
Beam axis
Exterior wall
Adjacent to beam transport
Concrete ceiling from past experimental setup

## Slide 12: Innovative solution (at least for us)
Use 3rd dimension
Platform instead of “ceiling”
Beam to other targets
Beam axis
(Target just inside port)
Notes: Over the past 4 years the average BRP has been 733 mrem/hr

## Slide 13: Current status
Beam axis

## Slide 14: Hazard matrix
 | Current |  | Future | 
 | Radiation | Other | Radiation | Other
Ground Floor | Adjacent beams | SIH | Adjacent beams In room beams Activation | SIH
Elevated Platform | Adjacent beams | SIH | Adjacent beams | SIH
SIH = Standard Industrial Hazards
Typical beam for experimental area: 136Xe @ 10MeV/u, 1pμA
- Estimated radiation: 72 rem/hr @ 0⁰ and 13.1 rem/hr @ 90⁰ (at 1m)

## Slide 15: loss points close to platform
AREA126 platform
Notes: Illustrates worker proximity to unshielded beam and loss points, due to being above shield wall.

## Slide 16: Beam Radiation potential since 2017
Chart: Beam Radiation Potential (rem/hr)
Beam Radiation Potential (BRP): Predicted maximum radiation for that experiment, scaled from explicit measurement (90⁰ @ 1m)
85% of beams had BRP<1 rem/hr
Facility limit: 100 rem/hr @ 1m (any direction)

## Slide 17: hazard mitigation – through 2021
Prompt Radiation Mitigation
Ground floor – interlocked by ARIS (ATLAS Radiation Interlock System)
Stairs to platform
  Locked and posted
  Access only granted without beam or with health physics review
Remaining Hazard Mitigation
Standard industrial hazards captured by ATLAS/PHY/ANL policies or procedures

## Slide 18: hazard mitigation – 2022 and beyond
Prompt Radiation Mitigation
Add platform area into ARIS; separate area
  Permits access only when:
    Instantaneous radiation is < 5 mrem/hr
    Integrated radiation is < 20 mrem/8 hr
  Above 100 mrem/hr area is physically locked
  Integration Jan. 2022
Remaining Hazard Mitigation
Standard industrial hazards captured by ATLAS/PHY/ANL policies or procedures

## Slide 19
Thank you. Questions?