## Slide 1: A New Experiment to Verify/Refute the OPERA Result
Michael Schmitt
Mayda Velasco
Northwestern University
October 24, 2011
Fermilab Neutrino Workshop

## Slide 2: Motivation
OPERA observed neutrinos arriving DT = 60.7 ± 6.9(stat) ± 7.4(syst) ns
too early.
Given their baseline, this corresponds to a velocity faster than the speed of light by
(v-c)/c = ( 2.48 ± 0.28(stat) ± 0.38(syst) )× 10-5
This result needs to be verified (confirmed or refuted) by an independent experiment, preferably with different methods.
There have been three points of criticism of the OPERA analysis:
  synchronization of CERN and LNGS clocks using GPS
  possible time-dependent primary beam & horn effects
  reliance on p waveforms to represent n waveforms
arXiv:1109.4897 (23-Sep-2011)

## Slide 3: Concept
Design Goals:
  use direct-sight laser for synchronization
  build in comparisons to relativistic non-n particles
  eliminate or minimize the statistical cost of long spills
  allow for changes of n beam parameters (especially energy)
Method:
  10km decay tunnel – laser propagates from target to detector
  p  mnm mainly in first 1-2 km; nm travels most of the distance
  allow m to reach the detector - compare TOF of m and nm
  take advantage of the time structure of the Main Injector / NuMI beam
(see also Kalbfleisch, PRL 43 (1979) 1361)
p
p
n
m
decay tube
target
detector
laser

## Slide 4: (some) Details
primary beam
  120 GeV Main Injector beam – very similar to current NuMI beam
    about 500 p batches, each batch is 8 ns long, 18.8 ns between batches
    assume 1019 to 1020 protons on target
    laser is synched to p batches via electrostatic pick-up, and detected/read-out through same device/channels as neutrino events
decay tube
  10 km long, on surface (not underground) filled with He at low pressure
  a small fraction of muons and some undecayed pions reach the detector
detector
  collects four kinds of signals:
    laser pulses
    neutrinos from pion decays
    muons from (other) pion decays
    “dual events” in which both the muon and the neutrino from a single pion decay interact in the detector
make a direct comparison

## Slide 5: Detector Concept
basic parameters
  transverse position resolution to 1 cm
  longitudinal position resolution to 3 cm
  time resolution to 10 ps
design
  sampling calorimeter with transverse segmentation
  dense material such as brass induces the showers
  quartz fibers provide fast narrow signal
    Cherenkov light from shower e±
    very good time characteristics
    showers appear narrow and compact
    energy resolution not great
  if necessary for position resolution, some layers of wire chambers, GEMs?
  inter-channel synchronization via laser pulse system and incoming muons

## Slide 6: Feasibility Study (1)
simulation
  simple PYTHIA at particle level
  incoming 120 GeV p beam on fixed p target
  define fiducial region for detector
  simple Gaussian smearing of position and time coordinates
physics assumption
  focus on TOF measurement
  take OPERA result as pertaining to n velocity
  for 10 km flight distance, TOF anomaly would be 0.8 ns (out of 33 ms)
yields
  about 4 × 10-5 neutrinos per proton: 4 × 1014 ns for 1019 pot
  s ≈ 4 × 10-38 cm2 1x1x3 m3 brass or iron: 24 tons
  2 × 104 charged-current events (twice OPERA sample)
  (MINOS near detector, 1kton, 1km away, > 106 events for 1020 pot)
(units for all forthcoming plots are meters and nanoseconds)

## Slide 7: Feasibility Study
n TOF in ideal case
TOF smeared by
position and time resolution
normal
TOF
if OPERA result
is correct

## Slide 8: Feasibility Study (2)

## Slide 9: Feasibility Study (3)
Observed time with respect to laser pulse.
Black histograms indicate reference distribution coming from muons and hadrons.
normal case
if OPERA result
is correct

## Slide 10: Feasibility Study (4)
normal case
if OPERA
result
is correct
toy fit
  assume only 1000 events
  perform an unbinned likelihood fit
  approximate the total resolution on TOF by a Gaussian s = 27 ps
  analytical function (convolution of a top-hat distribution and a Gaussian)
  huge difference in –NLL comparing the normal SM neutrino and the case in which the OPERA result is correct

## Slide 11: Feasibility Study (5)
dual events
  a pion decays and both the muon and the neutrino interact
  which one reaches the detector first?
  many resolution effects cancel
  event is “self-synchronized”
  events are biased toward
    higher energy
    decays closer to the detector
  still extremely powerful
  can expect hundreds of events
if OPERA result
is correct
normal case
(smeared)

## Slide 12: Summary
We have presented a concept for an experiment to verify or refute the OPERA results.
It bypasses all of the criticisms of the OPERA analysis.
It can be done with the NuMI beam line.
It requires a several-km decay tunnel.
It requires a detector carefully designed for time & position resolution
  assumed parameters are very challenging but not insanely so
  detector design is notional
If 10 ps is achieved, the tunnel can be shortened; if we have a 10 km tunnel, then 50 ps is good enough.
We can avoid using a horn
If the anomaly is confirmed, would vary neutrino parameters.

## Slide 13
extras

## Slide 14
Yields
simulate 4M pp collisions (120 GeV on fixed target)
for 4m x 4m
  3200 nu produced: yield is 8 x 10-4
    38% anti-nm and 62% nm
  15000 non-nu particles hit the detector: about 50 per nu
  4000 of these are muons (should be about the same as nu)
  about 100 dual events (3% of nu events)
for 1m x 1m, scale by 1/16
  5 x 10-5 nu per p
  6 x 10-5 muons per p
  1 x 10-6 “dual events” per p

## Slide 16
dual events
n
m

## Slide 17
dual events
mean neutrino decay distance (m)

## Slide 18
RHIC ZDC
quartz fibers
NIM A470 (2001) 488

## Slide 19
The inference of dt was done “blindly” – i.e., with an unknown offset.
The offset was corrected after the fits were completed and finalized.
OPERA

## Slide 20
OPERA

## Slide 21
also checked:
  day vs. night
  summer vs. fall+spring (no data during winter)
  “closure test” of fitting
    toy MC shows that intentional shift measured at better than ns level with expected statistical uncertainty
  for the actual fit to data,
    c2 / ndf = 1.06 for extraction 1, 1.12 for extraction 2
60 ns
OPERA

## Slide 22
right: the final result. left: divide in two energy bins.
OPERA