## Slide 1
Particle Accelerator Applications
Thomas Kroc, PhD
SIST – Summer Lecture Series
29 June 2021

## Slide 2: Accelerators built in the pursuit of science now have major impact on the economy… but many more opportunities
Radial Tires
About 30,000 accelerators are in use world wide
  Sales of accelerators > $ 2 B /yr and growing at 10% per year
  Accelerators touch over $ 500B/yr in products
  Major Impact on our economy, health, and well being
Some Products:
Digital Electronics
Shrink wrapped food
Aircraft

## Slide 3: Opportunities
We also imagine other transformational uses of accelerators like:
  Medical Device Sterilization
  highway lifetime extension
  hard rock tunneling

## Slide 4: What’s New?
All new accelerators for discovery science are superconducting.
But current SRF “science” accelerators are large and complex
Why SRF?
  Higher gradient, more energy per unit length
  More efficient, less wasted energy
LCLS-II Cryomodule
FNAL FAST 50 MeV injector and ILC cryomodule
CBEAF CW electron linac
2 K cryoplant
SRF Proton Linac
Spallation Neutron Source at ORNL

## Slide 5: What we are doing
We are combining a number of state-of-the-art technological advances into a simple to operate, compact, superconducting RF accelerator.
Inexpensive (relatively)
Efficient
  > 80%,mains to e-beam
Turn key operation
High reliability
 10 MeV
 250 kW
 0.7m  x 1.5 m long

## Slide 6: Heat
Eliminate liquid cryogens
Conduction cooling
  No LHe
Commercial cryocoolers
  2W each @ 4 K

## Slide 7: Conduction Cooling
4K
X78443 (D2)
X63112 (C4)
X42268(D3)
X63115 (C3)
X78442 (D5)
X78441 (C2)
42266 (D4)
X78440 (C5)
X8
Heater
40 Ohm,10W
X4
X1
X2
X7
X6
X5
X3
162
46
15
10
20
80
80
60K
300K
Copper wires
Phosphor-bronze wires
Connection
Thermal
anchoring
block
Cold head(s) of the cryocooler(s) connected to cavities by high purity aluminum
Heat Budget
4 – 6 W
US patent applications
#15/280,107
#14/689,695
Notes: This novel and proprietary configuration (Patent application #62/234,475) results in dramatic reductions in complexity, size, weight, and cost.

## Slide 8
Solid state or
Magnetron
Power Supply
Cryo-cooler
Compressor
The Compact SRF Accelerator
Integrated
Electron
Gun
Cryo-cooler
Cold Head
Low
Heat-loss
RF Coupler
Nb3Sn
Coated Cavities
No LHe

## Slide 9: Comparison of Gammas, X-rays, and e-beam
Chart: Energy Spectra
Chart: Depth of Penetration
| -2.8462998102470001E-2 | 0.19924098671730001 | 0.31309297912709999 | 0.48387096774190003 | 0.54079696394690002 | 0.68311195445920003 | 0.76850094876660002 | 0.91081593927890003 | 1.2239089184059999 | 1.6508538899430001 | 2.0777988614799998 | 2.732447817837 | 3.3870967741940001 | 4.1555977229599996 | 4.9525616698289996 | 5.777988614801 | 6.8311195445920001 | 7.7419354838709999 | 8.5388994307400008 | 9.8197343453509998 | 10.81593927894 | 11.92599620493 | 13.06451612903 | 14.089184060719999 | 15.11385199241 | 16.22390891841 | 17.47628083491 | 18.814041745730002 | 20.037950664139998 | 21.034155597720002 | 22.087286527509999 | 23.225806451610001 | 24.278937381399999 | 25.360531309300001 | 26.925996204930001 | 28.178368121439998 | 29.089184060720001 | 30
10 MeV X-ray | 39.6725 | 47.2528 | 54.9805 | 63.006 | 70.1388 | 75.9352 | 80.8394 | 87.0815 | 93.1768 | 98.0844 | 99.5745 | 98.5409 | 96.4671 | 93.9488 | 90.8363 | 87.5755 | 83.4255 | 80.017 | 77.3503 | 73.3511 | 69.9434 | 66.0911 | 62.8334 | 59.7232 | 57.0588 | 54.5438 | 51.4358 | 48.1801 | 45.3691 | 43.1501 | 40.9317 | 39.0114 | 36.793 | 35.1692 | 32.9559 | 31.0367 | 30.0056 | 28.8259
9 MeV electrons | 81.129 | 84.1044 | 89.3104 | 93.772 | 97.192 | 99.7214 | 99.7251 | 96.7556 | 92.3005 | 84.2792 | 76.8515 | 71.652 | 64.967 | 57.2409 | 49.6646 | 42.6821 | 35.1052 | 28.5684 | 20.8435 | 13.8613 | 7.7711 | 3.7629 | 1.6866 | 1.2496 | 1.412 | 1.4255 | 0.98965
Co-60 | 50 | 58.4158 | 68.9769 | 77.3927 | 82.5083 | 85.6436 | 87.7888 | 90.5941 | 92.9043 | 94.7195 | 96.3696 | 97.6898 | 98.6799 | 98.6799 | 97.8548 | 96.2046 | 94.2244 | 92.4092 | 89.934 | 87.6238 | 84.9835 | 81.8482 | 78.5479 | 76.2376 | 73.4323 | 70.132 | 67.8218 | 65.1815 | 62.2112 | 59.2409 | 56.1056 | 53.3003 | 50.165 | 47.5248 | 44.8845 | 42.5743 | 40.099 | 38.1188 | 35.8086 | 33.6634 | 31.0231 | 29.2079 | 27.5578 | 25.7426 | 23.7624 | 22.9373 | 21.7822 | 21.2871 | 21.1221

## Slide 10: Accelerators for the Environment: Flare Gas
Trailer mounted high power electron accelerators
Natural gas turbines provide the local electrical power
Liquid hydrocarbons created can be mixed and collected with crude oil produced by the well
Liquid hydrocarbons
Nat Gas
Gas turbine generator
Accelerator and RF Power
e.g. nCH4  CnH2n + H2
Details are Proprietary
Unconverted Nat Gas + Hydrogen drives gas turbine for power
High revenue can fund accel design
1 well flares ~ $ 5 M/yr for 1-2 yrs

## Slide 11: Contaminated Soils

## Slide 12: Contaminated Soils

## Slide 13: Mobile EB to extend lifetime of highways
1400 KW  2 lane-miles per 8 hr shift
Cost of 1 lane-mile interstate highway = $ 2.4 - 6.9 M
Huge value added ~ $ 500 K- $1.4 M per shift (1 yr extension)
$ 5-8 M capital cost  very short payback period!

## Slide 14: Sewage & Sludge Treatment

## Slide 15: Medical Device Sterilization

## Slide 16: Ballast Water

## Slide 17
Thank you