## Slide 1
Elvin Harms
Workshop on Maintaining PIP-II within the Accelerator Complex
15 July 2021
Accelerator Systems Considerations

## Slide 2: Introduction
“During the yearly planned 8-week shutdowns, the PIP-II Linac will remain cold (<20 K) for Accelerator Complex maintenance activities. During beam operations the PIP-II Linac is required to have 90% uptime availability”
Consider PIP-II operational expectations within the Accelerator Complex (AC), such as maintainability and operability of major systems, projected beam availability per year, and cryoplant and cryomodule operational assumptions.
Workshop Charges:
Understand the projected beam availability per year of the AC in the PIP-II era. What drives the duration of yearly planned AC shutdowns and can the duration be shortened?
Define the operational expectations for PIP-II, especially with regards to cryoplant and cryomodules during scheduled AC shutdowns. Is the design of PIP-II systems compatible with these operational requirements?
Identify the interfaces between the AC, Lab infrastructure and PIP-II. What are the expectations for maintenance and operation? Are there redundancies in systems to maintain operability

## Slide 3: Controls
Will the Controls system for the Linac support cryo operations during Accelerator Complex maintenance periods?
  Will network and server maintenance impact EPICS communication with
    Vacuum systems (PLC readback and controls)
    Cryo Plant controls (e.g. valve control)
How are servers in the Controls system maintained during maintenance periods
  Are there expectations of system upgrades during shutdowns which require loss of communication?
Impact of Controls failure or shutdown
  Can failure of a PLC, the whole unit or a module, lead to a loss of control and warmup of the CP? Linac? Linac vacuum?
  Can maintenance or failure of Controls infrastructure (network, EPICS servers, databases, etc.) lead to a loss of control and warmup of the CP? Linac? Linac vacuum?
How are failures of Controls rectified?
  Are there redundancies in the Controls system?
  Spares for vacuum PLC modules?
  Spare servers, VME cards?

## Slide 4: Controls
Typically, the summer shutdowns are when all major Control system work (non-emergency) gets scheduled
  Maintenance
  updates to hardware
  firmware updates
  operating system updates, etc.
Depending on what's being updated, outages could occur.
Coordinate major disruptions to the overall system with the scheduled power feeder outages
  two main summer shutdown outages that take down the control system as a whole are the CUB outage (typically 2 days, no cooling to MAC & AD Computer Room)
  x-gallery power outage (~8 hours no power to MAC & Computer Rooms)
  take down all the system servers and the main network switches in the computer room
  UPSs for the computer room and MAC room can ride out shorter outages, but not ones of this length
  lose the ability to monitor systems located around the site, but do not take down the local systems (VME, PLC, etc.) so long as they remain powered.
  System spares for PLCs, VME crates & cards, along with other field hardware normally on-hand
  Some server backup hardware is available

## Slide 5: Controls
Upgrades to network switches - don't take very long but to avoid disruption to PLC controls this would have to be planned more carefully
System upgrades - core controls servers and the database. Each one does not take long but there can be many of them. This has been tolerable in past summer shutdowns but again more careful planning will be required
Upgrades to the many rack mount servers – Individual updates don’t take long but there are many servers. In the future these will run containerized operating systems, individual updates should require minimal downtime.
Control system historically has been very modular and fault tolerant
  Many failures do not affect beam delivery. But if it is necessary to keep the cryomodules cold for many years through shutdowns that will require special attention
  Need to assess and learn from existing high availability facilities e.g. APS, SNS

## Slide 6: Vacuum
What components of the vacuum system have to be maintained and serviced during operations?
Are there vacuum system components that require warming up the Linac to be maintained/serviced or in case of failure?
  For example, can failure or maintenance of a vacuum PLC cause loss of vacuum in the Linac
We should be able to operate vacuum equipment in time intervals longer than 6-month operating periods.
Also, we should be able to design redundancy with vacuum gauges and controllers to meet the required operations runtime.

## Slide 7: Safety Systems
System | Testing cycle | Duration | Beam state | Access
Electrical | Every 6 months with a 4- month grace period | 4 hours | Beam is off | access to the enclosure is needed
Radiation Safety | Every 6 months with a 4- month grace period | 2 hours | Beam is off | 
ODH Cryo Building | Every 6 months with a 1- month grace period. | 4 hours | no effect on beam in Linac | 
ODH Linac | Every 6 months with a 1- month grace period. | 4 hours | Beam is off | access to the enclosure is needed
Laser Lab | Every 12 months with a 1-month grace period | 4 hours | Beam is off | access to the enclosure is needed

## Slide 8: Beam Instrumentation
Normally don’t require any sort of regular maintenance. However, there may be some conditions for PIP-II.
BPM-based absolute beam energy measurements
  might require regular (yearly?) calibration/tunnel access
Laserwire system
  Significant radiation might lead to need to replace optics or optical fibers on a regular basis
  darkening of the vacuum viewports or problems with the electron collection detector (e.g. scintillator aging) - open the warm units areas between the cryomodules to do any work. This is much more serious because we’ll have to open vacuum and work in a particle-free environment.
  Safety may have to regularly (yearly?) test the laserwire safety system. This is probably going to need to happen.
BCM
  Routine calibrations for MPS

## Slide 9: Machine Protection System
Any maintenance/upgrades should be able to be accommodated during planned maintenance
  Assuming no ad hoc requests
However, considering its critical function
  Routine (automated) system checks and calibrations
    Beam-measuring devices
    Configurations
    Input masks
Could very well be daily, weekly, monthly checks with no-beam periods
  LCLS-II anticipating this

## Slide 10: Magnets/Power supplies
Power supplies
  All racks will be fan cooled
  Goal is to operate supplies in their mid-range to reducing failure rates
  any mechanical device will require maintenance and replacement
  Filters will need to be cleaned
  Maintenance for the DC contactors we are planning on using for the dipole strings
  Over time power supplies will fail
  Annual maintenance will be needed
Magnets
  biggest operational concern is water cooling
  minimum water-cooling passage diameter of 5 mm but it is always possible over time for passages to get clogged which would require back flushing
  klixons on the coils to monitor the temperatures
  Filters would need maintenance at some rate

## Slide 11: Low Level RF
8-weeks is sufficient for normal maintenance & upgrades
  LLRF can suffer in shutdowns from:
    LLRF is working great – don’t change anything during the shutdown
    There seems to be problems with LLRF – don’t change anything during the shutdown
    Upgrades should coordinated as part of multi-year program planning
    Automation will be key for quick recovery from shutdown work
Unplanned power outage/extended warmup – cavity tuner control to park tuners in safe state
  If (Since) LLRF and Controls are on Generator/UPS then this could be automated
  Long power outages are rare but UPS carts could connect to Resonance Control Chassis one at a time in the Gallery
Reliability
  LLRF is generally reliable but subtle issues are hard to track down.
  Treating LLRF as both a controller and as part of a larger diagnostics package is a good approach

## Slide 12: High Power RF
Current design anticipates an amplifier failure (discrete component) every 30 days
  ~3-hour replacement time
Full cabinet replacement expected to be infrequent
  Likely ‘on the fly’
Build on PIP2IT and 32 kW experience

## Slide 13: Summary
Accelerator Systems maintenance work should fit within annual period
Necessary maintenance/outage durations should have no/little impact on keeping linac cold (<20K)
Ensure robust backup power (generator rather than UPS) for critical systems (LLRF & Controls)
Assess and learn from high availability facilities
This workshop is an excellent start; further thought and coherent planning needed