Advanced Tools for Physics-Based Modeling of Radiation Effects in Nanoscale

Microelectronics

Marek Turowski and Alexander Fedoseyev

CFD Research Corporation, Huntsville, Alabama 35805, USA

The recent enhancements to CFDRC's NanoTCAD 3D mixed-mode simulation package, combining physics-based models of nano-scale semiconductor devices and unique mixed-mode interface to the Cadence Spectre circuit simulator, have enabled simulations and in-operation analysis of ionizing radiation single event effects (SEEs) in modern high-speed electronic technologies and integrated circuits. Additionally, the NanoTCAD'  new, automated interface to Geant4 radiation models and the 3D solver capability to model very low temperature behavior, enable a comprehensive and accurate modeling of radiation effects in advanced microelectronics in the extreme radiation and temperature environments. Example simulations of SEEs affecting digital output of multi-GHz mixed-signal circuit are presented. Our 3D mixed-mode modeling results compare very well with experimental data. The developed approach has also been successfully applied to modeling of radiation damage in semiconductor materials in photodetectors and solar cells used in high-radiation space environments.

Radiation Hardening - exploring and developing a variety of approaches to make integrated circuits (ICs) and microelectronics devices resilient to radiation. Development of radiation-hardened, or rad-hard, microelectronic components requires changing designs and/or altering manufacturing processes. Computer modeling may significantly speed up this process.