## Slide 1: Re-engineering Frameworks for Concurrency
FNAL, 21-22 November 2011
B. Hegner & P. Mato, CERN

## Slide 2: Vision
Universal framework for simulation, reconstruction, analysis, high level trigger applications
Common framework for use by any experiment
Decomposition of the processing of each event into ‘tasks’ that can be executed concurrently
Ability to process several events concurrently
Optimal scheduling and associated data structures
Minimize any processing requiring exclusive access to resources because it breaks concurrency
Supporting various hardware/software technologies
Facilitate the integration of existing LHC applications code (algorithmic part)
Quick delivery of running prototypes. The opportunity of the 18 months LHC shutdown

## Slide 3: Why?
We need to adapt current applications to the new many-core architectures
  Expected no change in the overall throughput with respect trivial one-job-per-core parallelism
  Scaling to a much larger number of cores
Reducing the required resources per core
  I/O bandwidth
  Memory
  Connections to DB, open files, etc.
Reduce latency for single jobs (e.g. trigger, user analysis)
  Run a given job in less time making use of available cores

## Slide 4: Why the Framework managing the concurrency?
Concrete algorithms can be parallelized with some effort
  Making use of Threads, OpenMP, MPI, GPUs, etc.
  But difficult to integrate them in a complete application
    E.g. MT-G4 with Parallel Gaudi
  Performance-wise only makes sense to parallelize the complete application and not only parts
Developing and validating parallel code is difficult
  ‘Physicists’ should be saved from this
  Concurrency will limit what can and can not be done in the algorithmic code (policies)
At the Framework level you have the overall view and control of the application

## Slide 5: Concurrent ‘Task’ processing
Framework with the ability to schedule modules/algorithms concurrently
  Full data dependency analysis would be required (no global data or hidden dependencies)
  Need to resolve the DAGs (Direct Acyclic Graphs) statically and dynamically
Not much gain expected with today’s designed ‘Tasks’
  Algorithm decomposition can be influenced by the framework capabilities
‘Tasks’ could be processed by different hardware/software
  CPU, GPU, threads, process, etc.
Time
Input
Processing
Output

## Slide 6: Example: LHCb Reconstruction
DAG of Brunel
  Obtained from the existing code instrumented with ‘Auditors’
  Probably still missing ‘hidden or indirect’ dependencies (e.g. Tools)
Can serve to give an idea of potential ‘concurrency’
  Assuming no changes in current reconstruction algorithms

## Slide 7: Many Concurrent Events
Need to deal with the tails of sequential processing
Introducing Pipeline processing
  Never tried before!
  Exclusive access to resources or non-reentrant algorithms can be pipelined e.g. file writing
Need to design or use a powerful and flexible scheduler
Need to define the concept of an “event context”
Time

## Slide 8: Concurrency Programming
It is not simple but we are not alone
  Technologies like the Apple’s Grand Central Dispatch (GCD) are designed to help write applications without having to fiddle directly with threads and locking (and getting it terribly wrong)
New paradigms for concurrency programming
  Developer needs to factor out the processing in ‘chunks’ with their dependencies and let the framework (system) to deal with the creation and management of a ‘pool’ of threads that will take care of the execution of the ‘chunks’
  Tries to eliminates lock-based code and makes it more efficient

## Slide 9: Framework as a Set of Services
Better than a “new” complete and self-contained framework, LHC experiments would like to see a set of functional components from where to pick and choose what to incorporate into their frameworks
  Experiments have a huge investment in ‘algorithmic’ code and configuration based of a specific framework
Complete solution should be provided for new experiments
  The previous constraint does not apply to new experiments
  The timing is less critical for them

## Slide 10: Framework Services
EventStore
EventStore
Algorithm
Algorithm
Algorithm
Logging
Configuration
Persistency
Data Store
B-Field
Geometry
Material
Random
Scheduling
(*) Any resemblance to Gaudi is pure coincidence
const
non-const
Services
Direct Acyclic Graph

## Slide 11: Single “Memory Model” is Essential
Algorithm scheduling will be driven by the semantics of the memory model
  Knowing what data items an Algorithm “consumes” (reads) and “produces” (modifies, creates) determines when it can be scheduled without conflicts
Thorough design of shared “Services”
  Ensure state integrity (e.g. caches)
  Avoid case-by-case ad-hoc solutions
Products like ROOT and Geant4 will need to be accommodated to the same memory model

## Slide 12: Development of Key Services
“Concurrent White Board” (multi-event data store)
  Data declaration (in, out, update)
  Get synchronized data access (being executed)
  API for input, output, update and commit
“Dispatch Service” (scheduler)
  Management of task queues and threads
  For example could be based on GCD
“Logging Service”
  Ensuring message integrity
  Sorting by event

## Slide 13: Prototyping of Physics Services
Modeling them as ‘servers’
  Genuinely asynchronous
  Supporting concurrent clients (caching issues)
  Possible use of new hardware architectures (e.g. GPU, MIC)
E.g. Random Service
  Reproducibility in a concurrent environment
E.g. Magnetic Field Service
  Given a point, return the best estimate of the B-field
  It may involve complex interpolations and/or parameterizations
E.g. Material Service
  Given two points, return the best estimate of material between them

## Slide 14: Concurrency in Geant4
With an approach like the GDC we could exercise different factorizations
  Processing each event (set of primary particles) could be the ‘task’ (same as GeantMT)
We could also go at the sub-event level
  Development of Rene’s ideas of ‘baskets’ of particles organized by particle type, volume shape, etc.
  Would need to develop an efficient summing (‘reduce’) of the results
  Would require to study the reproducibility of results (random number sequence)

## Slide 15: Re-using Algorithmic Code
Data Store
Collection
Collection
It is essential to be able to re-use existing algorithmic code
We need to explore whether existing modules/processors/algorithms could be wrapped and interfaced to the new services
  Performance would not be great but could be used to evaluate the real benefits for concurrency
  Adiabatic adaption
Obviously the issues of re-entrance and thread safety remains
Algorithm
Marlin Processor
EventProxy
Collection

## Slide 16: Project
Collaboration of framework developers of CERN, FNAL, LBL, DESY and possible other Labs
  Start with small number of people (at the beginning)
  Open to people willing to collaborate
  Strong collaboration with ATLAS and CMS (and others)
    E.g. Instrumentation of existing applications to provide requirements
  Strong collaboration with Geant4 team
Quick delivery of running prototypes (I and II)
  First prototype in 12 months :-)
Agile project management with ‘short’ cycles
  Weekly meetings to review progress and update plans

## Slide 17: R&D Activities
Investigate current LHC applications to gather requirements
  Dependencies, data access patterns, opportunities for concurrency
Investigate design and implementations of state–of-the-art concurrency frameworks
  Scheduling (static, dynamic, adaptive), memory model, I/O
Prototype framework elements
  Identify ‘exemplar’ algorithms to be parallelized
  Data structures and memory allocation strategies
  New languages (C++11, Go, pypy, …)
  and libraries (OpenCL, CnC, STM, …)
The idea would be to organize these R&D activities in short cycles
  Coordinating the interested people to cover all aspects
  Coming with conclusions (yes/no) within few months

## Slide 18: Straw man Project Timeline
2011
2012
2013
2014
LHC shutdown
Today
R&D, technology evaluation and design of critical parts
Services and Integration Prototype I
Initial adaptation of LHC and Geant4 applications
Complete Prototype II with experience of porting LHC applications
First production quality release
Project definition

## Slide 19: Summary
Presented initial ideas for the development of a set of generic data processing framework services with concurrency to exploit new CPU/GPU architectures
LHC experiments should be the main players providing specific requirements, participating into the project development and taking advantage of the new framework
  Would imply some re-engineering of parts of the experiment applications
Need a R&D program to evaluate existing technologies and development of partial prototypes of critical parts
Some initial ideas for the project definition being outlined