## Slide 1
Matthew Hoppesch, UIUC
Supervisors – Jeffrey Eldred and David Neuffer
SIST Internship
11 August 2021
H- Injection Simulations for Multi-MW Upgrade

## Slide 2: Motivation
Beam Power upgrades at Fermilab have the goal of delivering more power to the DUNE/LBNF experiments
Injection at higher energies allows for higher intensity -> more powerful beams
PIP-II is planned for 2027
  0.7 MW -> 1.2 MW
Two proposals for after PIP-II (PIP-III) to increase power to 2.4 MW
  2 GeV RCS (Rapid Cycling Synchrotron)
  8 GeV SRF Linac
These new high intensity beams are demanding of foil injection, which is the focus of my summer project
Image from J. Eldred

## Slide 3: Foil Stripping Injection
How do we inject p+ from a Linac into a circulating beam
  Magnets around injection bend injected H- (primary) and circulating p+ (secondary) together
  Foil strips two e- from the H-, leaving two p+ circulating in beam
Problems
  Foil heating from foil interactions
  Power loss from large-angle scattering (especially at higher energies)
  Both problems scale with number of foil hits. Minimized by decreasing foil hits.
  Secondary hits scale quadratically with injection time
Image from J. Eldred
Notes: Talk about minimizing secondary hits

## Slide 4: Beam Painting Schemes
Correlated Painting
Anti Correlated Painting
Used in PIP-II
Images from D. Raparia
Painting decreases secondary hits by moving foil out of already circulating protons

## Slide 5: Foil Size
Foil Size – A smaller foil decreases the interaction probability by presenting a smaller target.
In order to capture 99% of the beam, the foil must have Area = L x W = [ cm^2 ]
Linac sigma i . It is dependent on the Twiss Beta Parameter
Some Injection mismatch was shown to decrease secondary hits without drastically increasing emittance
Notes: Painting on next slide

## Slide 6: Injection Mismatch
For PIP-III injection, matched injection would be a ξ of ~.42
Emittance growth minimal until beam is severely mismatched
Significant reduction in total foil interactions by reducing ξ
Pick a ξ of .2 to run PIP-III simulations

## Slide 7: Beam Dynamics
Beam propagates through transverse phase space according to the transfer matrix
Transfer matrix creates a “one turn map”, describing the transverse position of the beam at the injection point after one revolution
Only fractional tune matters in this simulation, and chosen to avoid resonance
Wille

## Slide 8: Benchmarking PIP-II Simulations
Python simulation matched Valeri Lebedev’s MathCad for PIP-II CDR
Included
  Dispersion
  Multiple Scattering
  Longitudinal Painting
My Simulation (Top) gives results similar to PIP-II CDR (Bottom)
  Top Hot Spot
  Bottom Hot Spot
Used this simulation as a jumping off point for the 2 GeV RCS and 8 GeV Linac Scenarios, with a few key differences
  Both the Linac and RCS are injected into dispersion free regions, which simplifies the simulation to 4D
  PIP-II Injection takes places over ~300 turns while the Linac and RCS scenarios are considering injecting over 1000 turns
Image from V. Lebedev

## Slide 9: PIP-II Longitudinal Injection Scheme Foil Hits
Off momentum (CDR)
  Booster Window: 0 < |f| < 0.55p
  Momentum offset: 7e-4
On Momentum (Paul Derwent)
  Booster Window: 0.15p < |f| < 0.7p
  No momentum offset
Results
  ~ 50% increase to total foil hits
  ~ 7% increase to peak hit density
Paul Derwent
Booster Separatrix injection for CDR (left), Paul (Right)

## Slide 10: Multi MW Upgrade Scenarios
Long Injections have painting split into five parts
PIP-III scenarios inject at higher intensity which requires longer injection
PIP-III injects into a larger emittance than PIP-II
Injection mismatch causes a minimal emittance increase
Image from J. Eldred

## Slide 11: Simulation Results
Conclusions
The MI Linac and RCS-AR scenario prefers correlated painting, as the alternative increases secondary hits by > 75%.
The 5mA RCS also prefers correlated painting, but to a lesser degree which offers more options.
For the 5 mA RCS scenario, the peak hit density per particle could be optimized close to PIP-II injection

## Slide 12: MI-Linac Painting Comparison
Notes: Mention Cut Corner Scenario

## Slide 13: Summary
Created a simulation in Python, benchmarked by PIP-II CDR
Investigated an on-momentum injection scheme for PIP-II
Ran both correlated and anticorrelated simulations for several PIP-III scenarios
Results of those simulations indicate that correlated painting becomes preferable as the time of injection rises. (more turns per injection)
Further investigations should include space charge, transverse coupling, dispersion from chicane magnets
Acknowledgments
I would like to especially thank my supervisors Jeffrey Eldred and David Neuffer as well as my group mentors Michael Geelhoed, Ahmed Syed, and Linden Carmichael for their support, guidance, and encouragement throughout my summer internship.
I would also like to thank Fermilab and the SIST Committee for allowing me to participate in research this summer.

## Slide 14: Accessory Slides

## Slide 15: Beam Painting Bump Functions
Correlated Painting
represents starting painting off center
Anti Correlated Painting
Images from D. Raparia

## Slide 16: Injection Mismatch
Mismatch refers to the ratio of
Method 1 is typical
  Linac is geometrically matched to the ring
  Allows room for emittance growth through multiple scattering in the foil
  More foil interactions, due to greater Linac spread
Method 2 presents a more aggressive painting scheme
  Linac is mismatched to to beam
  Greater emittance from particles injected outside of ring acceptance, less room for emittance growth
  Foil can be smaller due to compressed beam at injection, less foil interactions
Optimal Mismatch is somewhere between methods 1 and 2 and different for anticorrelated and correlated painting
Method 1
Method 2

## Slide 17: Injection Mismatch
95% emittance tolerable for the degree of mismatch proposed
Slightly Different Minima for Anticorrelated vs Correlated Painting
  Anticorrelated minimized at
  Correlated minimized at
This simulation indicates that future foil injection could benefit from some injection mismatch
  Realistic painting scheme will likely be more conservative, this simply demonstrates how injection mismatch can reduce foil hits
  Injecting at would represent at 40 – 50 % reduction in foil interaction depending on the painting scheme.
Note on Multiple Scattering
  RMS scattering angle scales as 1/p therefore small angle scattering is less of a concern at 2 and 8 GeV than at 800 MeV
  Power loss from large scattering is a concern at higher energies, minimizing foil interactions can help mitigate this effect
Scenario 2
Scenario 1

## Slide 18: 2 mA RCS Painting Comparison
Peak hits spot is ~15% less hot for Anticorrelated Painting
Total hits is ~70% greater for Anticorrelated Painting
14.69 hits/p+
8.65 hits/p+

## Slide 19: 5 mA RCS Painting Comparison