## Slide 1: “I can probably CAD that” or “It goes in the square hole”
Aaron Schwan

## Slide 2: Cage
It’s a box!

## Slide 3: Cage

## Slide 4: Cage Continued

## Slide 5: Why?
Integrate into the model of the shaft and headframe
Easy first check for materials to verify it can fit
Planning for material loads

## Slide 6: Loads
1) Not very awkward loads
2) Very awkward loads

## Slide 7: L-Beams
Too Large to fit in cage
Must be rotated to fit through headframe then rotated to fit into cage
Mostly 5.5 meters (18ft) and 3.6 meters (12ft)
Weighs 5458 kg (12,033 lb)
Notes: 1 pickup truck in length
2 pickup trucks in weight

## Slide 8: Paths
Path 1: Green
Through Southwest Door
Around Cage
Rotate on 10T
Path 2: Orange
Through Southwest Door
Through Cage
Rotate on 10T
Path 4: Purple
Through Southeast Door
Rotate while entering
More technical Lift
Will be in the correct orientation
Path 3: Blue
Through Northeast Door
Through Cage
Rotate on 10T
Path 1: Green
Path 2: Orange
Path 3: Blue
Path 4: Purple
North

## Slide 9: Path 1

## Slide 10: Rotation Idea
One chain hoist at a time is moved
Alternating process
  Shorten long side
  Lengthen short side
Maintained below critical angles of hoists

## Slide 11: I-Beams
Short
Below 7.5 Ton
Shorter than 8m
Long
Above 7.5 Ton
Longer than 8m
Notes: 2.5 pickup trucks in length
Almost 3 pickup trucks in weight

## Slide 12: Path into Headframe For Long I-Beam
Minimum angle of 13-degrees entry
Floor conditions
Shelfing outside headframe
Custom rigging

## Slide 13: Path into Headframe For Long I-Beam

## Slide 14: Guide Shoe Cart Combination
That could maybe work if physics doesn’t step in

## Slide 15: Guide Shoe Cart Combination
Guide Mode
Cart Mode

## Slide 16: Guide Shoe Cart Animation

## Slide 17: Guide Shoe Cart Overview
Retracting guides like how a door locks
Two sets of wheels
Lifting lug able to control insertion and extraction
Pulley system that retracts the opposite guides
Primarily designed around commercially available parts

## Slide 18: Guide Shoe Cart Retracting Guides
Linear rail reduces forces required
Anti-scratch guides
Spring loaded position in locked state

## Slide 19: Guide Shoe Cart Next Steps
Define parameters of operation
Evaluate practicality given the current facility
Submit requests for information to designing firms
Build the cart

## Slide 20: Bridge Crane RFI
Does it fit?

## Slide 23: What was done
Defined minimum hoist height
Defined travel and span
Identified possible issues with integration (brattice, doors, NE support, etc. )

## Slide 24: The Future
Who knows. It’s the future

## Slide 25: My Takeaways
Technical Skills
Large CAD projects
Finite Element Analysis and Engineering Analysis
Logistics and item transport
Soft Skills
Working as a small part of a large project
Think about the whole process not just the “best design”
Communication in a team

## Slide 26: Thanks for listening! Questions?

## Slide 27: Appendix

## Slide 28: Other things I have done
Transport summary doc
Non-awkward lifts & Packing
Cage summary doc
Chimney rotations
Started floor discussion for headframe
4850L Bridge Crane RFI
4850L Winch Integration Ideas/Starting
Other Awkward Materials
  Warm Skin Flat and Corner (Not completed)
  APAs (Not Completed)

## Slide 29: The square hole
https://www.youtube.com/watch?v=jkz7bnYfuOI

## Slide 30: Bridge Crane RFI

## Slide 35: Brow Winch Integration

## Slide 37: Anchors
Rock anchors
  Centered in cage compartment and north skip
Winch mounted on ceiling
Snatch block transferred from anchor to anchor

## Slide 38: Chimney Rotation

## Slide 40: Ground Conditions
Cautionary Tale
Current
Possible Solutions

## Slide 41: Ground Conditions a Cautionary Tale

## Slide 42: Rails
½ cm above the water
½ cm below the water
Rails are not perfectly flat
There will be slight tilts that must be evaluated if used
  L-beam vertical position maximum of a 5-degree tilt horizontal is a 11-degree tilt

## Slide 43: Current Ground Conditions Images
In-between the rails still a problem
Steel Plates in front of cage
Mini-headframe
Foundation
Standard Flooring in Headframe

## Slide 44: Entrances
Rails have a bump while being brought in
Northeast door has a concrete slab
Rail or cart has a bump to account for

## Slide 45
Crosses rails mostly flat initially
After rails there is a slight grade to the floor approximately 5cm over 20cm
Mostly broken concrete the closer you get to the mini-headframe