## Slide 1
High-intensity low energy muon beamline at MTA
Performance Simulations
Carol Johnstone, Anna Mazzacane, Rob Ridgway, Chris Izzo, J. Morgan
C. Johnstone
Review 8-23-2021

## Slide 2: Fermilab LDRD 2021: Multi-slice Target Development
Develop an economical approach to producing an intense mutli-application low energy muon source, both  - and  +
    Emphasis on an intense, multi-application  - beam
Provide essential R&D for muon beam planning for PIP-II era
Develop a heavy target for lower-energy proton beams (<1 GeV)
    Optimize interaction length, beamline orientation and capture 
    Optimize target geometry and orientation
    Optimize # of target slices and spacing
Test concepts at Fermilab MTA facility at the end of the 400 MeV linac
    Install a precision low-energy muon beamline in the MTA with in-house components during summer 2021 accelerator shutdown
    Study performance compared to simulations
    Support ARPA-E funded muon catalyzed fusion experiment to further quantify performance and successful application

## Slide 3: Final Beamline Geometry & Integration with Experiment
Rollup Door
33.5
ITA Cave
Front Porch
234” / 5.9436 m (z)
154.9”
3.934 m (x)
280.614” 7.1276 m
EXP
85.1”
2.2 m (x)
z
x
TUNGSTEN TARGET
Target is 3’ upstream of MW8 connecting flange
Straight shot to corner is 146.5
Experiment ~2m insertion length
Remaining length for beamline
  ~5m
  Insufficient for a full FODO cell
  Even with more quads and ramped currents
No dispersion - bonus
Large transverse acceptance
  On and off momentum
EXP – side view

## Slide 4: Matching Solenoid to Production Target size
Two beam envelope solutions because the linear dynamics solution is quadratic in target beam size – beam diverges from the target:
  sol (thin lens) tgt+ s2tgt (where  is  beam size2)
  For sol =5m and distance to center of solenoid = 0.4102m
    tgt = 0.03 m – solenoid captures a small, high divergent beam spot
    tgt = 4.85 m – solenoid captures a parallel beam
Using the acceptance of the beamline (180 mm-mr) gives target size
  ltgt@low   2.3 mm; ltgt@high    30 mm
Two optical solutions
Two target solutions
Primary beam
For low , IL = 2.3% for W
0.5 cm target length
For higher , IL = 60% for W
6 cm target length
Spot size
x
x’
Spot size
x
x’

## Slide 5: Summary of Design Approach
The experimental line captures ultra-low energy secondaries at a 146.5 backward angle relative to primary beam
At low energies, the geometric emittance is large; don’t have the advantage of long distances at MTA; optics must be highly efficient and compatible
  The experiment has requested 10-50 MeV muons; dp/p ~ 
    Energy has been finalized at 100 MeV/c (~30 MeV muons) based on simulations/components; dp/p > 2
    Experiment has adapted to this energy and momentum spread
For large acceptance (small betas) and a large dp/p
  Beamline optics are built on a short 90 FODO cell
  Focal length must be ~4 m to fit (half cell length ~3m); for magnetic length ~0.247  k ~1.0 m-2
    At 100 MeV/c, 8.9 gauss/cm; k ~0.25 m-2
    Requires 4 quads – to achieve this focal length
  For thick lens and 4 quads, k~0.5 m-2– this translates into ~2A @100 MeV/c
Solenoid is used to capture pions with equal phase space distributions in both planes
  Focus to the the “crossing” beta function of the FODO cell
  3 Quads match to FODO – similar k value

## Slide 6: Momentum Dependence of Design and Tracking to end of line
On Momentum
dp/p = -20%
dp/p = +20%
x,y tracking @experiment
200 mm mr
x,y losses @experiment
200 mm mr
Horz Phase space @experiment
200 mm mr

## Slide 7
100,000 π tracked/run.
Emittances are 100%, geometric.
are 100% momentum spreads.
Phase-space & distributions are uniformly populated.
The large horizontally defocusing kick provided by the Q01-series quadrupoles causes losses to build up almost entirely on the Q02A/B/C magnets’ 4” apertures.
Performance of Beamline

## Slide 8: Steering in the beamline
A horz inner dipole followed by a vertical inner dipole will be added to the first two quadrupoles in the beamline just after the solenoid
Another horz and vert inner dipole will be added to the last two quadrupoles in the beamline to steer into the experiment’s target area
The trim dipoles are able to provide 10mr of steering @4A.
Upstream moves the beam ~1” at experimental apparatus.
Angle is adjusted with downstream trim dipoles
Position and angle for 10 mr steering down the beamline

## Slide 9: The Target: Initial slice concept and rotation to backward production
Target slices reduce the mean free path – initial concept was a 90 facing secondary line
  This had to be rotated backward and concept adapted as dipoles could not be implemented
Filling the Loma Linda solenoid 2.5” (6 cm) aperture with target slices shown on left
  Rotating slices turns it into a longer solid target
8 cm is the longest target that can be accepted by the secondary beamline
Primary beam
45
(Actual 33.5)
6 cm
8.5 cm
6 cm
Primary beam
8 cm rod; 80% IL

## Slide 10: Sliced Target concept and opposite rotation
A sliced target can be used to increase surface to volume
Opposite orientation rotates into a series of slices normal to the primary beam direction
Pions produced from the opposing side of the target travel through significantly less volume
Net target length is reduced by ~half from the solid target approach
Primary beam
45
(Actual 33.5)
6 cm
8.5 cm
6 cm
four 1 cm slices; 40% IL

## Slide 11: Preliminary Un-normalized Pion Production 8-cm long solid W target

## Slide 12: Un-normalized Pions, 8 cm W target, entering solenoid aperture

## Slide 13: Check of Energy loss and Multiple Scattering in W
For ~30 MeV/cm, 4 cm to reduce 400 to 280 MeV pion production threshold. This is an energy limitation of the Fermilab Linac and a tungsten target – lighter targets such as graphite can be longer. PIPII @800 MeV will be able to use much longer tungsten production targets.
At 3 x rms beam scatters ~half a cm by the end of the 3 cm target. A 1.5 cm wide target is a reasonable choice to minimize pion reabsorption.
W Radiation length; 6.76 g cm-2 0.3504 cm

## Slide 14: Target Geometry and Position Considerations
Nuclear interaction models show the expected 10 cm IL behavior
  INCL++ and UrQMD standalone
Pions are not produced beyond 4cm (due to energy loss)
Optimal target length is currently estimated to be 3 cm
  3 cm horz x 1.5 cm wide (measured) x 3 cm vertically
    equal horz and vert spot sizes generated by target
    Horz width will be reduced in Figure and vert increased
  Production models are giving significantly different rates (x10)
  Significant differences in momentum distributions
Exponential nature of cross sections for an extended target
  Nonuniform filling of phase space
  Mean of distribution positioned on centerline of beamline
Horz 99% width will be reduced to 1 cm and vert increased to 3cm
Double minimum in horz and vert

## Slide 15: Nuclear Interactions - review
Nuclear interactions follow an exponential curve with target length
Nprimary=N0e-l where l is the length of the target and  is cross-section times #particles/cm3
  Cross sections are an effective area measured in barns – 10-24 cm2
  Anna has presented and compared cross sections of different models
Nuclear interaction length is the mean distance traveled by a proton beam in a target before an inelastic nuclear interaction occurs,
 =[ (density in g/cm3) x  (measured, cm2) x 6.022 x 1023 (Avogadros #)]/mole
Np
l
Np-Np x
Np-Npx - (Np-Npx) x
….
Cross section is area of dots – nuclei interaction region
Cross sections are measured experimentally and there are accurate models

## Slide 16: Target alignment
Mean of the distribution from the exponential interaction occurs about 1.3 cm into the target (4 – 2.7 cm).
For a 3 cm target this is only 2 mm from the center
  The production is sufficiently flat as a function of angle that a 2mm offset is likely insignificant

## Slide 17: Optimized Solid Target concept: 3 cm path and not rotated
Centered @ mean of distribution produces most dense central phase space
  Important for the small aperture muon catalyzed fusion experiment
  Slices will be more important for distributed or even lower energy muon beams
Centering to be determined from target modeling
Primary beam
33.5
3.0 cm
6 cm
1.5 cm target:
beam size ~1 cm
1.5 cm
Pion beam
1.3 cm
1.7 cm

## Slide 18: Optimized Solid Target concept: 3 cm path, rotated?
Does rotation reduce mean free path? NO
Rotation reduces density of particles – spreads out beam
  More backward the secondary angle, the smaller the secondary beam size
Long narrow target – no rotation is optimal
Primary beam
1.2 cm
Muon beam rays
1.5 cm
0.5 cm
3 cm
1.8 cm
1 cm
33.5
1.4 cm
2.5 cm
1.5 cm
3.0 cm
0.5 cm
1.4 cm
2.3 cm
1 cm
1 cm

## Slide 19: Beam Absorber
Modeled after MuCool operation
  20 cm steel beam absorber after RF cavity (in air)
  RF cavity: additional 2” of steel
Reuse two tungsten bricks
  Used for beam tests
  Removable (manual motion table)
  In a vacuum break between target housing and MW8
    As close as possible to target housing downstream port
  Additional shielding will be installed
    Target and beam absorber
Schematic of HPRF cavity Beam Test at MTA units in mm
Residual activation of Cu insert in beam
absorber. (Two 50-μs pulses provide 4.3 × 1011 p/sec.) Will be repeated for W absorber.

## Slide 20
Highest center phase space density is created by a solid rod target
Increase in pion production per proton vs PSI:
  30% vs 4% interaction length
  Factor of 8 in - production cross section, tungsten vs graphite
    Factor of 2 rather than 5 less vs + production (this is seen in studies)
  Factor of 10(?) increase in momentum acceptance
  Maybe a total factor of 600 increase in # -/- per proton
    Does not take into account pion production cross section is higher at 600 MeV
    PSI is CW MTA hall operational ASE and Linac duty cycle
Two 1.5-cm targets separated by 1 cm will also be studied
Expectations - Summary

## Slide 21: Operational Parameters of 400-MeV Fermilab Linac beam and MTA/ITA limits
ITA operation (local “cave” shielding)
Parameter | Value | Unit
Kinetic Energy | 401.5 | MeV
Repetition Rate | 20 Hz | 
Energy Spread | 1 | MeV
RF Structure | 201.24 | MHz
Bunch Length | 0.05 | ns
Max Pulse Length | 80 | µs
Max Particles Per Bunch (28 mA) | 0.88x109 | 
Max Particles Per Pulse | 1.4x1013 | 
Peak Current | 28 | mA
Avg Current | 34 | µA
Max Beam Power | 13.4 | kW
Beam Emittance (99%) | 8 | mm-mrad
Full Linac Beam Capability
Local shielding will be implemented for muon production target and a local beam absorber
Note: 6.56x1012 p/40 sec or 1.64x1011 p/sec

## Slide 22: Readiness Summary
Optics Design Complete
Major target studies complete
  Shielding assessment started
  Final performance and rate studies initiating
Layout complete
All beamline components tested and ready for installation
Alignment stake-out of stands and final beamsheet ~end of week
Target and housing modeled and target thermal analysis complete
Vacuum and stands engineered including experimental stand
  Drafting and engineering note in progress
  Materials list ready for order
Power supplies identified
Cabling and cable runs complete
  Electrician req was submitted a couple of months ago
Diagnostics – R&D
  Experiment has sophisticated muon and other radiation detectors

## Slide 23
BACKUP Slides

## Slide 24
Quantity | Value | Units | Value | Units
Atomic number | 74 |  |  | 
Atomic mass | 183.84(1) | g mole-1 |  | 
Specific gravity | 19.30 | g cm-3 |  | 
Mean excitation energy | 727.0 | eV |  | 
Minimum ionization | 1.145 | MeV g-1cm2 | 22.10 | MeV cm-1
Nuclear collision length | 110.4 | g cm-2 | 5.719 | cm
Nuclear interaction length | 191.9 | g cm-2 | 9.946 | cm
Pion collision length | 133.9 | g cm-2 | 6.936 | cm
Pion interaction length | 218.7 | g cm-2 | 11.33 | cm
Radiation length | 6.76 | g cm-2 | 0.3504 | cm
Critical energy | 7.97 | MeV (for e-) | 7.68 | MeV (for e+)
Molière radius | 18.00 | g cm-2 | 0.9327 | cm
Plasma energy ℏωp | 80.32 | eV |  | 
Muon critical energy | 150. | GeV |  | 
Melting point | 3695. | K | 3422. | C
Boiling point @ 1 atm | 5828. | K | 5555. | C
Atomic and nuclear properties of tungsten (W)
NOTES
The nuclear interaction length is 10 cm. An inelastic nuclear interaction is required to make pions
1 cm was initially chosen (10% IL) to be consistent with the shielding assessment for a target in the MTA experimental hall
>10% IL requires a local beam stop - Beam cannot be transported to the high intensity beam dump buried in the berm downstream of the hall
https://pdg.lbl.gov/2021/reviews/constants_atomic_and_related.html

## Slide 25: Compare with Carbon
PROJECTED PERFORMANCE
PSI – 1.5 cm 4%IL C target
Factors
30% vs 4%
4 x nuclear interactions
Factor of 3 and 8 from
+   
–   
Total increase from a carbon target = 60 for –
Momentum spread increase?
Rate correction for PSI CW beam (1 –/10 sec) vs 20 Hz duty cycle of Linac and macropulse length
Quantity | Value | Units | Value | Units
Atomic number | 6 |  |  | 
Atomic mass | 12.0107(8) | g mole-1 |  | 
Specific gravity | 2.210 | g cm-3 |  | 
Mean excitation energy | 78.0 | eV |  | 
Minimum ionization | 1.742 | MeV g-1cm2 | 3.850 | MeV cm-1
Nuclear collision length | 59.2 | g cm-2 | 26.79 | cm
Nuclear interaction length | 85.8 | g cm-2 | 38.83 | cm
Pion collision length | 86.5 | g cm-2 | 39.12 | cm
Pion interaction length | 117.8 | g cm-2 | 53.30 | cm
Radiation length | 42.70 | g cm-2 | 19.32 | cm
Critical energy | 81.74 | MeV (for e-) | 79.51 | MeV (for e+)
Molière radius | 11.08 | g cm-2 | 5.012 | cm
Plasma energy ℏωp | 30.28 | eV |  | 
Sublimination temperature (@ 1 atm) | 4098. | K | 3825. | C