## Slide 1
Rob Ainsworth
2021 IOTA/FAST Collaboration Meeting
October 28th 2021
Studies of Proton Beam Instabilities with a Wake-Building Feedback System

## Slide 2: Outline
Motivation
Wake building feedback system - Waker
Instability studies in the Fermilab Recycler
Future plans and moving to IOTA

## Slide 3: TMCI (Transverse Mode Coupling Instability)
Bunches oscillate with different transverse modes
Impedance in a machine can cause a detuning of these modes which scales with intensity
If the detuning is large enough, the frequencies of two modes couple -> TMCI
Wake parameter

## Slide 4: Space charge
Inside a bunch, there is a spread of tunes
Self field results in defocusing which leads to tune shift
Space charge leads to tune shift
  increases this spread with intensity
  Worse at low energy
  Depends on bunch length and beam size
Space charge
tune shift

## Slide 5: Space charge and TMCI
For many years, space charge was thought to have a stabilizing effect on TMCI
Space charge parameter
Wake parameter
Coherent tune shift from
wake/Qs
Incoherent tune shift from
Space charge/Qs

## Slide 6: Space charge and TMCI
In 2018, Alexey Burov predicted a new kind of instability, convective instabilities
  Occur in place of TMCI at strong space charge
  Results in huge amplification from head to tail
  Traditional dampers may make things worse
Space charge parameter
Wake parameter
IOTA (protons)

## Slide 7: Usually, the wake amplitudes which drive instabilities are machine dependent and are determined by the impedance of the components installed within the machine. A novel approach to control instabilities will be to install a `waker' system, a dedicated wake-building feedback system.

## Slide 8: Waker concept
The waker will mimic kicks from wake using a kicker
The system will measure the position and intensity along the bunch and apply multiple kicks along a single bunch
Bandwidth of the system should be much larger than the inverse bunch length
Waker allows vertical
movement on this plane

## Slide 9: IOTA is ideal to deploy the waker However, it’s 1-2yrs away from protons Can we take advantage of FNAL accelerator complex in the mean time?

## Slide 10: FNAL accelerator complex
H- linac
Booster
  h = 84
  15 Hz
  400 MeV -> 8 GeV
Recycler
  h = 588
  Slip-stack 12 batches (double bunch intensity)
Main Injector
  8 GeV -> 120 GeV

## Slide 11: Using the Recycler to study instabilities
Recycler is attractive for studying instabilities
  It doesn’t ramp i.e. energy is fixed to 8GeV
  It can already operate at strong space charge
  Study time availability
NuMI - MI
SY - MI
SY - RR
NuMI - RR
Muon - RR
Study cycle - RR

## Slide 12: Bandwidth requirements
The waker system needs to excite intra-bunch motion
  Needs large bandwidth compared to inverse bunch length
For standard operation this is tricky
  bunched at 53 MHz
  need a bandwidth on the order of GHz
  difficult to build!
Fortunately, RR has ability to create longer bunches
  Re-bunched to 2.5 MHz
  Need a bandwidth of at least 100 MHz - this is doable
Example of RR rebunch used for muon

## Slide 13: Waker system
0.5m stripline kicker
2.5 kW
Amplifiers
Reuse off-axis
Bpms

## Slide 14: Timing in the system
All cables were verified before timing in the system
Correct delay and bpm coefficients were found by performing open loop transfer function measurements.
To verify the system worked as expected, both damping and antidamping was demonstrated for 53 MHz and 2.5 MHz beam

## Slide 15: Time to try a wake
Start with Heaviside step function wake (theta wake)
  W0=0 ahead of bunch, W0=1 behind
  Kick is integral of dipole motion from timeslices infront
Started off at 5 booster turns, couldn’t see much
Increased to 10 booster turns, gain=5
Waker turned on at 1s for 50,000 turns
Beam fallout

## Slide 16: First instability observed
Observed on Stripline pickups
  Much smaller than bunch length
  Signal is current differential
Diff signal
  Proportional to
    postion x intensity
Sum signal
  Intensity

## Slide 17: Time for some studies
Tune shift vs intensity with waker off
  i.e. natural tune shift
Measurements less trustworthy at high intensity
  Ping too strong

## Slide 18: Tune vs gain
Tune vs gain
  +ve gain -> -ve tune shift
  -ve gain -> +ve tune shift
I’m a little skeptical of this measurements
  Tune varies depending on turn window used

## Slide 19: Parameters
Parameter | Value
Qs | 0.0005
Chromaticity (x,y) | 0.03,-0.15
Dp/p | 0.0005
Intensity | 1e11 - 5.5e11 ppb
Bunch length | 30 - 40 ns
Normalized emittance, 95% | 15 pi mm mrad
Beta | 0.9944
Machine radius | 528 m

## Slide 20: 4 booster turns, gain=2, just above threshold
Max
Difference
Signal
1.1e11 ppb
Qsc=-0.0028
Qs~0.0005
q=Qsc/Qs ~ 5.6

## Slide 21: 8 booster turns - gain=0.62, just above threshold
2.2e11 ppb
Qsc=-0.0056
Qs~0.0005
q=Qsc/Qs ~ 11
Max
Difference
Signal

## Slide 22: 16 booster turns - gain=0.325, just above threshold
5.1e11 ppb
Qsc=-0.013
Qs~0.0005
q=Qsc/Qs ~ 26
Max
Difference
Signal

## Slide 23: Coupling to +1 vs -1mode
Threshold at -ve gain appears a much higher gain
Without space charge
  Gain should be equivalent going +ve or -ve
With space charge
  Should need more gain when shifting tune down
However, machine impedance means waker needs more gain to shift +ve
Gain=-9
Gain=0.3
Qsc=-0.013
Qs~0.0005
q=Qsc/Qs ~ 26

## Slide 24: Modifications for next run
Need a better way to measure the tune
  Will add closed loop transfer function option to board
  Need an extra ADC for this
  Will doing A-B before board to free up 2 ADCs
200 MHz board in development (500 MHz but only need 200MHz)
  Moving from softcore to hardcore on FPGA
  Most likely ready by the end of the year
New postdoc (joined September) will be working on this as well

## Slide 25: Moving to IOTA
Most significant costs of the system are:
  RF amplifiers
  Board development
  Both are easily moved from Recycler setup
Will need pickups (x2) + kicker to complete system
IOTA RF frequency is similar to Recycler (around 2-2.5MHz)
Reduced revolution time could make things a bit tricky
  Recycler revolution time ~ 11 us
  IOTA revolution time ~ 1.8 us

## Slide 26: IOTA study plan
Recycler has some limitations
  Large natural tune shift due to impedance, magnets etc.
  Knob to control space charge is mostly based on intensity
IOTA studies
Study instability conditions at strong space charge
Compare with theory
  Easier in IOTA due to low velocity I.e. minimal impedance
Couple studies with other experiments
  e.g. electron cooling -> more control of phase space -> control of space charge

## Slide 27: Summary
Wake building feedback system has been commissioned in Recycler and will eventually be moved to IOTA when protons are ready
Will allow study of instability conditions in varying space charge and wake amplitude
Collaboration is welcome in both RR and IOTA for these studies

## Slide 28: Backup

## Slide 29: Key Parameters

## Slide 30: Timing in the system
Combining the bpm signals with the C1,C2 coefficients
  Can simulate a signal with optimal phase advance to the kicker
    i.e. 90deg
Set delay such that kicker kicks the beam
Can be found by performing open loop beam transfer function

## Slide 31: Open Loop Beam Transfer Function measurement setup
Break loop between board and amplifiers
VSA sends noise source in frequency bandwidth to the amplifier
Board sends combined bpm signal to the VSA

## Slide 32: Betatron sidebands
n*f_rev
(n+q)*f_rev
Tune = Q + q
Integer
Fractional
(n-q)*f_rev
Lower sideband
Upper sideband
Example measurement

## Slide 33: System delay
Sum of upper and lower sideband phase vs combined frequency of sidebands

## Slide 34: Coefficients of bpm
Once t_dly~0,
Phase difference between 2 sidebands is twice the phase advance from pickup to kicker
Ideal phase advance is 90deg, so sideband difference should be 180
However, phase response from notch results in 180 flip around revolution harmonic
Therefore, both sidebands should have the same phase
Not quite sure where the 10-15 deg offset comes from

## Slide 35: System timed in, try to damp/antidamp as test
First try on 53Mhz beam
Then try anti damp 2.5MHz beam
  Not sure why most motion is middle 2 bunches
Damp
Antidamp

## Slide 36: Stripline pickup analysis
Raw
Corrected
Zoom

## Slide 37: Baseline correction (CERN headtail monitor)