## Slide 1: ODU-SLAC Compact Crab Cavity RF Study
Zenghai Li, Lixin Ge (SLAC)
Jean Roger Delayen, Subashini D. Silva (ODU)
LARP CM18, Fermilab May 7-9, 2012

## Slide 2: Outline
The Parallel Bar/Ridged Design
Deflecting mode RF parameters
HOM damping coupler – preliminary
Cavity MP analysis

## Slide 3: Cavity Parameters
Geometry fits both H and V crabbing schemes
Parameters | Model-1 | Model-2
Operating mode Frequency | 400 MHz | 400 MHz
Operating Mode | TE11 like mode | TE11 like mode
Lowest acc mode Frequency | 731 MHz | 714 MHz
Lowest vertical HOM Frequency | 784 MHz | 757 MHz
Lowest horizontal HOM Frequency | 594 MHz | 612 MHz
Iris aperture (diameter) | 84 mm | 84 mm
Transverse dimension | 295 mm | 281 mm
Vertical dimension | 295 mm | 288 mm
Longitudinal dimension | 620 mm | 638
Transverse Shunt Impedance | 323 ohm/cavity | 339 ohm/cavity
Required deflecting voltage per cavity | 5 MV | 5 MV
Peak surface magnetic field | 84 mT | 89 mT
Peak surface electric field | 54 MV/m | 46 MV/m

## Slide 4: Deflecting Voltage Uniformity
Perform multipole analysis of the deflecting Voltage
E and B
at center cross section

## Slide 5: Deflecting Voltage Uniformity
Model 1
Model 2
Pole profile can be shaped to improve
Need specification of requirements

## Slide 6: Impedance (R/Q)

## Slide 7: Impedance
Transverse impedance referred in this file is RT

## Slide 8: Impedance budget: frequency dependence
0.7 eVs in 200 MHz @ 450 GeV, Nnom
2.5 eVs in 400 MHz @ 7 TeV, Nnom,
16MV and 8 MV
E. Shaposhnikova
200kohm

## Slide 9: Transverse impedance budget
For nominal intensity at 450 GeV threshold determined by the damping time of 60 ms is 2.5 MOhm/m. With margin for particle distribution - 0.6 MOhm/m
Approximate frequency dependence
  0.6 /(1-fr/1.6) MOhm/m for fr [GHz] < 0.8
  1.2 (0.5+fr) MOhm/m for fr [GHz] > 0.8
  → 0.8 MOhm/m at 0.8 GHz for ultimate intensity and
  0.4 MOhm/m for 2 identical cavities
Additional factor proportional to local beta-function β/‹ β ›
E. Shaposhnikova

## Slide 10: HOM Damping
Waveguide to damp H/V dipole and accelerating HOMs
No filter needed
One WG in each plane is enough for damping. WG stub maybe needed to symmetrize field
OR
Coaxial high-pass filter coupler
Next HOM ~200MHz higher than operating mode. A two-stage high-pass filter maybe adequate
Compact

## Slide 11: HOM Damping
Waveguide to damping
Coaxial high-pass filter coupler

## Slide 12: Qext with Waveguide Coupler
Strong damping achieved with waveguide couplers

## Slide 13: High-Pass HOM Damper
Two-stage high-pass coupler

## Slide 14: HOM Damping With High-pass Filter

## Slide 15: Impedance - (R/Q)*Qext
Solid lines: LHC-CC10 requirement

## Slide 16: Dip_H Impedance - (R/Q)*Qext
Solid lines: LHC-CC10 requirement
0.594
0.877
1.211
1.398

## Slide 17: dip_V Impedance - (R/Q)*Qext
Solid lines: LHC-CC10 requirement
0.784
1.050
1.419
0.890

## Slide 18: acc Impedance - (R/Q)*Qext
Solid lines: LHC-CC10 requirement
0.761
0.872
1.705

## Slide 19: Waveguide vs Coaxial Coupler
Preliminary designs
A few modes in the coaxial coupler design above the LHC-CC2010 requirement
Optimization in progress

## Slide 20: MP Simulation Using Track3P
Launch electrons on exterior surfaces with different RF phase and initial energy
Determine “resonant” trajectories by consecutive impact phase and position
Stable resonant MP: trajectories impact at same locations with same energies - Calculate MP order (#RF cycles/impact) and MP type (#impacts /MP cycle)
Run-away resonant MP: trajectories started resonant with RF and slowly slip away from resonance location and RF phase. Maximum enhancement counter calculated based on given SEY curve

## Slide 21: Multipacting Simulation Using Track3P
Field level scan:
  0.050 MV – 6.0MV, interval 0.025 MV
Initial Particles distributed on all exterior surface (using quarter symmetry)
Each field level ran 50 RF cycles.
Determine resonant trajectories – impact energy and type

## Slide 22: MP Resonant Particles

## Slide 23: MP Resonant Particles
MP band at deflecting voltage 0.5-2.6MV
  in cavity rounding corners & on end-plate
  with various MP orders
MP at 3-6MV deflecting voltage
  in end-plate rounding corner
  first order with low impact energies
No significant MP found in coupler

## Slide 24: Summary
ODU/SLAC compact cavity design is being optimized
Preliminary coaxial high-pass filter coupler and waveguide coupler being developed. Effective damping achievable with both schemes
Further coupler improvements
  Coupler geometry
  Pass-band RF parameters
  Analyze multipacting due to beam excited modes (e.g. acc mode)
Multipacting being analyzed for the deflecting mode
  MP band from 0.5-2.6MV – impact energy in range of high SEY
  Resonant trajectories from 3-6MV - low impact energy (low SEY)
  No significant MP found in coupler
  Cavity shape around the MP region could be improved to minimize MP resonances