## Slide 1: Fluka Modeling of the Interaction Region
H. Matis, S. Hedges, M. Placidi, A. Ratti, W. Turner
[+several students] (LBNL)
R. Miyamoto (now at ESSS)

## Slide 2: Overview of Simulations
Using FLUKA with IR1 and IR5 geometry implemented by CERN
We have added a detailed model of the TAN including forward detectors and BRAN

## Slide 3
IP model developed at
CERN
FLUKA model of ATLAS IP1
TAN Model developed by LBL
2011 Version
ATLAS
ZDC
BRAN

## Slide 4: FLUKA model of CMS IP5
ZDC Detector
BRAN

## Slide 5: 2011 CMS Tan (side view)
Air

## Slide 6: How we do simulations
Use geometry for ATLAS and CMS
Collide beams in the center of IR
Transport fragments through the Experimental Magnets and focusing dipoles to the TAN
Measure ionization deposited in the TAN/interacting particle
  We can then scale this number to number of interacting collisions/bunch

## Slide 7: ATLAS Simulation (p-p)
Fluence at BRAN
Energy Deposition at BRAN

## Slide 8: Momentum Distribution at BRAN
Large difference in # of particles allows the BRAN to detect PbPb collision
Even though there is significantly reduced luminosity

## Slide 9: Average Energy Collected/pp interaction
Difference of energy between ATLAS and CMS due to different absorbers
Total energy deposited decreases with increasing crossing angle
  Missing part of the shower
Mapped energy response from 3.5 to 7.0 TeV beam energy with varying crossing angle
  Plot at 240 µrad
If BRAN starts to saturate with increased intensity or luminosity
  can lower pressure and/or
  add attenuators.

## Slide 10: Crossing Angle Asymmetry
Define Crossing angle asymmetry ratio as
BRAN is sensitive to the crossing angle OF THE MACHINE
Ratio becomes steeper as energy of LHC increases
Full Crossing Angle

## Slide 11: Two methods of readout
All four quadrants read out for each bunch and turn
Data is processed in two ways
  Counting Mode (currently recorded for left side of each IP)
    Each bunch is counted as a “1” if exceeds a certain threshold
    Software integrates over a specific number of turns
    At lower luminosity this is linear as BRAN has a low acceptance
    At higher luminosity can saturate
  Pulse Height Mode (currently recorded for right side of each IP)
    The signal voltage for each bunch is collected and summed for a number of turns
    This higher statistical fluctuations but linear up to maximum digitization of the ADC (There are several ways to reduce the signal)

## Slide 12: Simulated Counting Mode with Pileup
Counting mode with thresholds of 10, 15, 20, 25 mV (value includes attenuators and cable lengths)
Counting mode is linear but starts to saturate as rate increases
One can reach a linear region by increasing threshold
# of collisions/bunch
% of bunches that trigger
% of bunches that trigger/
interacting bunches
# of collisions/bunch
10 mV
25 mV
10 mV

## Slide 13: Updating to Higher Lumi Configuration (2012+)
ATLAS 2011
ATLAS 2012

## Slide 14: CMS Update
CMS 2011
CMS 2012

## Slide 15: Work in Progress
How does the detector respond to Heavy Ion Collisions?
Demanding CPU requirements
New regime of physics for FLUKA
  In collaboration with FLUKA group at CERN

## Slide 16: How does the detector respond to Ion Collisions (fluence)?
208 pp collisions
1 Pb collision

## Slide 17: Difference in Crossing Angle PbPb
0 µrad
240 µrad

## Slide 18: Asymmetric Collisions for 2012
Very Preliminary results
LHC will be running p-Pb collisions later this year
Define p-Pb as p beam heading toward to the BRAN
Pb-p as Pb heading toward the BRAN
Results show that there will be a 103 asymmetry for left and right side
Depending on the luminosity probably will only be able to use one of the BRANs/IP
ATLAS at 1.38 TeV/A

## Slide 19: Goals for the Summer Student
Integrate latest models of the IP from CERN
Run simulations for 2012 data configuration
Compare PbPb and pp results

## Slide 20: Summary
We have done a detailed study of the BRAN for pp in the 2011 configuration
Working closely with CERN FLUKA group to incorporate the BRAN in their configuration and to develop the PbPb models
Implementing PbPb collisions
Preparing for LHC runs with p-Pb collisions
  Detector responses will be different for left and right sides
  Need to be prepared
  Decide BRAN configuration before this Asymmetric Ion Run