## Slide 1: LQ mechanical performances Status and lessons learned
Collaboration Meeting 18
May 7th to 9th 2012, FNAL
Helene Felice

## Slide 2: Overview
Magnet overview
LQ assemblies summary:
from LQS01a to LQS03
Lessons learned

## Slide 3: LQ Design overview
90 mm aperture coils with Ti poles
Iron pads, masters, yokes, Al shell
Pre-load with bladders and keys
Short-sample limits (4.5 K – 1.9 K)
  Gss: 240 T/m – 267 T/m
  Iss: 13.8 kA – 15.4 kA
  Peak field: 12.3 T - 13.6 T
End support: plate and rods
Magnet/coil length: 3.7/3.4 m

## Slide 4: LQ assembly
Total of 60 gauges mounted (q and z)
20 on shell, 32 on coil poles, 8 on rods
Four axial locations along coil length

## Slide 5: LQ strain gauges
Shell and coil stations
  q and z gauges thermally compensated
  10 shell stations
  4 stations per coil
2 gauges/rod => 1 signal/rod
Total of 60 gauges
Measurements presented here are averages of the various gauges

## Slide 6: FEM analysis supporting LQ
Preload for 260 T/m
sq and eq at 300 K
target (3D): + 56 MPa
  + 750 me
sq and eq at 4.3 K
target (3D): + 183 MPa
  +2080 me
  sq (MPa)
Shell
Preload for 240 T/m: 471 kN
sz and ez at 300 K
target (3D): +88 Mpa (178 kN)
  +455 me
sz and ez at 4.3 K
target (3D): + 239 MPa
  + 1138 me
Rod
End Contact pressure (Mpa)
Preload for 260 T/m
sq and eq at 300 K
target (3D): -82 MPa
  -580 me
sq and eq at 4.3 K
target (3D): -157 MPa
  -1031 me
sq (MPa)
Pole
NO gap

## Slide 7: LQS01a loading conditions
LQS01a Gradient preload: 230-240 T/m
Nominal
Oversized
Some unloading of the pole suggested lack of preload
From LQS01a to LQS01b
Reduction of the radial shimming from 30 to 15 mils
Fuji Test to confirm
LQS01b
LQS01a

## Slide 8: LQS01b azimuthal loading conditions
LQS01a Gradient preload: 230-240 T/m
LQS01b Gradient preload: 260-270T/m
LQS01b loading required a bladder pressure of 8000 psi

## Slide 9: LQS02 300 K Loading conditions
LQS01b training performance
  Target gradient reached in 2 quenches
  Good memory - Improved training rate
  220 T/m reached in 4 quenches
LQS01b loading sequence used as reference scenario for LQS02
  Target LQS02 shell strain: 700 – 900 me
    Bladders pressurized one quadrant at the time
    Max. bladder pressure: 7000 PSI (Upper bound is 8000 psi)
  Target LQS02 Rods strain: 500 me
    Applied at the end of the azimuthal loading like in LQS01a and b

## Slide 10: LQS02 loading conditions
LQS01a Gradient preload: 230-240 T/m
LQS01b Gradient preload: 260-270T/m
LQS02 Gradient preload: 260-270 T/m

## Slide 11: LQS02 Mechanical performance Cool-down
sq and eq at 4.3 K
average: +183 ± 9 MPa
average: +1960 ± 119 me
4.3 K target 3D/2D:
+ 183/179 MPa
  +2080/2271 me
Shell
Rod sz and ez at 4.3 K
average: +235 ± 10 Mpa
average: +1119 ± 47 me
4.3 K target (3D):
+ 239 MPa
  + 1138 me
Rod
Coil pole sq and eq at 4.3 K
average: -133 ± 28 Mpa
average: -764 ± 372 me
4.3 K target (3D/2D):
- 157 / -178 MPa
  -1031 / -1371 me
Pole

## Slide 12: LQS02 Mechanical performance Pole during excitation
From the measurements
some signs of unloading seen in LQS02
Ds during unloading is 100 MPa
Consistent with expected unloading due to Lorentz forces at 11 kA
Behavior consistent with low preload seen in a few stations
Ramps of the 08/12/2011 Measurements up to 11kA

## Slide 13: LQS02 Mechanical performance Rods during excitation
Variation of rod axial strain at 11 KA
  - + 10 to 20 me
Elongation of the coil
    - 34 to 68 microns

## Slide 14: From LQS02 to LQS03
Some uncertainty about the reason behind the lack of performance of LQS02
Concern about mid-plane block quenches
  Conservative approach by keeping the same preload (not higher)
  1-to-1 comparison with LQS02 – only change of conductor
  Unloading of the pole can be handled by a “healthy magnet” => TQS03a
  Possibility to increase the preload in LQS03b
227 T/m
209 T/m
93% Iss

## Slide 15: LQS03: Pressure sensitive film
The coils of LQS03 are similar in size to the LQS02 coils
Attempt to improve the cool-down:
  Decision to reduce the G10 shims between coil and pad from 15 (375 mm) to 10 mils (250 mm)
  Pressure sensitive film test to confirm

## Slide 16: LQS03 Azimuthal loading
Identical target as LQS02
Shell
Poles
Target 300 K: 750 me
Target 300 K: -600 me
724 me +/- 100
-597 me +/- 170
Target 4.4 K: 2100 me
Target 4.4 K: -1000 me

## Slide 17: LQS03 axial loading
Target 300 K: 455 me
472 me +/- 21
Max Piston pressure: 5900 psi (41 MPa)
Target 4.4 K: 1150 me

## Slide 18: LQ assemblies summary
56 MPa
-82 MPa

## Slide 19: LQS03 Status – Electrical checks
B4
B3
Short detected during sequential R measurement in coil 19 between Vtaps B3 and B4
Hypertronic connector
Ohm-meter
LQ19 => R = 0.9 ohm
Typical coil => R=23 ohm which includes wires + ss trace and coil segment
AWG 28 wires
Traces: 25 microns thick and 0.635 mm wide
Decision to unload axially the magnet

## Slide 20: Investigation
After axial unloading and removal of the endplate
After removal of the stainless steel pusher
After removal of the G10 pusher

## Slide 21: Status and Next steps
Repair completed
Preparation for axial loading ongoing
Axial loading will be performed at the end of the week while monitoring the status of B3 B4 vtaps
Shipment expected May 18th

## Slide 22: Lessons learned toward LHQ
From LQS01 to LQS01b
  Importance of the matching between
  coil OD and pad/collar ID
  Assessment required before each assembly using
  pressure sensitive film
From LQS02 and LQS03 assemblies
  High risk of pinching vtap wires during assembly
  Need to protect better the instrumentation to avoid damage during assembly
Still to investigate
  Spread in the SG reading: related to parts tolerances?
  Preload gain during cool-down: still smaller than expected from computation

## Slide 24: LQS01a Coil Stress distribution (FEM)
Shell stress: +148 MPa (2D) model
Pole stress: -59 MPa (2D) model
Coil pole tension: >20 MPa (inner layer)

## Slide 25: LQS01b Coil stress distribution (FEM)
Shell stress: +180 MPa (3D/2D) model
Pole stress: -160/-180 MPa (3D/2D) model
Coil pole compression

## Slide 26: LQS01b Pole SG measurements