## Slide 1: MICE RF System Overview
Derun Li
Center for Beam Physics
Lawrence Berkeley National Laboratory
MAP Winter Meeting at SLAC
March 6, 2012

## Slide 2: MICE RF System Overview
Hardware
  Two RFCC modules: two pairs of four 201-MHz RF cavities with 16 coaxial loop RF couplers and ceramic RF windows (two per cavity) - LBNL
  Amplifiers and power distribution systems - DL
  Vacuum and water cooling systems - RAL
  Diagnostics and control systems
Software
  LLRF firmware and cavity tuning control
MICE data analysis
  Controls and correlation between detectors and RF amplitude/phase
RF system design review held in December 2011

## Slide 3: 2 RFCC Modules in MICE Channel
RFCC Module #1
RFCC Module #2

## Slide 4: RFCC Module Overview
The MICE RF and Coupling Coil Module has been designed by LBNL and our collaborators
The MICE cooling channel incorporates two RFCC modules to be provided by LBNL
Each module consists of a single superconducting Coupling Coil integrated with four tunable 201 MHz normal conducting RF cavities and a vacuum vessel
The Coupling Coil design was developed by the Harbin Institute of Technology (HIT) in China (a MICE collaborator), in collaboration with LBNL
A third Coupling Coil (first delivered) for MuCool will be sited in the MTA at Fermilab
The 201 MHz cavity design is based on the prototype cavity developed by LBNL and J-Lab and has been operated in the MTA

## Slide 5: RFCC Module Overview
RF Cavities
Coupling Coil
Tuner arms
Couplers

## Slide 6: Status of RF Cavities
  Ten RF cavities (two spares) at LBNL now;
  All 11 beryllium windows received at LBNL;
  Ten ceramic RF windows;
  Six tuner flexures are being fabricated at
  Fermilab;
  Components for 6 actuators are being
  fabricated;
  RF loop coupler design has been updated to
  eliminate the gap between the outer coax and the RF loop;
  EP preparation in progress at LBNL:
    Fabrication of fixturing complete;
    ES &H approval for EP in progress at LBNL;
    Preparation of the cavity surface: mechanical smoothing;
    EP to start after the ES & H approval.
  Measurements of the remaining six cavities to start after EP;
  Each cavity will be tuned to a center frequency after EP.

## Slide 7
EP setup at LBNL
Tuner arms fabricated at FNAL
Coupler
design
Be windows at LBNL
Wire EDM at FNAL
Tuner design

## Slide 8: RF Power System Components
2 MW Amplifier
2 MW Amplifier
Master Oscillator
Controls etc
201 MHz Cavity Module
2 MW Amplifier
2 MW Amplifier
201 MHz Cavity Module
LBNL
CERN
300 kW Amplifier
300 kW Amplifier
300 kW Amplifier
300 kW Amplifier
HT Supplies
HT Supplies
Daresbury
DL Test System
At present
Auxiliary Systems
Auxiliary Systems
Not found

## Slide 9: RF Amplifier Status
Refurbishment of LBNL and CERN RF components:
  First medium power (250 kW) amplifier and power supply system tested 2008
  Refurbishment and rebuild of first high power (2 MW) amplifier complete October 2009
  Power supplies for first 2 MW amp operational
  Two further 300 kW amplifiers awaiting repair
  Two refurbished 2 MW CERN amplifiers partly tested, awaiting assembly and high power test
Need to build 3 more sets of power supplies
One more 300kW amplifier to buy/acquire

## Slide 10: RF Power Distribution
Trombone phase shifter
Hybrid power splitter
RF load
Outputs to cavity

## Slide 11: RF Power Distribution

## Slide 12
4616 Medium Power Amplifier
High Power Amplifier
MTA RF setup
Andrew Moss working at Daresbury Laboratory
Reached 1 MW RF power

## Slide 13: MICE RF Power 1 MW/cavity

## Slide 14: 20 kV Power Supply for 4616
Capacitor Charger
20 kV+
Control Crate
PLC Crate
Heater Controller
Grid PSU
(300 Vdc)
Screen PSU (600 Vdc)
Screen Pulser
(2000 Vdc)
RF solid state amplifier
RF Signal Generator
(201 MHz)
4616 Tube
Heater Transformer
Crowbar (Ignitron)
Capacitor
29 uF
Dump Relay
HV Power Supply 20 kV
Auxiliary Rack
Earth Switch
Water cooling
circuits (4)
Compressed air
cooling
HV cable
0.95V
500A
Grid cable
Screen cable
RF cable
RF output (co-ax)
4616 Circuit
Enclosure
Resistor bank

## Slide 15: 38 kV Power Supply for TH116
Capacitor Charger
40 kV+
Control Crate
PLC Crate
Heater Controller
450V DC Bias PSU
TH116 Tube
Heater Transformer
Crowbar (Thyratron)
Capacitor
140 uF
Dump Relay
HV Power Supply 38 kV
Auxiliary Rack
Earth Switch
Water cooling circuit
Compressed air
cooling
HV cable
20V
500A
RF input from
4616 (co-ax)
RF output (co-ax)
TH116 Circuit
Enclosure
Cathode Modulator
Cooling Fans
Trigger pulse
Resistor bank

## Slide 16: RF Test Area at DL

## Slide 17: Water Cooling System at DL
DL site cooling system decommissioned
Ex-SRS twin-circuit chiller installed
  Demin for amplifiers
  Glycol for load
Now fully operational

## Slide 18: TH116 Circuit #1
Mechanically complete
New fans fitted
Cathode modulator built
Motorised tuners
Electrical control panel
Heater controller
Safety interlocks
Tested to 1 MW RF output

## Slide 19: Cathode Modulator
IGBT switch
IGBT control board
Potential divider
Zener diode array
38 kV
Trigger
450Vdc
15k
2R7
33R
From 4616
IGBT
TH116
TH116 CATHODE MODULATOR CIRCUIT
Fully operational
Second unit now complete

## Slide 20: Circuit Tuning Motors

## Slide 21: TH116 Electrical Control Panel
Fan control-gear
Heater controller (thyristor)
Circuit-breakers
Tuning control relays

## Slide 22: RF Control and Monitor System
Network/ Controls Rack
VME Crate
Canbus modules
DAC/ADC modules
EPICS Server
Heater Controller (4616)
450V DC Bias PSU
Digital signals/serial link
4616 & TH116
Aux. Racks
PLC Crate (4616)
Grid PSU (4616)
Analog & digital signals
Heater Controller (TH116)
Analog & digital signals
Analog & digital signals
Interlocks
Panel switches
Water flow
Compressed air pressure
Heater V and I
Heater V and I
Interlocks
Typical I/L
PLC Crate (TH116)
Digital signals/serial link
Screen PSU (4616)
Analog signals
Analog signals
Enable
Enable
Enable
Enable
Enable
Interlocks

## Slide 23: RF Power Supplies – MICE Hall Layout
Layout of North Mezzanine
Air Conditioning Units
RF Amplifiers
RF Power Supply Racks
RF Network/Control Racks

## Slide 24: Current Status/Plan of RF Power Sys.
Amplifier test system tested to 1 MW with power supplies;
Coax system designed to phase match RF into each cavity, all coax lines are the same length and have the same number of elbows;
Hybrids will be used to split RF power and give good isolation, reject load can be small as balanced reflected; power will be directed back to triode, this should not present an issue;
Cavity phasing can be done using a combination of LLRF and limited range high power phase shifters;
Nitrogen gas pressure will be used to extend the peak voltage stand off of the coax guides.

## Slide 25: Single Cavity Vacuum Vessel
The design kept as much as possible of
the same dimensions and features of
the RFCC module
One vessel to accommodate two types
of MICE cavities (left and right)
Possible for future LN operation
RFCC module

## Slide 26: Single Cavity Vacuum Vessel Status
Design was completed in mid-2011 at LBNL
Fabrication is complete at Keller Technology
in Buffalo New York
The vessel should arrive Fermilab this week

## Slide 27: Testing of the Single Cavity Vessel
Check engineering and mechanical design
  Fully define the fabrication process
  Incorporate any design changes into the RFCC vacuum vessel design
Test of the RF tuning system with 6 tuners and actuators on a cavity and verify the frequency tuning range
Obtain hands-on experience on assembly and procedures
Cavity installation
  Develop fixturing for inserting the cavities into the vacuum vessel
  Beryllium windows
  RF couplers and connections
  Water cooling pipe connections

## Slide 28: Testing of the Single Cavity Vessel
  Vacuum port and connections
  Tuners and actuator circuit
  Mounting and alignment of the tuners onto the cavity is critical to alignment of the cavity in the vacuum vessel
  Alignment of actuator (through the vacuum vessel wall) to the tuner is important
Aligning cavity with hexapod support struts
  Test developed MathCAD alignment software program
Vacuum vessel support and handling
Verify operation of the getter vacuum system
RF processing MICE cavities
RF power system and future LN operation

## Slide 29: Summary and Tasks
Progress in MICE RF hardware development;
Progress of RF system and control;
Specification/Interface between RF power system and RFCC modules;
Plan/development for diagnostics and controls, in particular with detector/analysis group:
  Communications/meetings started recently at LBNL, but need a real plan;
  A LLRF/DAQ Workshop will be held April 16-17 in DL, UK
Testing plan of using the single cavity vessel at the MTA, Fermilab
  Waiting for cavity EP at LBNL, fabrication of other accessory components;
  Assembly and integration;
  MICE cavity tuning and control;
  Experimental study of high magnetic field at RF coupler region;
  Welcome RF testing proposals from MAP collaborators.