## Slide 1: Target Magnets & Shielding
Bob Weggel
Particle Beam Lasers, Inc.
Magnet Optimization Research Engineering, LLC.
March 4, 2012

## Slide 2: Isometric View of Three Target-Magnet Designs
Design IDS120h (top), IDS120i (middle) & IDS120j (bottom) [courtesy Van Graves]

## Slide 3: Cross Sections of Target-Magnet Designs [courtesy Van Graves]
IDS120h: I.R.’s step down gradually from 120 cm to 45 cm; minimal gaps between coils
IDS120i: Large gaps between cryostats; I.R.’s = [120, 100, 80, 60] cm; gaps at [3, 9, 15] m
IDS120j: 3 coils per cryostat; I.R.’s = [120, 90, 70, 50] cm; gaps at [4,10,15] m; zmax = 20 m

## Slide 4: Cross section of Coils & Shielding Vessels of IDS120h
Tubes & flanges: = 7.85 g/cm3; shielding = 10 g/cm3; Outer ≈ 30 tons/m; Inner ≈ 8 tons/m.

## Slide 5: Isometric View of Meshed Shielding Vessels of IDS120h

## Slide 6: Sag of Shielding Vessel vs. Length L & Wall Thickness t
O.R.max = 114 cm; I.R.min = 60 cm; γ = 7.85 g/cm3; γshielding = 10 g/cm3; tin = ½tout; ~30 tons/m.
With tout = 4 cm, tin = 2 cm & L = [6, 7, 8, 9] m, sagFEM = [1.5, 2.5, 4.1, 6.4] mm Limit L to 8 m.

## Slide 7: Sag of Shielding Vessel vs. Length L & Wall Thickness t
O.R.max= 58 cm; I.R. min = 16 cm; tout = 4 cm; tin = 2 cm; γ = 7.85 g/cm3; γshielding = 10 g/cm3;
~8 tons/m. When L = [6, 6½, 7, 7½, 8] m, sag = [2.0, 2.9, 4.0, 5.4, 8.0] mm  Limit L to 7 m.

## Slide 9: Normalized Maximum Hoop Stress σ* ≡ σmax / (B1 j1 a1)
a1 ≡ I.R. of coil; a2 ≡ O.R. of coil; B1 ≡ B(r=a1), B2 ≡ B(r=a2); j1 ≡ current density

## Slide 10: On-Axis Field Profile B(z)of Target Magnet IDS120j
<B(z)> = 20 T over the 75-cm length centered at z = −37.5 cm. B(z=15 m) ≈ 1.5 T.

## Slide 13: Field Magnitude |B| ≡ (Br2+Bz2)½ of Target Magnet IDS120j
Maximum field = 20.4 T; contours at 1.5 T and integer values from 1 T through 20 T

## Slide 14: Hoop Strain σhoop in Magnet of Copper Hollow Conductor
700-MPa coil banding limits σhoop in each coil to 0.35%; contour interval = 0.02%.

## Slide 15: σhoop in Copper & Nb3Sn Magnets (Most-Upstream Cryostat)
Maximum hoop strain in each coil is 0.35%; contour interval = 0.02%.

## Slide 16: σhoop in Coils of Cryostat #2 (NbTi Conductor)
Maximum hoop strain in each coil is 0.35%; contour interval = 0.02%.

## Slide 17: σhoop in in Coils of Cryostat #3 (NbTi Conductor)
Maximum hoop strain in each coil is 0.35%.

## Slide 18: σhoop in Coils of Cryostat #4 (NbTi Conductor)
Maximum hoop strain in two upstream coils = 0.35%; max.(σhoop) in downstream coil also is 0.35% if one adds an identical set of coils downstream.

## Slide 19: Target Magnet “DS120j5”: Optimized I.R. of Flanking Coils
I.R.’s of coils in cryostats #2-#4 are [120, 90, 116] cm, [76, 70, 75] cm & [67, 50, 67] cm.

## Slide 20: On-Axis Field Profile B(z)of Target Magnet IDS120j5
Maximum field error is nearly 30% less than in design IDS120j.