MOM Update
Status of the MICE Online Systems
Pierrick Hanlet
 6 March 2012

---
Outline
Introduction
Data Acquisition
Online Reconstruction
Controls and Monitoring
Infrastructure
Conclusions

---
Outline
Introduction
Data Acquisition
Online Reconstruction
Controls and Monitoring
Infrastructure
Conclusions

---
Introduction
Beamline – create beam of muons
Particle ID – verify/tag muons (before/after)
Spectrometers – measure e (before/after)
Absorber (LH2 or LiH) – cooling
RF – re-establish longitudinal momentum
MICE beamline
MICE cooling channel

---
Online Responsibilities
The MICE Online Group creates, maintains, and ensures proper use of all tools (hardware, software, and documentation) within the MICE Local Control Room (MLCR) used by the experiment to efficiently record high quality data. We are responsible for:
Data Acquisition (DAQ)
Online Monitoring and Reconstruction (OnMon/OnRec)
Controls and Monitoring (C&M)
Data Transfer
Networking and MLCR Computing
We also interface closely with systems related to the Online sector including MICE Operations, Offline Software, and Computing

---
Online Structure
Linda Coney	– head of Online Group, Online Reco
David Colling	– head of Software & Computing, GRID PP contact
Yordan Karadzhov	– head of DAQ, OnMon
Pierrick Hanlet	– head of C&M, connection to Config DB
Daresbury Lab	– C&M - Brian Martlew (head of DL group)
Paul Hodgson	– C&M (target)
Matt Robinson	– C&M (target,tracker), System Administrator
Mike Courthold	– Networking
Henry Nebrensky	– GRID, Data Transfer, MICE Data Manager
Janusz Martynikk	– MICE Data Mover – Data of Online System
Paul Kyberd	– GRID, Contact person for GRID PP
Craig Macwaters	– MLCR Network, Hardware, Computing
Antony Wilson	– Config DB, MICE PPD IT Contact
Chris Rogers/Chris Tunnell – link with Software Group

---
Online Structure

---
Online Group
New leadership and organization (June '11)
Redmine used to record/track issues
prioritize issues and effort
search-able
remotely accessible
Excellent progress successful Dec '11 run

---
Outline
Introduction
Data Acquisition
Online Reconstruction
Controls and Monitoring
Infrastructure
Conclusions

---
Data Acquisition
Description:

---
Data Acquisition
DAQ and Trigger requirements:
stable over long-term & maintainable
non-expert use (documentation)
600 particles per 1 ms spill at 1 Hz
event size <60 MB (normally ~30 MB)
flexible:
select FEE to read and trigger
run independently of target and RF
interface with C&M
interface with OnMon & OnRec

---
Data Acquisition
Description:
Interface
w/Target &
Spill Gate
DAQ Trigger
distribution
KL
TOF & CKOV
Scalars and particle
trigger NIM Logic
DATE (ATLAS)
framework
Shapers
GVA Discri,
KL cosmics trg
TOF discriminators and
trigger CAMAC Logic

---
Data Acquisition
Status:
prototype EMR detector and electronics successfully integrated
simultaneous readout of both trackers during cosmic ray data-taking using DATE
communication established linking DAQ, C&M, and CDB – allows monitoring of the DAQ status and archiving of DAQ parameters in the CDB
new unpacking code

---
Data Acquisition
Efforts:
upgrade DAQ – DATE version and OS
software trigger selection
incorporate new detectors
EMR – spring cosmic run with new DAQ
tracker – single tracker station test
improve system performance
improve error handling
incorporate new DAQ computers (LDCs)
integrate with C&M and CDB

---
Outline
Introduction
Data Acquisition
Online Reconstruction
Controls and Monitoring
Infrastructure
Conclusions

---
Online Monitoring
and Reconstruction
Two components:
Monitoring (OnMon)– DAQ raw distributions
Reconstruction (OnRec) – same code as offline reconstruction software
OnMon and OnRec run over socket
Now using new MAUS software framework
Excellent progress successful Dec'11 run

---
Online Monitoring
new unpacking software
TOF hit profiles
trigger
fADC
TDC
CPU monitor
parallelization
scalars
preliminary
MAUS TOF
hit profiles

---
Online Reconstruction
real-time physics & detector functionality
TOF, KL, & CKOV detector readout
beam dynamics parameters
time-of-flight distributions for PID
data transfer out of the MLCR (Online responsibility limit) automated
archives of all online plots
data transferred to public webserver

---
Online Reconstruction
t1-t0
TOF 2D profiles
t2-t1
trace-space
distributions
t2-t0
Dt distributions
px vs x
py vs y
m momentum

---
Outline
Introduction
Data Acquisition
Online Reconstruction
Controls and Monitoring
Infrastructure
Conclusions

---
Controls & Monitoring
Purpose:
Controls refers to:
user interface to equipment
proper sequencing of equipment
Monitoring serves to:
protect equipment (early notification)
protect data quality
user monitoring

---
Controls & Monitoring
Status and immediate needs:
Step I complete
Beamline
Particle ID – PID
Alarms, archiving, external gateway
Experimental hall environment
SS and FC acceptance testing
Run Control

---
Controls & Monitoring
Next focus – cooling channel:
AFC
m
trackers
RFCC

---
Controls & Monitoring
ON / OFF
ON / OFF
ON / OFF
ON / OFF
ON / OFF
SD16
CX05
SD11
SD05
CX06
SD12
SD06
CX07
SD07
CX08
SD27
SD01
CX09
SD15
SD03
SD10
CX01
CX02
CX12
Level 1
Level 2
Level 3
CC 1
CC 2
CC 3
CC 4
Single
CC 5
Pressure
SD02
SD08
SD14
Vacuum Vessel
Radiation Shield
Cold Mass
Heater Power
SD26
SD25
SD23
SD19
Fill Line
Heater Power
CX11
CX10
ON / OFF
SD13

---
Controls & Monitoring
quench
protection
(FNAL)
standalone
C&M (DL)
power
supply
(LBNL)

---
Controls & Monitoring
MICE is a precision experiment:
measure a muon cooling effect to 0.1%
imperative – control all systematic errors
ensure data taking parameters of all of the apparatus in MICE be carefully recorded/restored to/from the CDB.
To accomplish this, the target DAQ,
the experiment DAQ, controls for beamline elements, MICE state machines, and PID have been integrated with the CDB into a single “Run Control” process.

---
Controls & Monitoring

---
Controls & Monitoring
Other aspects and future:
FC – similar to SS (due at same time!)
RF tuners – MTA single 201MHz RF cavity
MICE Hall services control
EMR test
Target & Tracker controls upgrade
LH2
RF

---
Outline
Introduction
Data Acquisition
Online Reconstruction
Controls and Monitoring
Infrastructure
Conclusions

---
Infrastructure
Dedicated system administrator!!!
Necessary improvements made to the online system infrastructure:
Hardware vulnerabilities were assessed, leading to the replacement of several DAQ crates and the purchase of spares
Easily-swapped-in computers have been prepared in the event of key machine failure
All hardware damaged during an unexpected power surge in early 2011 has been repaired or replaced

---
Infrastructure
An upgrade of the OS for all online computers has been initiated using two test computers added to the MLCR network to facilitate a controlled migration
Operations and Online systems documentation has been reviewed, updated, and posted

---
Online Future
March run for online software tests
June run for EMR and single station tracker
Present foci:
C&M for Step IV
DAQ for EMR (June)
DAQ for single tracker station (June)
continued involvement from software group for online reconstruction
online accelerator physics analysis tools

---
Summary
Online group restructured June'11
Online Systems in place
Step IV work progressing well
Evolving needs being recognized and met

---
Backup slides

---
Controls & Monitoring
Procedure for a data taking run:
query: run & trigger types, beamline, etc
query: C&M for MICE states, verify compatibility with requested run
query: CDB for beamline and particle ID settings for requested run configuration
determine apparatus readiness (states) and initiate setting beamline and PID parameters
query target DAQ for actuation number, target depth and delay
give pertinent information to experiment DAQ and initiate arming procedure
inhibit C&M from allowing any changes
user initiates run, Run Control reads experiment parameters and stores them in CDB
end of run, query for final actuation number, sum scalers, and write end of run values to CDB and to experiment DAQ