## Slide 1: Barium daughter tagging for more sensitive 0nbb decay detection
William Fairbank
Putting together input from the NEXT and nEXO Collaborations

## Slide 2: Novel instrumentation: 136Ba daughter tagging in bb decay “Physics areas”
Neutrinoless double beta decay
The only known sensitive way to establish the Majorana nature of the neutrino
Observation would establish violation of lepton number conservation.
Potential window into matter-antimatter asymmetry in the Universe.
Would shed light on neutrino mass and the origin of that mass.
Detecting 136Ba daughter provides final discrimination against all non-bb decay backgrounds and increases 0nbb sensitivity
Both the NEXT and nEXO collaborations are developing methods of Ba tagging for use in future 0n bb detectors
136Xe double beta decay

## Slide 3: Demonstrators
CCD
TPX Cam
Ba2+
e
e
e
EL (+HV)
RFC
CCD
CCD
TPX Cam
CCD
Ba++ ion
10 bar Xe
NEXT Data
2. Single Ba2+ ion tagging w/SMFI
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
3. RF Carpet ion transport in xenon gas
SIMION simulation
NEXT-CRAB concept:
NEXT-BTX concept:
Single ion sensor development is now fairly advanced
Important R&D remains for ion concentration and collection:
  Sensor-to-ion (BTX concept)
  Ion-to-sensor (CRAB concept)
 Demonstrator phases under intensive development on 2-3 year timescale
Molecules found that fluoresce when Ba++ ion is captured
Single molecules with Ba++ can be imaged

## Slide 4
Ba tagging with single Ba ions extracted to Xe gas and vacuum
RF funnel has been operated and is being improved.
Linear Paul Trap, Quadrupole mass filter and MRTOF have been built are being commissioned.
Work on demonstration of a laser ablation source in high-pressure gas
Upgraded nEXO TPC

## Slide 5
Barium tagging by imaging of single Ba atoms and ions in solid Xe
Ion Source
ExB Filter
Cryostat
Concept tested with mass-selected Ba+ ion beam in vacuum
Window with a little frozen SXe
SXe on cryoprobe frozen from LXe and raised

## Slide 6: "Instrumentation Requirements"
Instrumentation Requirements include:
Extraction of the daughter 136Ba from a large 0nbb TPC
Transport to a single Ba detection region
Count 1 or 0 Ba atom
Do all this with high efficiency and selectivity
Do it with equipment that does not compromise event detection capability and uses low background materials.

## Slide 7: "Instrumentation Challenges"
Instrumentation challenges include:
Detecting single Ba atoms – much progress but continued R&D to achieve high efficiency and selectivity
R&D on extraction and transport in each case
Implement controlled and characterized sources of Ba isotopes for tests
  e.g., radioactive Cs isotopes beta decay to Ba isotopes
  Eventually 2nbb decays as a source
Detect Ba daughters from individual decays - Cs beta decays in small Xe test cell and then 2nbb decays in a large enough TPC
Engineering of a 0nbb decay detector with Ba tagging

## Slide 8
For nEXO, Ba tagging is envisioned as a possible upgrade after n years of operation.
There are considerable engineering challenges even after Ba tagging is demonstrated on a smaller system.
Experiments with 139Ba daughters from 139Cs b decay planned at TRIUMF
Development of technology to extract daughter 136Ba from anywhere in a LXe detector vessel
Some of the next phase work beginning
nEXO TPC:

## Slide 9
For NEXT, Ba tagging is envisioned as a capability for second module in an N-module system
Outline of NEXT Ba tagging activities for Snowmass period:
Sensors (both molecules and microscopes) under continuing optimization for efficient dry ion sensing using both Ba++ and Rn++ beams at table-top scale, targeting convergence in ~2-3yr.
At least one of ion-to-sensor or sensor-to-ion transport methodologies must be proven. Focus is now shifting onto this challenging aspect of the problem.
Ambition is to follow R&D in first half of Snowmass period with tests using Ba from 2nubb in demonstrator-scale 136Xe underground system(s) during the second half.
High pressure single molecule microscopy in xenon gas
STM showing dry barium chelation in crown ether complex
Planning for first NEXT-Ton module without barium tagging at Canfranc is underway, with EOI submitted to LSC in 2021.

## Slide 10
Summary
Single Ba atoms and ions can be detected by laser imaging techniques – many photons from one atom or ion
R&D on methods of 136Ba daughter transport to a single Ba detection region continues through Snowmass period
Staged approach toward demonstrator detectors is planned for the Snowmass period.
136Ba daughter tagging is considered an important technique for background free neutrinoless double decay detectors of the future