## Slide 1
Preliminary Study of Target Shapes for g-2 with Yield Measured at Start of M2 Beamline

## Slide 2
Purpose of today’s presentation is to simulate capture of pions to end of 3 deg bend and cross check against Sergei Striganov’s study at the target
Targets with a slab configuration are introduced to simulate a side of a thin wall cylinder that is more realistic than an thin rod target.
Overview

## Slide 3
100 million Protons on Target (POT)
KE = 8 GeV
Using Sergei’s (1/10/12) most optimistic spot size:
σx = σy = 0.15 mm, ε = 0.3 mm-mrad
σx’ = σy’ = 0.6366 mrad
From design goal (Weiren’s Oct. 27, 2011 talk):
σt = 20 nsec (100 nsec full width; 2.5 sigma)
Proton Beam Properties

## Slide 4
Target material is the nominal inconel that was used for pbar production.
Distance from center of target to center of Li lens is 25.16 cm (the old nominal). Dean Still has a different distance, but did not bother to change this for this study.
Lens is 16 cm long and 1 cm radius.
Gradient in lens is 256.25 T/m
PMAG is reverted back to that in Nikolai’s original MARS file which scaled B from 8 GeV protons to 3.1095 GeV/c pions:
B = 0.542219 T.
  Choice is based on making P(pi+) distribution at start of M2 to peak near 3.1 GeV/c rather than forcing reference to follow 3○ bend.
Target, Li Lens, & PMAG Properties

## Slide 5
100 protons on target
Virtual detector at entry of 1st quad in M2 line. R = (3.28/2)”=4.17cm
Top View of Targetry Layout
(material sliced in y=0 plane)
Fe
1/16” SS316
Various targets used

## Slide 6
Target length = 74 mm is chosen based on assumption that β = 1.5 cm is possible.

## Slide 7
Dependence on target radius is weak.
Will use radius = 0.375 mm or width = diameter = 0.75 mm for nominal target.

## Slide 8
Target Shape | Target Length (mm) | Target Width / Diameter (mm)
Cylinder | 74 | 0.75
Horizontal Slab* | 74 | 0.75
Vertical Slab | 59, 74, 89 | 0.60, 0.75, 0.90
Default Pbar Target | - | -
Target Shapes and Dimensions Studied
Pmagic = 3.094 GeV/c
P(pi+ & protons) = 3.15588 GeV/c +/- 2% (1.02 x Pmagic +/- 0.02 x Pmagic)
P(mu+) = 3.094 GeV/c +/- 0.15%
* Will simulate multiple target lengths and widths for horizontal slab in near future.

## Slide 9
Target Shape | Length (mm) | Width/ Diameter (mm) | N(pi+)/POT | N(proton)/POT | N(mu+)/POT
Cylinder | 74 | 0.75 | 4.735x10-5 +/- 2.0% (+8.65% wrt default) | 1.004x10-4 +/- 1.4% (+10.3% wrt default) | 2.627x10-8 +/-58%
Horizontal Slab | 74 | 0.75 | 4.684x10-5 +/- 2.0% (+7.48% wrt default) | 9.891x10-5 +/- 1.4% (+8.69% wrt default) | 8.553x10-8 +/-45%
Vertical Slab | 74 | 0.75 | 4.684x10-5 +/- 2.0% (+7.48% wrt default) | 9.862x10-5 +/- 1.4% (+8.37% wrt default) | 1.086x10-12 +/-71%
Default Pbar Target* | - | - | 4.358x10-5 +/- 2.1% | 9.100x10-5 +/- 1.4% | 3.556x10-8 +/-41%
Yields vs. Target Shapes
*Comparison of 4.358x10-5 pi/POT here to 0.718x10-5 pi/POT reported in 12/21/2011 meeting has two components that have changed:
  PMAG(12/21) = 0.51236T (3 deg) vs. PMAG(today) = 5.422T(default)
  Spot size: 12/21: σx=0.5533mm σy=0.551.1066mm; σx’=σy’=0.00038
    Today: σx = σy = 0.15 mm; σx’ = σy’ = 0.0006366
  Will simulate with old spot size and updated PMAG in future to quantify gain from reduced spot size.
Sergei’s conclusion of 40% increase assumes target is immersed in a lattice with optimal beta value.
If relative yield between cylinder target and default target is preserved between analyses at target and that at end of 3 degree bend (M2 start), then value of beta at the target can be estimated using Sergei’s 1/10/12 study. See next slide.

## Slide 10
Sergei Striganov’s 1/10/12 Target Team Meeting
+8.7%
β = 3.5 cm?

## Slide 11
Length (mm) | Width (mm) | N(pi+)/POT | N(proton)/POT | N(mu+)/POT
59 | 0.60 | 4.126x10-5 +/- 2.1% (-5.32% wrt default) | 8.879x10-5 +/- 1.4% (-2.43% wrt default) | 1.865x10-8 +/-50%
59 | 0.75 | 4.205x10-5 +/- 2.1% (-3.51% wrt default) | 8.871x10-5 +/- 1.4% (-2.52% wrt default) | 3.79x10-8 +/-50%
59 | 0.90 | 4.197x10-5 +/- 2.1% (-3.69% wrt default) | 8.855x10-5 +/- 1.4% (-2.69% wrt default) | 3.637x10-8 +/-58%
74 | 0.60 | 4.696x10-5 +/- 2.0% (+7.76% wrt default) | 1.001x10-4 +/- 1.4% (+10.0% wrt default) | 6.879x10-13 +/-100%
74 | 0.75 | 4.684x10-5 +/- 2.0% (+7.48% wrt default) | 9.862x10-5 +/- 1.4% (+8.37% wrt default) | 1.086x10-12 +/-71%
74 | 0.90 | 4.841x10-5 +/- 2.0% (+11.1% wrt default) | 9.944x10-5 +/- 1.4% (+9.27% wrt default) | 2.524x10-8 +/-58%
89 | 0.60 | 4.944x10-5 +/- 2.0% (+13.4% wrt default) | 1.073x10-4 +/- 1.4% (+17.9% wrt default) | 1.797x10-8 +/-58%
89 | 0.75 | 5.014x10-5 +/- 2.0% (+15.1% wrt default) | 1.097x10-4 +/- 1.4% (+12.1% wrt default) | 1.507x10-8 +/-45%
89 | 0.90 | 5.041x10-5 +/- 2.0% (+15.7% wrt default) | 1.081x10-4 +/- 1.4% (+11.9% wrt default) | 1.793x10-8 +/-50%
Default Pbar Target |  | 4.358x10-5 +/- 2.1% | 9.100x10-5 +/- 1.4% | 3.556x10-8 +/-41%
Yields for Vertical Slabs of varying dimensions

## Slide 12
Chart: 
| 0.6 | 0.75 | 0.9
Length = 59 mm | 4.126e-05 | 4.205e-05 | 4.197e-05
Length = 74 mm | 4.696e-05 | 4.684e-05 | 4.841e-05
Length = 89 mm | 4.944e-05 | 5.014e-05 | 5.041e-05
Vertical Target Yields for Pi+

## Slide 13
Check consistency with Sergei’s results for pion yields versus target length

## Slide 14
Length (mm) | Width (mm) | N(pi+)/POT | N(proton)/POT | N(mu+)/POT
59 | 0.60 | 4.126x10-5 +/- 2.1% (-5.32% wrt default) | 8.879x10-5 +/- 1.4% (-2.43% wrt default) | 1.865x10-8 +/-50%
59 | 0.75 | 4.205x10-5 +/- 2.1% (-3.51% wrt default) | 8.871x10-5 +/- 1.4% (-2.52% wrt default) | 3.79x10-8 +/-50%
59 | 0.90 | 4.197x10-5 +/- 2.1% (-3.69% wrt default) | 8.855x10-5 +/- 1.4% (-2.69% wrt default) | 3.637x10-8 +/-58%
74 | 0.60 | 4.696x10-5 +/- 2.0% (+7.76% wrt default) | 1.001x10-4 +/- 1.4% (+10.0% wrt default) | 6.879x10-13 +/-100%
74 | 0.75 | 4.684x10-5 +/- 2.0% (+7.48% wrt default) | 9.862x10-5 +/- 1.4% (+8.37% wrt default) | 1.086x10-12 +/-71%
74 | 0.90 | 4.841x10-5 +/- 2.0% (+11.1% wrt default) | 9.944x10-5 +/- 1.4% (+9.27% wrt default) | 2.524x10-8 +/-58%
89 | 0.60 | 4.944x10-5 +/- 2.0% (+13.4% wrt default) | 1.073x10-4 +/- 1.4% (+17.9% wrt default) | 1.797x10-8 +/-58%
89 | 0.75 | 5.014x10-5 +/- 2.0% (+15.1% wrt default) | 1.097x10-4 +/- 1.4% (+12.1% wrt default) | 1.507x10-8 +/-45%
89 | 0.90 | 5.041x10-5 +/- 2.0% (+15.7% wrt default) | 1.081x10-4 +/- 1.4% (+11.9% wrt default) | 1.793x10-8 +/-50%
Default Pbar Target |  | 4.358x10-5 +/- 2.1% | 9.100x10-5 +/- 1.4% | 3.556x10-8 +/-41%
Yields for Vertical Slabs of varying dimensions

## Slide 15
Sergei Striganov’s 1/10/12 Target Team Meeting
β = 3.5 cm?
r = 0.45 mm, d = 0.90 mm
Dependence on Target Length

## Slide 16
Check consistency with Sergei’s results for pion yields versus target width

## Slide 17
Chart: 
| 0.6 | 0.75 | 0.9
Length = 59 mm | 4.126e-05 | 4.205e-05 | 4.197e-05
Length = 74 mm | 4.696e-05 | 4.684e-05 | 4.841e-05
Length = 89 mm | 4.944e-05 | 5.014e-05 | 5.041e-05
Vertical Target Yields for Pi+

## Slide 18
Sergei Striganov’s 1/10/12 Target Team Meeting
β = 3.5 cm?
Dependence on Target Radius/Width
not 74 mm

## Slide 19
Summary & Future
Yields at end of 3 deg bend is consistent with Sergei’s study if β = 3.5 cm for existing Li lens system extrapolated back to target.
Simulations planned:
  Default pbar target with old larger spot size and PMAG = default to quantify enhancement due to smaller spot size.
  Multiple target lengths and widths for horizontal slab, where pions bubble off the side of the target in the non-bend plane. Large vertical beta in 1st quad may negate any gain, but quads can be adjusted and so forth…
Question: Should we choose one configuration (default?) to make a high statistic sample and convert to g4beamline tracks?

## Slide 20
Backup