## Slide 1: BPM Udates
January 31, 2012

## Slide 2: Overview
Reviewed beam path for both g-2 and Mu2e operations, as well as beam requirements. See the two talks listed in https://indico.fnal.gov/categoryDisplay.py?categId=203 for slides.
We assumed the beam requirements shown in the next slide.
We set the target beam intensity to the target that the BPMs would have to operate in as between 0.5e12 and 1.0e12.

## Slide 3
Beam Line/Ring (Service Building) | g-2 | Mu2e
P1->P2->M1 (Ap1) (MI-60, F0, F1, F2, F23, F27, AP0) | 1.0E12 primary beam (protons) 2.5 MHz 120 nsec 8.89 GeV/c <rate>=15Hz burst up to 100Hz | 1.0E12 primary beam (protons) 2.5 MHz (no longer 53MHz) 120 nsec 8.89 GeV/c <rate>=6Hz burst up to 18Hz
Target (AP0) | AP0 | N/A
M2 (AP2) ->M3 (AP3) (AP0, F27, AP30) | Low intensity secondaries (105 m+, 107 p+, 2 x 107 protons) 3.1 GeV/c | Same as P1->P2->M1 {No M2}
Accumulator | N/A | N/A
Debuncher (AP10, AP30, AP50) | 3.1 GeV/c Secondaries (105 m+, 2 x 106 p+, 2 x 107 protons) Circulates a few turns Kicked out | Same as P1->P2->M1 Slow Resonant Extraction every 56 msec
Abort Line (old downstream AP2) (AP50) | Low intensity 3.1 GeV/c protons 10msec burts | 3 to 5% of primary protons
M4 (new), g-2(new) (AP30, Experimental Halls) | Low intensity 3.1 GeV/c m+ Pulses every 10msec | 1.0E12 protons Slow spill every 56 msec

## Slide 4: Beam Line BPMs
Review plan for beam line (P1, P2, M1, M2, M3) BPMs and Delivery Ring BPMs for g-2 and Mu2e operations. P1, P2 and M1 BPMs will be used with both Mu2e and g-2 operations.
  Will use existing Echotek BPM electronics
  Peter will need to revisit the signal intensity and gain in the channels for 2.5Mhz and modify the Mu2e BoE accordingly.
M3, Delivery Ring and maybe Delivery Ring Abort can use existing BPM hardware and repurposed BPM Echotech electronics for Mu2e operations.
  Need 1st turn and closed orbit capabilities.
  The 2.4Mhz Delivery Ring RF should be in the operating range of the existing 2.5MHz filters used in the Echotech systems.

## Slide 5: Rings BPMs
M2, M3, Delivery Ring, Delivery Ring, M4, and g-2 will most likely not be able to use our existing BPMs We may want to consider running two different sets of BPM electronics/hardware - one for Mu2e and one for g-2.
One limiting factor for 2.5MHz beam is the length of the BPMs. To get the same signal per beam intensity registered on a 53MHz BPM, the physical size of the BPM must be much larger - up to 21 times longer! For g-2 operations, we could consider installing a couple "long" BPMs in straight sections. This would give us possible BPM measurements in a few locations around the ring.
Another option is to bunch the beam with a different frequency RF system for studies to get BPM measurements, and then turn the RF off for normal operations.
Dave Peterson will in parallel look at the possibility of using the Accumulator preamps and Sten boards for g-2 operations.

## Slide 6: To do list
Update Mu2e BoE costing documentation need for upcoming Mu2e review. Peter will generate new BoEs by Monday.