## Slide 1: Cryogenic Instrumentation – DUNE Perspective
Carl Grace 05/19/2022 HEP-IC 2022
Lawrence Berkeley National Laboratory

## Slide 2: The DUNE Experiment
The Deep Underground Neutrino Experiment (DUNE) is an international science collaboration focused on neutrinos
Key Purpose:
Enable the search for CP Violation
Help us understand the matter/antimatter
imbalance of the universe.
LBNL is leading the development of the Near Detector (ND) and has an important role in the cold electronics for both the ND and Far Detector (FD).
Neutrinos have a mean-free-path of 60 light years in water so extremely intense beam and dense detector material (Liquid Argon) needed
Illustration courtesy LBNF

## Slide 3: DUNE Far Detector
Fiducial volume of each detector is 10 kTon (17.5 kTon total mass)
Liquid Argon (LAr) is detection medium
TPC size: 12.0 m x 14 m x 58.2 m
Single-Phase module
Bo Yu (BNL)
JINST 15/T08010

## Slide 4: DUNE Far Detector – Scaling & Low Noise
Immersing CMOS electronics in LAr greatly reduces the cabling capacitance, allowing lower achievable noise, and serves as an enabling technology for DUNE
Warm Electronics
Cold Electronics
JINST 15/T08008

## Slide 5: Key Electronics Challenge: Long-Term Reliability
Reliability and biasing drift
“Hot” carriers cause early device aging
E. Afacan Thesis, 2016
BNL and FNAL conducted lifetime studies and developed design guidelines to assure long-term reliability
UPenn and FNAL developed a cryogenic compatible standard cell library for 65nm CMOS

## Slide 6: The DUNE Far Detector Electronics
JINST 15/T08010
Charge collection system uses 3-chip solution
LArASIC – 16 channel preamp
Cold ADC – 16 channel ADC
COLDATA – data aggregator and high-speed digital communications
All chips are immersed in LAr and have a 30-year required lifetime
24000 LArASIC, 24000 ColdADC, and 6000 COLDATA ASICs are required to instrument a Far Detector Single-Phase Module

## Slide 7: DUNE Far Detector (LArASIC)
LArASIC requirements:
low noise : approximate ENC of 450 e- with 1 µs shaping
low power (to not boil LAr) : 5.5 mW per channel achieved
16 channels
Ability to instrument both induction and collection wires

## Slide 8: DUNE Far Detector (LArASIC)

## Slide 9: DUNE Far Detector (ColdADC)
Three-lab collaboration (LBNL, FNAL, and BNL) developed ColdADC to read out LArASIC in the DUNE Far Detector
Functional Block Diagram
65 nm CMOS
IEEE TNS 2022

## Slide 10: DUNE Far Detector (ColdADC)
The DUNE Far Detector ColdADC will operate for 30 years sealed in a cryostat and was designed using design techniques for reliability and custom simulation models. Interoperated successfully in recent run of ProtoDUNE.
Superior Noise Performance at Cold Temperature (well below preamp noise)
Excellent dynamic performance
(73.34 dB SNDR)
Measured Performance
Achieved better noise performance than commercial solution used in Short Baseline Neutrino Detector (SBND) Experiment
IEEE Trans. Nuclear Science 2022

## Slide 11: DUNE Far Detector (COLDATA)
Data Formatter
High-Speed Serializer
Cable driver (to warm Front-End Motherboard)
PLL to generate all system clocks
Programmer for LArASIC and ColdADC (via serial interface)
COLDATA tasks

## Slide 12: DUNE Far Detector (COLDATA)
Measured Performance
IEEE Trans. Nuclear Science 2019
65 nm CMOS
RT
LN2 Temp

## Slide 13: DUNE Near Detector
Conventional Facilities
Liquid Argon detector
Installation
Power distribution and DAQ
Cryogenics
Energy chain and traveling systems
Beam line monitor
LBNL developing readout electronics
For LAr detector

## Slide 14: Key Near Detector technical challenge
The DUNE ND will experience ~10M neutrino events per year. Below is a simulation of neutrino pileup in the ND from a single beam pulse (each color indicates a separate neutrino interaction) not including neutrino background.
Approximately 50 neutrino interactions per beam spill

## Slide 15: Key Near Detector technical challenge
The much larger Far Detector (FD) uses a conventional wire-based liquid Argon (LAr) Time Projection Chamber. Electrons generated by neutrino collisions are drifted in an electric field to wire planes in the cold volume.
When tracks/showers are parallel to anode plane, all signals are simultaneous. This leads to ambiguity which could be a showstopper with the high event rate in the DUNE ND.
Solution: True 3D readout with a pixelated detector immersed in LAr for the DUNE Near Detector.
3 GeV electron neutrino charge-current interaction in LAr.

## Slide 16: LArPix – Liquid Argon Pixel ASIC
Approach: Integrating Amplifier with Self-triggered Digitization and Readout
Front-end amplifier
Self-triggering Discriminator
Standard SAR Digitizer
Digital Control
Achieve low power: avoid digitization and readout of mostly quiescent data.
64 channels per ASIC
  Charge Sensitive Amplifier
  Discriminator (self trigger)
  ADC (per channel)
  Digital Control logic
Global control logic
2k FIFO
On chip references and bias currents
Only decoupling capacitors needed
Immersed in Liquid Argon (-200° C)

## Slide 17: Quick Design Iteration  Continuous Improvement
5.28 mm
6.25 mm
5.0 mm
5.0 mm
LArPix-v1
LArPix-v2
32 channels, 33 mm2
64 channels, 25 mm2

## Slide 18: LArPix Pixel Tile
Tile with 100 LArPix-v2 ASICs (6400 channels)
Closeup of tile
Prototype tiles have 100 LArPix ASICs
(30 cm by 30 cm)
ND Tiles will scale to 160 ASICs/tile

## Slide 19
Demonstrate system scalability in large LArTPC: ArgonCube 2x2 Demonstrator
System successfully operated.
Demonstrator for DUNE Near Detector
4 modular LArTPCs
Total active mass: ~3 ton
Readout area: 6.4 m2
400k pixels, 6.3k ASICs

## Slide 20
Demonstrate system scalability in large LArTPC: ArgonCube 2x2 Demonstrator
Raw data (no filtering) of cosmics in ArgonCube module0 demonstrator.
Pixelated detector delivers unprecedented track fidelity and would be impossible to implement without custom ASICs
The final DUNE Near Detector will require approximately 350k ASICs to instrument a 100m2 pixel plane (22.4 Mpix)

## Slide 21: Thank You
This work was supported in part by the U.S. Department of Energy under Contract No. DE-AC02-05CH11231