## Slide 1
Workshop on Muon Driven Colliders
26th and 27th January 2022
Neutrino Radiation Assessment and Mitigation
C. Ahdida, C. Carli, N. Guilhaudin, G. Lacerda, A. Lechner, G. Lerner, Y. Robert, D. Schulte, K. Skoufaris

## Slide 2: Outline
Recap of the Neutrino Radiation Issue
Analytical Approximation of Radiation from Neutrinos
Overview of workflow related to a refined dose model
FLUKA MC Studies
Geoprofiler
Summary and Outlook

## Slide 3: Recap of the Neutrino Radiation Issue
Radiation due to showers generated by neutrinos reaching the earth surface
  Matter in front (“shielding”) does not help but makes situation even worse
  Narrow radiation “cone” for a short piece of the machine with length
Strong increase with muon energy
  Cross sections about proportional to energy
  Typical energy per interaction of neutrino with matter proportional to muon energy
  Opening of radiation inversely proportional to muon energy
3
Collider ring
Radiation cone

## Slide 4: Analytical Approximation of Radiation from Neutrinos
Analytical estimate base on approach by B. King
  Neutrino energies from production in muon rest system and Lorentz boost
  Cross section assumed proportional to energy
  Identical (almost) similar results for m- and m+ and despite different cross sections …
  Absorbed dose per muon decay at distance Ls and offset d with g the relativistic Lorentz factor)
  Conversion absorbed dose to effective dose 1 Sv/Gy optimistic!
Absorbed dose per muon decay for
10 TeV com energy at Ls = 100 km

## Slide 5: Analytical Approximation of Radiation from Neutrinos
Dose due to neutrinos for realistic lattice with divergence from beam
  Needs integration over longitudinal position
  Rms opening angle of cone becomes and
  With the repetition rate times the number of muons per cycle and the circumference
  Additional widening of cone due to time dependent orbit or machine deformations to be added later

## Slide 6: Analytical Approximation of Radiation from Neutrinos Dose from arc cell for 3 TeV com MAP lattice
X-pole with 2 T dipolar
0.30 m drift with small divergence
0.30 m drift with some divergence
Beam intensity to be checked
5000 h operation

## Slide 7: Analytical Approximation of Radiation from Neutrinos Dose from region around IP for 3 TeV com MAP lattice

## Slide 8: Overview of workflow related to a refined dose model
Operational scenarios
Dose assessment
MC simulations
Folding with realistic source term
Dose surface map
Sensitivity analysis
Demonstration of compliance
Optimization process
Slide by C. Ahdida

## Slide 9: FLUKA MC Studies
Motivation
  Get an improved model for the dose distribution generated by neutrinos
  Verify and improve analytical expression given before
  Effective dose instead of absorbed dose
  Quantify widening of neutrino radiation cone due to transverse extension of shower
Procedure
  Start with mono-energetic muon beam without divergence
  Generation of neutrinos from muon decay
  Obtain effective dose distribution (per decayed muon) at different distances from muon decay
  Fit with simple expressions – Gaussians good enough?

## Slide 10: FLUKA MC Studies
Very first results
  Plot shows absorbed dose for direct comparison
  At a first glance good agreement with analytical estimate
Effective dose distributions for m- and m+ at different distances expected very soon
Work by G. Lerner

## Slide 11: Geoprofiler – Radiological Analysis
Goal: Geolocate and display neutrino radiation affected areas for a given accelerator scenario.
  Interactively as it is edited and positioned, requiring good performance.
Issue: Large study area and complex calculations in geolocation and radiation dose estimation.
Problem needs to be simplified and the solution approximated as best as possible!
Initial Approach: Focus on tracking and geolocating a few directions of most intense radiation (sections surrounding interaction points) with simple line models.
  Flexibly allow analysts to select other interesting study points
Iterative improvements:
    Display general radiation data sourced from refined dose model.
    More encompassing and realistic radiation spread model.
    Characterization of land and dose impact at “hotspots”.
* Unrealistic positioning, for illustrative purposes only!
Slides by G. Lacerda

## Slide 12: Geoprofiler – Radiological Analysis
Geoprofiler Application – currently focused on geological analysis, allows the user to edit and reposition the ring with immediate recalculation of the geology along the tunnel.
Radiological Analysis Goal: Quick exploration and identification of locations of good potential concerning land jurisdiction / rights, urbanization, minimal radiation impact, etc.
For this it will feature:
  Enlarged study area
  Multiple tunnels per configuration / scenario
  Radiation dose impact estimate charts
  Information about impacted areas (rights, urbanization …)
* Prototype, for illustrative purposes only!
* Unrealistic positioning, for illustrative purposes only!
Slides by G. Lacerda

## Slide 13: Geoprofiler – Radiation Geolocation Workflow
In the input:
Each survey command output section defines a tunnel of the scenario.
Markers identify interaction points and other points of radiological interest.
Additional metadata identifies initial coordinate system, position and orientation.
More information, such as descriptive tags, functional sections and surface access points, can be encoded in similar fashion.
Slides by G. Lacerda

## Slide 14: Geoprofiler – Radiation Geolocation Workflow
Adding Dose Information
An independent dose model tool allows for separation of concerns.
Implies transforming back and forth between coordinate systems.
Slides by G. Lacerda

## Slide 15: Summary and Outlook
Radiation due to showers generated by neutrinos reaching the earth surface a serious issue
  Doses increase strongly with muon energy!
Procedure to assess dose due to neutrinos being set up
  FLUKA simulations for realistic radiation cone without divergence from beam
  Folding of lattice properties (geometry, divergence, orbit deformations …) with neutrino radiation cone
  Tool to geo-localize areas with (high) effective doses
Optimizations to reach acceptable maximum doses once 10 TeV lattice available
  Lattice (attention to straight sections, divergence from dispersion in arc …)
  Positioning of machine (hot spots only in suitable locations)
  Spreading of radiation over larger area by time varying orbit deformations and/or deformation of whole machine