## Slide 1: Evolution of Proton Capabilities: Fermilab and Elsewhere
Steve Holmes
Short Baseline Neutrino Workshop
March 21, 2012

## Slide 2: Outline
Fermilab
  Proton Improvement Plan
  Project X
Elsewhere
  J-PARC
  CERN
  PSI
Notes: Test
2

## Slide 3: Fermilab Capabilities Today
The Fermilab Proton Source (Linac + Booster) can currently deliver about 41 kW at 8 GeV
  4.3E12 protons per pulse × 8 GeV × 7.5 Hz
This power is currently deployed as follows:
  28 kW to the Main Injector for acceleration to 120 GeV and delivery to the NuMI target  390 kW at 120 GeV
  14 kW to the Booster Neutrino Beam program (MiniBoone) at 8 GeV
Inherent limitations in the current performance are:
  The Main Injector is operating with a 2.2 second cycle time, primarily due to 0.67 fill time at 8 GeV
  Booster could in principle run at 15 Hz, but is only delivering beam at 7.5 Hz
The former limitation is removed by NOvA

## Slide 4: NOvA Upgrades (2013)
The Main Injector cycle time will be reduced to 1.33 seconds:
  Utilization of the Recycler as a proton accumulator eliminates 0.67 seconds and allows accumulation of an extra (12th) Booster pulse
  Additional rf stations and upgrades to the quadrupole power supplies does the rest
Booster operates at 9 Hz (beam)
  There is no increase in Booster beam intensity per pulse
  NOvA beam power = 390 × (2.2/1.33) × (12/11) = 700 kW at 120 GeV
The inherent performance limitations will be:
  If the Booster is limited to 9 Hz there is no beam left for the 8 GeV program
This limitation is removed the Proton Improvement Plan

## Slide 5: Proton Improvement Plan (2016)
Goals
  Increase beam repetition rate to 15 Hz
  Retain current per pulse intensity  > 2E17 protons/hour
  Eliminate major reliability vulnerabilities and maintain reliability at present levels (>85%) at the full repetition rate
  Eliminate major obsolescence issues
  Ensure a useful operating life of the proton source through at least 2025
Scope
  Replace Cockcroft-Walton with RFQ
  Upgrade DTL High Power RF System
  Booster Solid State RF System
  New Booster RF cavities
  Booster Tuner System Upgrade
  Booster Collimation Upgrade
  Instrumentation/Controls Upgrades
  BRF Anode and Bias supplies & test stand
  Conventional Systems Upgrades
  Vacuum System Upgrades

## Slide 6: Proton Improvement Plan (2016-2021)
120 GeV
8 GeV

## Slide 7: Project X Reference Design
3 GeV CW superconducting H- linac; 1 mA average beam current.
3-8 GeV pulsed linac capable of delivering 300 kW at 8 GeV
Upgrades to the Recycler and Main Injector to provide ≥ 2 MW to the neutrino production target at 60-120 GeV.

## Slide 8: Project X Performance Goals
Linac
Particle Type H-
Beam Kinetic Energy 3.0 GeV
Average Beam Current 1 mA
Linac pulse rate CW
Beam Power 3000 kW
Beam Power to 3 GeV program 2870 kW
Pulsed Linac
Particle Type H-
Beam Kinetic Energy 8.0 GeV
Pulse rate 10 Hz
Pulse Width 4.3 msec
Cycles to MI 6
Particles per cycle to MI 2.61013
Beam Power to 8 GeV 190 kW
Main Injector/Recycler
Beam Kinetic Energy (maximum) 120 GeV
Cycle time 1.4 sec
Particles per cycle 1.61014
Beam Power at 120 GeV 2200 kW
simultaneous

## Slide 9: Project X Staging
Staging opportunities are under discussion with DOE
  Goals
    <$1B/stage
    Significant physics program at each stage
    Full Reference Design ultimately realized
Stage 1
  1 GeV CW linac injecting into existing (upgraded) Booster
Stage 2
  Add 1-3 GeV CW linac
Stage 3
  Add 3-8 GeV pulsed linac injecting into (upgraded) Recycler/MI
Stage 4
  Upgrade power to 4 MW at 8 GeV

## Slide 10: Power Profile for the Research Program
Program: | Stage-0: Proton Improvement Plan | Stage-1: 1 GeV CW Linac driving Booster & Muon Campus | Stage-2: Upgrade to 3 GeV CW Linac (MI>70 GeV) | Stage-3: Project X RDR (MI>60GeV) | Stage-4: Beyond RDR: 8 GeV power upgrade to 4MW
MI neutrinos | 470-700 kW** | 515-1200 kW** | 1200 kW | 2300 kW | 2300-4000 kW
8 GeV Neutrinos | 15 kW + 0-50 kW** | 0-40 kW* + 0-90 kW** | 0-40 kW* | 85 kW | 3000 kW
8 GeV Muon program e.g, (g-2), Mu2e-1 | 20 kW | 0-20 kW* | 0-20 kW* | 85 kW | 1000 kW
1-3 GeV Muon program | ----- | 80 kW | 1000 kW | 1000 kW | 1000 kW
Kaon Program | 0-30 kW** (<30% df from MI) | 0-75 kW** (<45% df from MI) | 1100 kW | 1100 kW | 1100 kW
Nuclear edm ISOL program | none | 300 kW | 300 kW | 300 kW | 300 kW
Ultra-cold neutron program | none | 300 kW | 300 kW | 300 kW | 300 kW
Nuclear technology applications | none | 300 kW | 300 kW | 300 kW | 300 kW
# Programs: | 4 | 8 | 8 | 8 | 8
Total* power (mean): | 660 kW | 2020 kW | 4210 kW | 5490 kW | 11300kW
* Operating point in range depends on MI energy for neutrinos.
** Operating point in range is depends on MI injector slow-spill duty factor (df) for kaon program.

## Slide 11: Elsewhere
M Seidel, PSI
Project-X

## Slide 12: The High Duty Factor Proton Source Landscape This Decade...
x Duty Factor
*
*
*
PSI
TRIUMF
power
Stopped/Slow kaon yield/Watt
* Beam power x Duty Factor
Project-X CW-Linac

## Slide 13: J-PARC Current Plan
J-PARC Power Projection [MW]
2008 2009 2010 2011 2012 2013 2014
3 GeV (RCS)
pre-earthquake plan
30 GeV (MR)
pre-earthquake plan
200 kW
Earthquake
Stop
FY
145 kW
Earthquake
RCS Power
MR Power
Normal
Summer
400MeV
RFQ,
IonS.
Construction of 400 MeV Linac
New Funding for 3 years
for Linac and 3 GeV

## Slide 14: Summary
Fermilab has a plan of continuous improvement to proton performance
  Today → NOvA → PIP → Project X
  400 kW → 11000 kW
This program will support a world leading Intensity Frontier program encompassing:
  Long and short baseline neutrinos
  Rare processes based on muons, kaons, and nuclear edms
  Nuclear energy applications
This program will provide a platform for eventual construction of a muon based facility(ies)
  Neutrino Factory (Intensity Frontier)
  Muon Collider (Energy Frontier)
Project X is the centerpiece of the program
  >5 MW beam power available in Reference Design; upgradable to >9 MW
  CW linac is unique for this application, and offers capabilities that will be hard/impossible to duplicate in a synchrotron
But the competition doesn’t rest
So we need to keep moving!

## Slide 15: Backup

## Slide 16: Project X Operating Scenario 1-3 GeV Program
1 msec period at 3 GeV
Muon pulses (12e7) 162.5 MHz, 80 nsec 700 kW
Kaon pulses (12e7) 27 MHz 1540 kW
Nuclear pulses (12e7) 13.5 MHz 770 kW
Separation scheme
Ion source and RFQ operate at 4.4 mA
77% of bunches are chopped @ 2.1 MeV  maintain 1 mA over 1 msec
Transverse rf splitter
1 msec

## Slide 17: Siting

## Slide 18: CERN Proton Upgrades
Most recent info I have is from early late 2009
Plan appeared to go on hold following Chamonix 2010
  Except Linac4 which is under construction
New European strategy under development that could bring (some of this) back to life
PSB
SPS
SPS+
Linac4
(LP)SPL
PS
LHC /
SLHC
DLHC
Output energy
160 MeV
1.4 GeV
4 GeV
26 GeV
50 GeV
450 GeV
1 TeV
7 TeV
~ 14 TeV
Linac2
50 MeV
Proton flux / Beam power
PS2

## Slide 19: Beam Configurations Low Energy Neutrinos
Accumulator Ring Concepts
  Issues
    Injection
    Extraction

## Slide 20: Reference Design Capabilities
3 GeV CW superconducting H- linac with 1 mA average beam current.
  Flexible provision for variable beam structures to multiple users
    CW at time scales >1 msec, 10% DF at <1 msec
  Supports rare processes programs at 3 GeV
  Provision for 1 GeV extraction for nuclear energy program
3-8 GeV pulsed linac capable of delivering 300 kW at 8 GeV
  Supports the neutrino program
  Establishes a path toward a muon based facility
Upgrades to the Recycler and Main Injector to provide ≥ 2 MW to the neutrino production target at 60-120 GeV.
Utilization of a CW linac creates a facility that is unique in the world, with performance that cannot be matched in a synchrotron-based facility.
Notes: ADS Development with Nuclear Energy Applications

## Slide 21: R&D Program
The primary elements of the R&D program include:
  Development of a wide-band chopper
    Capable of removing bunches in arbitrary patterns at a 162.5 MHz bunch rate
  Development of an H- injection system
    Require between 4.4 – 26 msec injection period, depending on pulsed linac operating scenario
  Superconducting rf development
    Includes six different cavity types at three different frequencies
    Emphasis is on Q0, rather than high gradient
      Typically 1.5E10, 15 MV/m (CW)
      1.0E10, 25 MV/m (pulsed)
    Includes appropriate rf sources
    Includes development of partners
Goal is to complete R&D phase by 2015

## Slide 22: SRF Linac Technology Map
Section | Freq | Energy (MeV) | Cav/mag/CM | Type
HWR (G=0.1) | 162.5 | 2.1-10 | 9/6/1 | HWR, solenoid
SSR1 (G=0.22) | 325 | 10-42 | 16/18/ 2 | SSR, solenoid
SSR2 (G=0.47) | 325 | 42-160 | 36/20/4 | SSR, solenoid
LB 650 (G=0.61) | 650 | 160-460 | 42 /14/7 | 5-cell elliptical, doublet
HB 650 (G=0.9) | 650 | 460-3000 | 152/19/19 | 5-cell elliptical, doublet
ILC 1.3 (G=1.0) | 1300 | 3000-8000 | 224 /28 /28 | 9-cell elliptical, quad
b=0.11
b=0.22
b=0.4
b=0.61
b=0.9
325 MHz
10-160 MeV
b=1.0
1.3 GHz
3-8 GeV
650 MHz
0.16-3 GeV
CW
Pulsed
162.5 MHz
2.1-10 MeV
Notes: I would suggest that you point out that Indian DAE labratories are already working on SSR1, 650 and ILC cavities.

## Slide 23: Joint PX/NF/MC Strategy
Project X shares many features with the proton driver required for a Neutrino Factory or Muon Collider
  NF and MC require ~4 MW @
  10 5 GeV
  Primary issues are related to
  beam “format”
    NF wants proton beam on
    target consolidated in a few
    bunches; Muon Collider requires
    single bunch
  Project X linac is not capable of
  delivering this format
It is inevitable that a new ring(s) will be required to produce the correct beam format for targeting.

## Slide 24: Accelerator Requirements: Rare Processes
 | Proton Energy (kinetic) | Beam Power | Beam Timing
Rare Muon decays | 2-3 GeV | >500 kW | 1 kHz – 160 MHz
(g-2) measurement | 8 GeV | 20-50 kW | 30- 100 Hz.
Rare Kaon decays | 2.6 – 4 GeV | >500 kW | 20 – 160 MHz. (<50 psec pings)
Precision K0 studies | 2.6 – 3 GeV | > 100 mA (internal target) | 20 – 160 MHz. (<50 psec pings)
Neutron and exotic nuclei EDMs | 1.5-2.5 GeV | >500 kW | > 100 Hz