## Slide 1: AtomECS
Dr. Elliot Bentine

## Slide 2: AtomECS
Started as MOT simulation code but now has many features.
Magnetic fields, analytic or precalculated over grid.
Scattering forces on atoms in near-resonant optical fields.
  Multi-beam rate equation approach.
  Respects Doppler limit, to some extent recoil limit.
  More detail given in paper.
Magnetic and dipole-force traps.
S-wave collisions between particles.
Written in rust using Entity Component System (ECS) pattern.
Data-oriented architecture gives great parallel performance.
Unit tests, integration tests and continuous integration
  Automated testing of each module in the program, and all modules together. Currently 37 different tests.
  Make changes without fear of breaking functionality!
Above: Simulations of Doppler limit in AtomECS for a 3D MOT. Inset: Good agreement between theoretical limit over a range of beam detunings.
Developers now also include:
Cambridge: Xintong Su, Kimberly Tkalcec, Brian Bostwick
Oxford: Abigail Coughlan, David Garrick
Software suite for simulating cold atom experiments.

## Slide 3: Entity-Component-System (ECS) pattern
Position
Entity 1
Velocity
Position
Entity 2
Velocity
Position
Entity 3
Velocity
Components describe the entities.
Each thing is an entity.
Position
Entity 4
BField
Systems implement program functionality by operating on collections of entities and components
The ECS bit of AtomECS

## Slide 4: Advantages of ECS
Position
Entity 1
Velocity
‘Atom’
Position
Entity 1
Intensity
‘laser beam’
1. Produces a flat, contiguous program memory structure – really fast for getting memory into processor.
Position
Position
Position
Position
Position
Position
…
…
Velocity
Velocity
Velocity
Velocity
Velocity
Velocity
…
…
2. Easy parallelisation! Systems are explicit about the components they read and write, and so solving dependency is easy.
Position
Velocity
UpdatePositionSystem
Write Access:
Read Access:
3. Behaviour by composition avoids the behaviour by inheritance antipattern. Flexible program structure.
4. Small systems implement very specific features – easy to test!
Versus ‘heap’ in managed-memory applications
DopplerShift
Velocity
CalculateDopplerShiftSystem
Write Access:
Read Access:
Trivial to run simultaneously!
Direction
Detuning
Mass

## Slide 5: Example systems
Systems used in the magnetics module, which calculate the magnetic field at each atom’s location.

## Slide 6: AtomECS performance
(a) shows the wall time per step per atom for a MOT simulation.
  For >1000 atoms the parallel execution becomes effective.
(b) shows fit to Amdahl’s law for 106 atoms. Gives ~85% of program parallelised.
Benchmarks:
  AION 2D MOT, capture from an oven: 106 atoms initially ejected, 15ms of motion, 200 atoms captured. 4s to simulate.
  Evap,magnetic trap: 5x103 pseudo-particles simulated, s-wave collisions, 2s of motion. Takes 2.5s to simulate.
Right: Load balancing of AtomECS over multiple CPU cores

## Slide 7: Development cycle
Written in rust (‘c-like’)
Repository hosted on GitHub
  Open source, GPL-3.0
Development milestones listed
Issue-driven development
  Developer raises a pull request to fix an issue.
  Community review, comments & discussion
  Continuous integration/unit tests run
  PR merged back into the codebase
Updates published to the rust ‘crates’ repository.

## Slide 8: AtomECS & AION
Current sidearm simulations:
  Chamber 1: Capture and cooling of fast atoms from oven into 2D MOT.
  Chamber 2: Capture and cooling of atoms from the 2D MOT source.
Upcoming simulations @ Ox:
  Chamber 1: Van der Waals collisions with thermal atoms required for oven scaling
Oven
2D-MOT
Blue MOT
Red MOT
ODT loading
Evap
Trans-port
Final cooling
Cloud splitting
Launch
AI seq
Imaging
AtomECS I:
Optical scattering forces
Atom sources
Performance optimisations
https://arxiv.org/abs/2105.06447
AtomECS II:
Dipole traps
magnetic traps
s-wave collisions
Cooling transition Stark shift
Inelastic collisions
(Abi & Leonie)

## Slide 9: Transverse-loaded 2D MOT
Current AION sidearm source:
  Atoms exit from oven, collimated by nozzle.
  Large area, high-power beams exert laser cooling forces (
  Narrow, high-intensity push beam directs atomic flux towards the second chamber.
Flux improvement:
  Cooling beam radius: larger capture volume; longer stopping distance; angle
  Oven performance: collimation; higher flux; larger size
  Hybrid with Zeeman slower beam
    Nosske et al, PRA 96 (2017)
1
2
3
Sr 2D MOT source at Oxford

## Slide 10: Simulated 2D MOT properties
Visualisation of trajectories
No significant overshoot – atoms turn and are directed out of the aperture
Axial and transverse velocity distributions
Remember that only ‘captured’ atoms are counted
Shows distribution of atoms below 40m/s target velocity
Transverse velocity corresponds to about ~1mK temperature
Angular divergence
Initial velocities of captured atoms

## Slide 11: Chamber 2 MOT recapture
Constraints
Incoming_velocity = 50m/s 10m/s greater than target axial velocity of the source for contingency.
transverse_temperature = 1mK
cooling_beam_power = 5mW
cooling_beam_waist: 9.0955
cooling_beam_detuning: -56.1467
quadrupole_gradient: 40.9443
Capture fraction
50m/s
40m/s
60m/s
Incoming velocity

## Slide 12: Cold Atoms at Oxford
Abigail Coughlan
Dr. Thomas Hird
Dr. Elliot Bentine
Prof. Chris Foot
Team AION
Team BEC
Abel Beregi
David Garrick
Shinichi Sunami
Thank you for listening!
Dr. Kenneth Hughes

## Slide 13: Red cooling transition
https://github.com/TeamAtomECS/AtomECS/issues/7
arXiv:1706.04807v1
AtomECS

## Slide 14: Zeeman slower
Also considering a design based on a Zeeman slower combined with transverse cooling.
AOSense source: includes Zeeman slower, heated window, transverse cooling
1
2
3
4
Transverse Cooling
Oven
Zeeman slower
Current simulations show similar performance – but at lower required cooling power, and smaller size.
  May provide better scaling to higher fluxes.
5%
0.1%
= 7mm,
P = 120mW