## Slide 1
MAGIS-100 Phase Fitting
Mathematica based study
ND-doc-845

## Slide 2: Mathematica-based simulation described last week
Start with (Jeremiah: ND-doc-767)
analytically derived wavefunction  atom population in the imaging region at end of interferometer sequence
Simulation ingredients (SG: ND-doc-845)
photon emission rate & imaging time
Atom diffusion during imaging
optics: geom. acceptance & magnification
CCD pixel geometry & quantum efficiency
pixel readout noise: Gaussian fluctuations
Atom statistics: Poisson fluctuations
Photon emission statistics: Poisson fluctuations

## Slide 3: Fitting the Simulated Image to Extract a Phase
500
1000
1
1
200
400
pixel x-index
pixel z-index
photons/bin (x1000)
Asymmetry

## Slide 4: Some numbers to keep in mind
Statistical precision of each measurement depends upon the number of atoms in the cloud N and the average number of photons per atom imaged and recorded fg
We anticipate that initially MAGIS will operate with N ~ 106.
To estimate fg assume:
  the CCD camera lens accepts 0.4% of the solid angle
  Photon emission rate per atom is 108 / sec
  QE = 0.5
which yields fg = 2 for an imaging time t = 10ms .

## Slide 5: Setting expectations: Toy Model
Establish what to expect by simulating and fitting a simple model.
Consider a Gaussian envelope modulated by a cosine fringe pattern:
Set f = 0, center the atom cloud and chose a distance scale so that the pixel plane extends from x=0 to x=1.
With N=106, for a given l & s, fit for the phase f.
Repeat many times to extract the variation in the fitted f → phase resolution.
Example: l = 0.1 s = 0.1
x

## Slide 6: Toy Model Fit Results
Phase resolution (mr) for N = 106 tabulated as a function of the cosine wavelength l and the RMS of the Gaussian envelope s :
For 106 atoms we obtain a phase resolution of ~ 1mr which, if we had estimated analytically, is what we expect.

## Slide 7: Adding Readout Noise
where B is the integrated background and S = N x fg is the integrated signal
Analytically we expect the phase resolution

## Slide 8
FIND: (Eq. 8)

## Slide 9: Fitting the Simulated Images
500
1000
1
1
200
400
pixel x-index
pixel z-index
Fitting modules in the package offer a number of OPTIONS:
fit the entire pixel plane or restrict the fit to the image regions
fit a single interferometer or two interferometers as a gradiometer
fit two ports separately or together or the two-port asymmetry
weighted or unweighted fits
The toy-model (Gaussian + Cosine + Background) is used as the fit-function → provides an adequate description of the simulated images → good fits Parameters varied in the fit: f , B, S, cloud position(s) & width(s), l

## Slide 10: Fitting the Simulated Images
Analysis methods described in ND-doc-845
Method G weighted is the one where everything is nominally done optimally
All methods with weighted fits yield results consistent with our simple Gaussian + Cosine + Background expectations for that method

## Slide 11: Imaging Time
Can recast the previous Eq 8 to show dependence of the phase resolution on imaging time t. where tg is the imaging time corresponding to 1 photon/atom recorded and tB is the imaging time corresponding to S/B = 1 and

## Slide 12: Contrast
Stray paths not yet implemented in the simulations for the fitting study (Leonie – in progress) ... Hence we do not yet have a model for the image contrast.
Assume something unrealistically bad ... that the contrast loss is uniform over the image. Contrast factor fc:
Plan to repeat this study once we have at least a parametric model for the impact of stray paths on the position-dependent contrast.

## Slide 13: Two-Port Asymmetry
So far the fits have been to the 1D-fringe distributions. Can also fit the two-port asymmetries ... statistically equivalent.
Nothing in the simulations (so far) favors asymmetry fits over 1D-fringe fits although in the future we may discover the systematics associated with these alternative are different.

## Slide 14: A more complicated wavefunction
Add a quadratic term to the wavefunction (Jeremiah ND-doc-767) at the input of the simulation & also to the fitting function:
aQ = 10-12
aQ = 10-3
aQ = 10-1
aQ = 0
aQ = 10-4
aQ = 10-2

## Slide 15: A more complicated wavefunction: Asymmetry Fits
aQ = 10-12
aQ = 10-3
aQ = 10-1
aQ = 0
aQ = 10-4
aQ = 10-2

## Slide 16: A more complicated wavefunction: Fit Results
Phase resolution as a function of the dimensionless quadratic amplitude aQ
There is a penalty for using a more complicated fit function ... So don’t use it unless you have to [for aQ > O(10-4)].
Using a fit function w/o the aQ term seems to be the best strategy for aQ < O(10-4).

## Slide 17: FINAL REMARKS
Things will become more interesting as the simulations become more realistic
  optics, stray paths ...
I think we should plan to fit the acquired images in real time as a high-level monitor of data quality
  fit for phase, background level & contrast, cloud amplitude, center & width ...
  if we can’t fit every image, we can still sample (robust online fitting that monitors all relevant parameters may be more rewarding than fast fitting)