## Slide 1
Mtest experiment (activation)
Feb. 16, 2012
Activation group
Hiroshi Yashima

## Slide 2
To obtain experimental data(activation cross section, mass yield distribution)
for Ep>120 GeV)
Mtest Experiment(activation)
Trigger detector
120GeV
2e11 pps
3e5 particle per spill
NE213 neutron detector at several angles
TOF
MI
Activation samples in M01
Cu Target 60cm L

## Slide 3
  One M01 control access for setting up samples
  after beam time(18:00-)
  One beam operation ( 4:00- >4hours, 1.0e9 p/sec)
  depends on the schedule of radiation safety staff
  who bring samples to HIL for beam stop
  3. One M01 control access for pick up samples to HIL after irradiation
Before irradiation experiment,
beam spot check by using GAFCHROMIC Film
One M01 control access for setting up film
irradiation (1 hour, 1.0e9 p/sec)
One M01 control access for pick up film
Experimental procedure (2010Feb. Dec.)
irradiation experiment
1 sample per day ×5 samples (see next slide) = 5 days
In each day,
Activities induced in samples were measured by HPGe detector

## Slide 4
Beam spot check
GAFCHROMIC Film

## Slide 5
Sample position
Beam profile
sample
Scan

## Slide 6
monitor: Al 3cm× 3cm×0.01cm×3foils
sample: Cu 3cm× 3cm×0.02cm×3foils
monitor: Al 3cm× 3cm×0.01cm×3foils
sample: Co 3cm× 3cm×0.02cm×3foils
monitor: Al 3cm× 3cm×0.01cm×3foils
sample: Al 3cm× 3cm×0.05cm×3foils
monitor: Al 3cm× 3cm×0.01cm×3foils
sample: Ni 3cm× 3cm×0.02cm×3foils
monitor: Al 3cm× 3cm×0.01cm×3foils
sample: Au 3cm× 3cm×0.02cm×3foils
monitor: Al 2.5cm× 2.5cm×0.01cm×3foils
sample: Y 2.5cm× 2.5cm×0.01cm×3foils
1st experiment(Feb. 2010)

## Slide 7
proton flux by 27Al(p,3pn)24Na reaction
For Ni, Al, Au, current(Al monitor) > current(SEM)
→For thick sample irradiation, there are some
influence of secondary particle?
proton flux were estimated by using cross section 8.04 mb
2nd experiment

## Slide 8
sample: Al 0.025mm ×3
sample: Cu 0.025mm ×3
sample: Au 0.2mm ×3
sample: Au 0.03mm ×3
sample: Ni 0.2mm ×3
To calibrate SEM
To check secodary
particles by using
thinner sample
Try again by using
thicker sample
To check secodary
particles by using
thinner sample
Try again by using
thicker sample
2nd experiment(Dec. 2010)

## Slide 9
proton flux were estimated by using cross section 8.04 mb
SEM calibration by 27Al(p,3pn)24Na reaction
result of Al monitor foil agree well with result of SEM.
natCu(p,x)24Na reaction
result of this work agree well with result of S.I.Baker et al.
proton flux determined by SEM were used for analysis

## Slide 10
Results
Product mass
small
large

## Slide 11
Cu
Co
Ni
Asano et al.,
Physical Review C 28,1718(1983)
Projectile:12GeV proton

## Slide 12
Summary
Activation cross section data for Cu, Ni, Co
by 120 GeV proton beam
・Measurement and analysis for long half-life products
・Activation cross section data for Au and Y
・Mass yield distribution, charge distribution
・Simulation(Nuclear reaction, secondary effect)
σ(Cu) ≒ σ(Co) ≠ σ(Ni)
Future works