## Slide 1: Muon Campus Report
Jim Morgan
February 11, 2022

## Slide 2: Weekly overview and current issues
Intentional Accelerator
Standby Period
Downstream D30 Crossover Pipe
g-2 cryo degrading
  Two cryo valve flushes in the past week
  Eventually will need several days down for purification
  Last purification was week of December 13
Generally good up time when g-2 could take beam
Thursday down day for maintenance
  In parallel with second g-2 cryo flush
  Priority was to reduce LCW loss rate, three magnets repaired
  Numerous other smaller jobs
Ongoing problems
  Bad D:IB transformer to power supply cable prevents 8 GeV operation
  CTAGs about 15% lower than previous runs (a bit better then last week)
Two tuning and measurement sessions
  Tuesday, M1 optics and spot size on target
  General tuning of the Muon beamlines and Delivery Ring

## Slide 3: Target SEM beam profiles
February 8, 2022
June 14, 2018
June 26, 2021
Target SEM wire spacing
0.125 mm inner wires
0.500 mm outer wires

## Slide 4: Beam to g-2 this week
Beam to AP-0 target
g-2 T0 Detector
Decay Positrons
Delivery Ring
Trolley Run
g-2 Cryo valve flush
g-2 kicker problem
g-2 access
Trolley Run
Trolley Run
g-2 Cryo valve flush
Trolley Run
Muon accesses
Trolley Run
Tuning
M1 studies

## Slide 5: g-2 Run 5 Protons on Target
Detectors shifted upstream

## Slide 6: g-2 Protons on Target
Detectors shifted upstream

## Slide 7: g-2 Performance this run
2.50 BNL

## Slide 8: g-2 Overall Performance
3.22 BNL
2.21 BNL
1.94 BNL
5.51 BNL
2.50 BNL

## Slide 9: Short term plan
Keep running beam to g-2
  No 8 GeV studies possible until D:IB is repaired
  Hope to align D:IB repair and other work with g-2 cryo purification
Continue investigating low CTAGs
  Investigate why spot is large and isn’t improving with normal tuning knobs
  Periodic tuning sessions and studies to identify problem areas
  When tuned up, presently getting around 430 CTAGs @ 1E12 POT (normal ~500)
  More protons on target always helps and is greatly appreciated