## Slide 1
Elizabeth Lee (emlee@lbl.gov)
Manufacturing Engineer
Lawrence Berkeley National Laboratory
LBNL Respooling Machine Procurement Review
February 17, 2022

## Slide 2: Overview
Background
Procurement Objectives
Target Specifications (Constraints)
Procurement Options
Front Runners
Additional Concerns
Conclusion and Future Work
Questions?

## Slide 3: Background: What’s a respooling machine?
What is a respooling machine?
  Respooling machines (respoolers) are used to subdivide bulk lots of wire into smaller unit lengths.
Where is the respooler located?
  LBNL Cabling Facility (B77A-103)
Who uses this respooler/facility?
  Cabling team technicians, but any project relying on cabling work at LBNL is a direct stakeholder
Which respooler does LBNL currently use?
  Meteor ME-301 linear solenoid winding machine (~1950’s era), with additional QC subsystems
Why is it important?
  Respooling machine is used to prepare all wire lengths used for LBNL cabling activities (Rutherford cabling, wire annealing spool prep., etc.)
  First step in most processes at LBNL cabling facility - initial QC for all wire
Charge: 2

## Slide 4: Background: Spool Types in use at LBNL
Photo credits: Hugh Higley

## Slide 5: Background: How does the ME-301 work?
Basic function
  Motor drives spindle (i.e., rotates spool) to take up wire
  Traversing pulley geared to motor – moves from side to side to level-wind, controlling the number of wire turns/layer
  Lengths recorded by attached footage counter assembly
    Not a stock feature – added by LBNL
Important Features
  Level winding
    Layers are wound flat
    No bunching of wire
  Automatic-traverse
    Transmission prevents technicians from having to watch wire, respool and move the traverse to level wind
Footage counter assembly
Al Spool mount
Traversing guide pulley
Charge: 1,2

## Slide 6: Background: Recent Issues and Impact
Main transmission broke down in November 2021 due to accelerated wear & tear from large project work
  Pre-LARP/AUP, average length respooled was ~60 km/yr
  During LARP/AUP, respooling rate increased to ~600 km/yr (10x increase)
Support availability extremely poor
  Meteor AG is a Swiss company – sole U.S. distributor provided poor support and had extremely long part lead times
  Machine assemblies poorly documented due to machine age
  Gear and mating worm drive had to be sent to a specialty machine shop in Milwaukee, WI for reverse-engineering and fabrication
Breakdown caused 2.5 month delay for cable production at LBNL; entire facility “dead in the water”
Brass worm gear had worn through original set of teeth (almost no engagement with worm drive)
Friction transfer roller worn down, poor contact/power transmission
Detail: worm gear damage from where mating worm had cut past gear’s original set of teeth
Charge: 2

## Slide 7: Procurement Objectives
System reliability
  Increase level of vendor support/maintenance
  Decrease maintenance frequency
  Define safe operating state/limits for machine to prevent early failure
Operational consistency
  Improve consistency of level winding operation (smoother layers)
  Enable faster respooling operation
  Improve wire tensioning consistency
System performance
  Respool a wider range of wire types/diameters
  Hold and wind larger take up spools (transfer/storage, annealing)
  Increase weight capacity of machine
Charge: 1,2,3

## Slide 8: Target Specifications
Electrical Input: 208 V three phase or 115/120 VAC preferred
Footprint: 72” x 35” max. area
Min. Take-up spool flange diameter: 12” (preferably up to 18”)
Weight capacity: 200 lbs
Max. Traverse: 20”
Features:
  Level-winding
  Automatic traverse
  Wire tensioning system
  On/off button operation
Charge: 2

## Slide 9: Vendor Preferences for New Machine
Warranty for any device purchased
Existing and active parts department
Existing and active service department
Willing to provide mounting footprint and center of gravity (CG) information at time of quote so that we can assess installation costs/feasibility
Note that LBNL is subject to the Buy American Act for purchases beyond a certain threshold
Charge: 3

## Slide 10: Vendor Survey
Tried to identify as many manufacturers of linear solenoid winding machines as possible
  Limited total number of potential suppliers substantially; winding machines of this type are not common
  Primarily tried to find manufacturers online
  One manufacturer (Broomfield) was referred to our attention because another team had LBNL had visited a local winding factory with many Broomfield machines
  One manufacturer (Gorman) provided a list of other legacy U.S. manufacturers as part of their “History” page
    Attempted to contact manufacturers on this list, if still in business
Only got responses after request for quote (RFQ) from four companies – these are the manufacturers of the options presented here
Charge: 3

## Slide 11: Option 1
Broomfield 200 Series Winder
Charge: 1, 2

## Slide 12: Option 2
George Stevens GS-F100CXLB
Charge: 1, 2

## Slide 13: Option 3
Gorman HDH Winder
Charge: 1, 2

## Slide 14: Option 4
Meteor M22-400
Charge: 1, 2

## Slide 15: Options Summary
Manufacturer | Model | Options | Max. Travel | Max. Diameter of Take-up Spool | Min. Wire Diameter | Max. Wire Diameter | Device Weight | Footprint (L x W x H) | Elec. Requirement | Lead Time | Warranty
Broomfield | 200 Series | DT-124 Dereeling + tensioning stand, auto-run spindle control, 3 free days of training at Broomfield site | 32" | 20" | No limit given | No limit given | 1600 lbs | 72" x 35" x 56" | 208 V, three phase | 5-6 months | Not listed
Gorman | HDH | Bar extension for automatic traverse | 39" | 12" | No limit given | 5.189 mm | 200 lbs | 44" x 24" x 24" | 115 VAC | Not listed | Not listed
Meteor | M22-400 | Mechanical tensioner, dual roller wire guide, 2 days set up and training | 15.7" | 7.87" | 0.01 mm | 2 mm | 120 kg | 71" x 20" x 20" | 220 VAC, 10 A | Not given until receipt of order, per quote description | 1 year or 2000 hours
George Stevens | GS-F100CXLB | Custom | 20" | 20" | 1.29 mm | 3.66 mm | Not given | Not given | 208 V, three phase | 3.5-4 months | Not listed
Charge: 2, 3

## Slide 16: Ranking by Feature
Arbitrary scoring system: use international track and field meet scoring to see which device gets the most “points”
  1st through 4th place: 5, 3, 2, and 1 points for each parameter, respectively
First place criteria
  Largest maximum take-up spool diameter
  Smallest minimum wire diameter
  Lowest weight
  Smallest footprint
  Minimal electrical work (existing access: 208 VAC three phase, 115/120 VAC)
Charge: 3, 4

## Slide 17: Ranking by Feature: Results
In arbitrary scoring system, Gorman and Broomfield score the highest – can eliminate Meteor and George Stevens, which we do not believe will have adequate performance
 | 1st | 2nd | 3rd | 4th
Maximum Travel | Gorman | Broomfield | George Stevens | Meteor
Max. Diameter of Take-up Spool | Broomfield / George Stevens | Gorman | Meteor | 
Min. Wire Diameter | Broomfield / Gorman | Meteor | George Stevens | 
Max. Wire Diameter | Broomfield | Gorman | George Stevens | Meteor
Device Weight | Meteor | Gorman | Broomfield | George Stevens
Approximate Footprint (L x W x H) | Gorman | Meteor | Broomfield | George Stevens
Elec. Requirement | Broomfield | George Stevens | Gorman | Meteor
Broomfield | Gorman | Meteor | George Stevens
29 | 31 | 17 | 18
Charge: 3, 4

## Slide 18: Broomfield 200 vs. Gorman HDH
Broomfield 200
(72” x 36” x 55”)
Gorman HDH
(44” x 24” x 16”)
Charge: 3, 4

## Slide 19: Broomfield 200 vs. Gorman HDH
What makes the Broomfield 200 different from the Gorman HDH? It is 4X more expensive than the HDH – why?
  Additional features
    Auto Run spindle control
    Programmable controller
    3 days of free training for up to three people to ensure the transition goes smoothly and machine works for our application
    Wire payoff stand with pneumatic braking
  General performance increases
    2 hp motor with variable speed drive vs 1 hp DC motor
    20” max. coil diameter (vs 14” on Gorman)
    250 lb coil weight capacity
  Gorman HDH is a reasonable direct replacement for the ME-301, but the Broomfield machine would help “future-proof” the cabling facility
Charge: 4, 5

## Slide 20: Additional Considerations
Broomfield is a larger supplier – they sell to coil manufacturers and solenoid winding facilities/subsidiaries
  Have time/energy invested into services and parts departments because their core customers need industrial reliability
  Customers include Eaton, GE, Philips Medical, Schneider Electrical, and Siemens, among others
Gorman was the most responsive vendor in initial communications, but it is a very small company
  Family owned business
  If firm were to go out of business, LBNL would be back at square one (unsupported machine)
Operator preference
  LBNL head cabling technician has assessed these options and indicated his preference for the Broomfield 200 due to perceived build quality and reliability
Charge: 4, 5

## Slide 21: Team Preference: Broomfield 200
System reliability
  Vendor should be capable of providing prompt technical support
  Operational limits and maintenance recommendations for new machine are both well-defined and documented
Operational consistency
  Supplier included de-reeling stand should help stabilize feed spool and improve respooling speed/consistency
System performance
  System will be able to respool a wider range of wire types/diameters
  System can hold larger/heavier take up spools than the current respooler
Charge: 4, 5

## Slide 22: Conclusion
The LBNL cabling team wants to replace the current respooler to ensure operational continuity and adequate support for ongoing scientific projects
The LBNL cabling team would like to improve facility respooling capabilities to support a wider variety of wire and cable types
The Broomfield 200 machine is very strong candidate for a “future-proofing” LBNL’s respooling capabilities
If wire cannot be prepared for Rutherford cabling, cables cannot be produced – the LBNL cabling team hopes that the facility respooler can become an enabling technology, and not a limiting one
Charge: 4, 5