## Slide 1
Silvia Peiro
Supervisors: Jinhao Ruan and Auralee Edelen
SIST/GEM 5 Mins/5 Slides
6/12/2022
Resonance Control at FAST using NNs

## Slide 2: Background
System used to regulate the resonant frequency of the electron gun at the Fermilab Accelerator Science and Technology
How does it work?
Controllable variables:
  Flow control valve setting (FVC)
  Heater power setting (HP)
Figure 1: Water System with Indicated Controllable Variables
A NN consists of a collection of functions with weighted connections between them.

## Slide 3: Why should we apply NN-based control methods?
Large thermal and transport time constants produce long variable time delays
Figure 2: Large time constants locations

## Slide 4: Why should we apply NN-based control methods?
Large thermal and transport time constants produce long variable time delays
Recursive behavior in the cooling system
Figure 4: Recursive Behavior
Figure 3: Oscillatory loop in response of recursive behavior

## Slide 5: Why should we apply NN-based control methods?
Large thermal and transport time constants produce long variable time delays
Recursive behavior in the cooling system
Fluctuations in the low conductivity water (LCW) supply temperature
+-0.5ºC

## Slide 6: Why should we apply NN-based control methods?
Large thermal and transport time constants produce long variable time delays
Recursive behavior in the cooling system
Fluctuations in the low conductivity water (LCW) supply temperature
Changes between TIN and T02 without a registered change in the ambient temperature
Figure 5: T02 and TIN indicated in water system

## Slide 7: Why should we apply NN-based control methods?
Large thermal and transport time constants produce long variable time delays
Recursive behavior in the cooling system
Fluctuations in the low conductivity water (LCW) supply temperature
Changes between TIN and T02 without a registered change in the ambient temperature
Temperature recorded at TCAV will be higher than the real bulk cavity temperature under RF power
Figure 6: RF and TCAV indicated in water system

## Slide 8: Goals
  Accurately identify the transport delays
Figure 7: Large time constants locations

## Slide 9: Goals
  Accurately identify the transport delays
  Quantify the combined effects of TOUT, T01, FCV setting, and HP setting on T02 (and subsequently on TIN and TCAV)
Figure 8: Water system with indication of temperature readings affected (red) by temperature and HP values (blue)

## Slide 10: Goals
  Accurately identify the transport delays
  Quantify the combined effects of TOUT, T01, FCV setting, and HP setting on T02 (and subsequently on TIN and TCAV)
  Quantify the combined effects of TIN and RF power on TCAV. Also, a model that uses T02 instead of TIN
Figure 9: Water system with indication of temperature readings affected (red) by temperature and RF values (blue)

## Slide 11: Goals
  Accurately identify the transport delays
  Quantify the combined effects of TOUT, T01, FCV setting, and HP setting on T02 (and subsequently on TIN and TCAV)
  Quantify the combined effects of TIN and RF power on TCAV
  Quantify the impact of ambient temperature on the temperature differences seen within the water system and the cavity
Figure 10: Water system with major areas affected by ambient temperature

## Slide 12: Process
Gather Data for the RF gun
Train a model on the new data through
  Supervised learning
  Auto differentiation
Put model into model predictive control loop to be tested offline
Run model on the gun

Figure 11: Water System

## Slide 13: References
Edelen, A. L., Biedron, S. G., Chase, B. E., Edstrom, D., Milton, S. V., & Stabile, P. (2016). Neural Networks for modeling and control of particle accelerators. IEEE Transactions on Nuclear Science, 63(2), 878–897. https://doi.org/10.1109/tns.2016.2543203