## Slide 1
Linac/FEL Physics Design and
Beam Dynamics Issues
P. Emma, for the NGLS team
March 15, 2012
FNAL Visit

## Slide 2
NGLS Accelerator Design
Need ~2.4 GeV e- linac at 1-MHz beam rate (CW, 0.3-1 mA)
Must generate & preserve e- brightness (cathode, gun, CSR, wakes, etc)
Two magnetic chicanes compress bunch in 2 stages (600 A)
RF phase and amplitude jitter tolerances are demanding (~0.01% & ~0.01 deg rms)
Switchyard distributes electrons to one of 3 FELs at 0.1-1 MHz each (baseline) – 10 FELs in long term
Many design issues similar to LCLS, but lower energy & MUCH higher beam rate (120 Hz  1 MHz)

## Slide 3
~13 MV/m gradient (increase to 16+ MV/m?)
26-30 ~12-m long cryo-modules (22-26 @ 16 MV/m)
7 RF cavities per module?
2 bunch compressors (2nd optional)
1 laser heater (damps micro-bunching instability)
3 identical spreader beamlines + straight-ahead dump
3.9
CM1
CM2
CM3
CM9
CM10
CM30
BC1
168 MeV
R56 = 75 mm
sd = 0.57%
BC2
640 MeV
R56 = 48 mm
sd = 0.57%
GUN
1 MeV
Heater
85 MeV
R56 = 4 mm
sd = 0.19%
L0
j = …
Ipk = 50 A
L1
j = -28º
Ipk = 50 A
Lh
j = 180º
L2
j = -31º
Ipk = 150 A
L3
j = +14º
Ipk = 600 A
SPRDR
2.4 GeV
R56 = 0
sd = 0.09%
670 m
to spreader end
Linac Layout “10/25/11”

## Slide 4
Linac Layout in MAD (Inj. to Spreader)
M. Venturini
Heater
BC1
BC2
Spreader
85 MeV
2.4 GeV
Tracking
(600 A)

## Slide 5: Start-to-End Simulations for NGLS…
Q  0.3 nC
Ipk  600 A
sz  0.03 m
sE  100 keV
Emittance growth (CSR)
Longitudinal Phase Space at 2.4 GeV
M. Venturini

## Slide 6
APEX Gun: High-Brightness MHz e- Source
APEX R&D project well underway at LBNL with full RF power and CW operation achieved - F. Sannibale, R. Wells
Notes: Repetition rate 1 MHz
Charge per bunch from ~10 pC to ~1 nC
Emittance <10-6 mm-mrad (normalized)
Electric field at the cathode ≥~10 MV/m (space charge emission limit)
Beam energy at the gun exit ≥~500 keV (space charge control)
Bunch length ~100 fs to ~10 ps for handling space charge effects, and for allowing different modes of operation
Compatible with magnetic field control within the gun (emittance exchange and compensation)
10-11 Torr vacuum capability (cathode lifetime)
Accommodates a variety of cathode materials

## Slide 7
Electrostatic
Septum (FNAL)
Magnetic
Septum
DC Bends
Electrostatic septum allows weak kicker (~0.04% rms stability tolerance)
Overall footprint reduced by optimization ~1/3
Kicker
(0.6 mrad,
was 3 mrad)
M. Placidi,
C. Sun,
W. Wan, et al.
Optimizing the Beam Spreader

## Slide 8
Three FEL Design Options
E (GeV) 2.4
ge (mm) 0.6
Ipk (A) 600
sE (keV) 100
FEL Photon Energy Tuning Range:
1.2 – 0.27 keV (+ 3rd & 5th harmonics)
Electron beam
Name | Gap (mm) | Und. Period (mm) | Mag. Und. Length (m) | Und. Type | Comment
102511DP | 7.5 | 29, 23 | 39+24 = 63 | HPM | “Conservative”
102511SC | 7.5 | 19 | 43 | Nb3Sn | Needs R&D
122011DPSC | 6.0 | 18, 13 | 35+20 = 55 | Nb3Sn | Enhances 6 keV
G. Penn, M. Reinsch

## Slide 9
Photon Flux over Wavelength Tuning Range for Two NGLS Designs
Perm. Mag. Und.
SC-Undulator
E = 2.4 GeV
gm = 7.5 mm
l = 19 mm
Lmag = 43 m
Photons/pulse
Photons energy (keV)
requirements
fundamental
3rd harm.
5 harm.

## Slide 10
0.5 eV
20 eV
Factor of 40 BW reduction
diamond OUT
diamond IN
Self-Seeding Demonstrated at LCLS
diamond
crystal