## Slide 1: Project X Energy Station Spallation Target
March 20, 2012
D. Wootan, D. Asner
david.wootan@pnnl.gov

## Slide 2: Versatile Project X Energy Station
Could support much needed testing of materials for DOE Office of Nuclear Energy programs to:
  Ensure the sustainability and safety of the current fleet of reactors for current lifetime extensions from 40 to 60 years, as well as future extensions from 60 to 80 years or more,
  Develop new higher performance and safer reactor fuels and materials,
  Enable the development of innovative economical small reactors,
  Enable the development of new advanced reactor concepts, such as those using liquid metal or molten salt coolants,
  Enable the development of transmutation fuels for reducing legacy wastes requiring deep geologic storage, and
  Enable the investigation of accelerator driven systems as a means for transmutation of waste from power reactors.
In addition, could support DOE Office of Science programs such as the
  Fusion Program
  Isotope Production Program
  Basic science research such as ultra cold neutrons, exotic isotopes, etc.

## Slide 3: Nuclear Energy: Experimental Station

## Slide 4: Key Features of Energy Station Concept
1MW Proton beam
Liquid metal spallation target
Closed Loop Modules for irradiation testing
protons
neutrons

## Slide 5: Characteristics of Energy Station Concept
1 MW CW proton beam on liquid lead or lead-bismuth spallation target produces copious neutrons with energy spectrum similar to fission spectrum but with high energy tail
  1 GeV 1 mA – 3 GeV 0.33 mA proton beam
Surrounded by vessel filled with liquid lead, lead-bismuth, or sodium that provides test region and maximizes test volume (360 degrees)
Azimuthally arrayed closed loop test modules provide independently tailored irradiation environment
  Varied Materials – coolant, moderator
  Independent cooling system for each test section, controlled temperatures, ceramic/vacuum insulation
  Modular test sections – each can be removed and the active section shipped offsite for processing
  Online cleanup of Pb-Bi spallation target could also be source of beneficial isotopes
Potential in-beam testing region

## Slide 6: Potential Flexible Test Matrix Capabilities
Test Zone | Characteristics
Materials | Miniaturized specimens, Instrumented, controlled temperature, pressure
ADS | Lead or lead-bismuth flowing loop, materials compatibility, corrosion, pin-type transmutation fuel and cladding tests, on-line cleanup
HTGR | Graphite structure, TRISO materials, pebble bed, compacts, He coolant
SFR | Sodium coolant loop, advanced high temperature long life materials, pin-type transmutation fuel and cladding tests
LWR | Pressurized water loop, LWR conditions, address sustainability issues
MSR | Molten salt loop, materials compatibility, corrosion, dissolved fuel
Fusion | Lithium loop, radiation damage in materials, fusion blanket tests
Other | Liquid He loop for cold neutrons, possible neutron beam extraction
Nuclear Data | Integral cross sections, isotopic burnup, fission product yields
Isotope Production | Spectrum tailoring for specific isotopes, rabbit system for rapid insertion, moderators: D2O, graphite, beryllium, metal hydride Beneficial use of leakage neutrons (238Pu, 60Co)

## Slide 7: Energy Research Station Concept
Chart: 
Chart: 
Proton beam
Proton beam
Neutron beams
lead
Liquid He for cold neutrons
Proton beam access
Axial cross section
Radial cross section
Cleanup system
Isotopes

## Slide 8: Characteristics of Energy Station
Flexible, able to support multiple missions
Robust technology allows it to be designed and constructed with today’s technology in order to fill gaps in tomorrow’s technology
Spallation neutrons energy distribution similar to fast reactor fission spectrum but with high energy tail up to proton energy
H and He generation in materials higher than in reactor allowing accelerated aging testing
Continuous wave, high availability, high beam current provides potential for irradiation tests to high fluence
Ability to tailor gamma to neutron flux ratio
Ability to tailor neutron spectrum from fast to thermal
Spallation reactions on target (lead or lead-bismuth) produce broad range of reaction products similar to fission products – some gaseous and mobile, so a gas and liquid cleanup system offers removal pathway and potential source of beneficial isotopes
Beneficial isotope production and/or cold neutron beams might be done simultaneous with irradiation testing

## Slide 9: Tailored Neutron Spectrum Possible in Each Module
Light Water Module
Graphite/He Module
Sodium Module
Lead Module

## Slide 10: Potential Test Volumes and Neutron Flux at 1 MW
Neutron Flux Range | Dimensions 5 cm (R1) | Available Test Volume
3e14-5e14 | 10 cm (R2) x 50 cm (H) | ~8 liter
1e14-3e14 | 40 cm (R2) x 90 cm (H) | ~270 liter
5e13-1e14 | 60 cm (R2) x 110 cm (H) | ~600 liter
1e13-5e13 | 100 cm (R2) x 180 cm (H) | ~2400 liter
3 m
1 m

## Slide 11: How can the Project X Energy Station Concept Benefit the Project X Physics Station Design?

## Slide 12: Program…
Material Science
  The high power proton beam from Fermilab Project-X would provide a test bed for structure and target material for accelerated radiation damage and liquid metal effects
  Neutron and gamma ray spectra and temperatures typical of a wide range of reactor concepts can be recreated for materials testing without building a reactor or requiring reactor fuel
  These radiation environments may throw light on new materials or physics which has not been encountered so far
Chemistry/Performance of Targets
  Study the chemistry/irradiation-induced changes of Lead-Bi Liquid Alloy or solid spallation target concepts in a prototypic high radiation environment
Physics
  Investigate life-limiting phenomena (transmutation produced impurities, radiation damage)
  The rate of incineration very long lived minor actinides or fission products in a given neutron spectrum
  Neutron/photon/electron heat generation and deposition

## Slide 13: Spallation Targets for Particle Physics
Common interests between NE and the particle physics research program
  Isotope Production
  Material Irradiation
  Thermal Neutron Beams
  Transmutation of radioactive waste/ Power Generation
Beginnings of conceptual design for next generation particle physics experiments involve Mega-Watt targetry design and infrastructure for muons, kaons & spallation research programs

## Slide 14: Spallation Targets for Particle Physics
Proton beam
  ISOL, EDM
  Proton reaction cross section measurements
  Proton rich isotope production
    On-line targets sputter or recoil isotopes
    Sealed targets that are retrieved and processed for isotopes
    Fluid or gas extraction
  Create neutrons for subsequent targetry
  Recover proton induced reactants
    Sputter
    Gas
    Liquid target cleanup
Spallation Neutrons
  Fission product production
  Neutron reaction cross section measurements
  Neutron rich isotope production
    On-line targets sputter or recoil isotopes
    Sealed targets that are retrieved and processed for isotopes
  Neutron beams - Cold neutrons, Ultra-cold neutrons
  Cold Neutron Irradiation Tank (liquid He4 or less)
    Investigate n properties reactions

## Slide 15: Energy Station Applications
The CW beam from the Project-X linac will be a unique facility in the United States to address key physics and technology demonstration
Accelerator physics and technology issues:
  Beam dynamics modeling and benchmarking of beam loss and halo mechanisms,
  Reliability of front-end systems,
  Robust SRF linac technology - RF power generation and delivery
  Beam instrumentation needed to support high power and reliable operation
Potential Nuclear Physics Uses
  CW accelerator/spallation similar to reactor neutron source
  Isotopes, neutron beams
  Access to irradiation volume

## Slide 16: High Power Target Issues in Common Between Energy Station and Physics Station
Energy deposition
Secondary particle production
Target material response using FEA codes
Target cooling or replacement
Activation and radiation damage everywhere
Thermal shock
Target lifetime
Particle capture, moderation and delivery
Beam windows
Target station design, including shielding, remote handling, licensing, etc
Diagnostics in high radiation environments
Demanding environmental and safety requirements

## Slide 17: Energy Station Could Benefit Design of Physics Station
Materials selection for targets, diagnostics, structures, mechanical systems typically based on limited data from fission reactor community, fusion community
Potential for much different response in high power accelerator due to high flux of high energy particles
Materials irradiation in Energy Station can address Physics target issues
  Beam-Target Interface
  Radiation damage/transmutation reaction impurities
  Remote Handling
  Liquid metal target components