## Slide 1: Numerical assessment of the inhomogeneous temperature field and the quality of heat extraction from Nb3Sn impregnated magnets for the High Luminosity upgrade of the LHC
Patricia Borges de Sousa, Kirtana Puthran, Marta Sabaté-Gilarte, Francesco Cerutti, Susana Izquierdo Bermudez, Ezio Todesco, and Rob van Weelderen
2LOr2A-03
Applied Superconductivity Conference, 23-28 October 2022, Honolulu, Hawaii, USA
2LOr2A – HL-LHC: Nb3Sn Magnets II

## Slide 2: Framework
In the context of the High-Luminosity upgrade of the LHC at CERN, a robust multi-region CFD numerical toolkit for the modelling of heat transfer in complex cryogenic system geometries involving He II has been developed
Initial work aimed to provide thermal design requirements early enough in the MQXF design phase such that they could be implemented in the mechanical design
The work presented here is a continuation of previous studies, implementing updated MQXF geometry and dose maps (April 2022) as well as a fully upgraded numerical toolkit

## Slide 3: Thermal mapping of HL-LHC inner triplets
Context:
Previously established temperature margins along the full cross-section of Nb3Sn magnets and enveloping cold masses need to be reevaluated to reflect changes in both power deposition and geometry, and to validate the heat extraction design.
Objective:
Systematic assessment of temperature fields and resulting theoretical margins in the magnet coils and validation of the heat extraction design of the cold mass under peak power deposition conditions at nominal luminosity
Tools:
A 2D numerical framework has been developed to model the temperature distribution in the combined solid-superfluid He system of each magnet and enveloping cold mass using open-source software.

## Slide 4
Experimental evaluation of heat transfer of coil samples in He II
Extraction of material properties and interface resistance from exp. data
Numerical toolkit created, applied to experimental-size samples
Numerical toolkit used to validate heat extraction strategy and temperature margins of full-scale magnets and cold masses
Validation of numerical toolkit by comparing exp. results with simulation using extracted props.

## Slide 5: Numerical toolkit used to validate heat extraction of full-scale magnets and cold masses
Libraries and solver implemented in OpenFOAM v7
Geometry of magnet/cold mass created via Python API for Salome 9.7, easily adjustable for parametric studies
Currently, toolkit can handle 2D geometries and stagnant He II conditions and He II → He I transition (no flow)
Dose maps can be mapped onto the geometry and converted into peak power deposition; as dose scales linearly with luminosity, peak power can be easily scaled
Alternatively, direct heat input can be applied to any part of the geometry for dedicated studies

## Slide 6
MQXF v7 + cold mass
(ST0703448)
Simplified geometry for simulation (coded in Python and Salome)
Resulting 2D meshed geometry (coded in Python and Salome)
Geometry MQXF coil + cold mass (I)
Geometry created with dimensions in warm (300 K) conditions
Coil described in detail, simplifications mainly on iron yoke (bladder structure omitted), main He pathways included
He II heat extraction passages in Titanium pole/G10 keys (Ø8 mm hole every 50 mm) converted to 1 mm slit in 2D geometry
Mesh composed of 3.5M cells, prisms; coil pack refined → especial refinement on thin insulation layers

## Slide 7: Geometry MQXF coil + cold mass (II)
Outer vessel
Al shell
Iron yoke
Axial rods
Al collar
G10 keys
Cold bore
Coil wedge
Titanium pole (w/ He slit shown)
Inner insulation
Inter-cable insulation
Interlayer insulation
Nb3Sn cables
Outer + ground insulation

## Slide 8: Input for heat deposition from dose calculations (I)
Source: Review of estimates of energy deposition, M. Sabate-Gilarte
For each magnet/cold mass, the cross-section that corresponds to the highest dose (and consequently heat load) is selected
12 cross-sections selected (Q1/2/3 A and B, vertical and horizontal crossings)
Distance from interaction point [m]

## Slide 9: Input for heat deposition provided dose calculations (II)
For each magnet/cold mass, the dose at peak location for nominal luminosity (7 TeV, 5.0x1034 cm-2s-1) provided by FLUKA is mapped onto the mesh
Mapped dose is converted to 2D power density (mW/cm3) map at the peak (maximum) location according to each component’s density
Mesh is split into two regions, a He II region and a solid region. The solid region is composed of many different zones each with their own material properties
Q2B IR1-HC – dose @ peak loc.
Q2B IR1-HC – power dep. @ peak loc.
Luminosity 5.0x1034 cm-2s-1 Cold bore included
He II region (connected passages via poles)
Solid region (17 parts)

## Slide 10: He II region and (composite) solid region
Mesh is split into two regions: a He II region and a solid region
The solid region is composed of many different zones each with their own temperature-dependent material properties
Helium region Connected passageways via Titanium poles/keys
Solid region 16 areas with different properties
NB1: annular space 1.2 mm
NB2: 8 mm holes every 50 mm converted to 1 mm slit in 2D
NB3: cold bore insulation thickness of 510 µm

## Slide 11: Boundary conditions for calculations
Outer surface (inside of cold bore and outside of shell):
  Zero gradient
Pressurized He II to saturated He II HEX:
  Fixed value T = 1.9 K
Solid-to-Helium interface:
  Kapitza-resistance mediated interface , and derived from MQXF experimental data
On full cross-section:
  Resulting mapped power density computed from FLUKA, different for each magnet

## Slide 12: Results: example Q2B IR1-HC @ nominal luminosity
NB: Cold bore included, dose for luminosity = 5.0x1034 cm-2s-1
Max T in cold bore
Maximum coil temperature 2.2 K
Dose at peak location
Power deposition at peak location
Power deposition at peak location (coil detail)
Temperature distribution at peak location
Temp. distribution at peak location (coil detail)

## Slide 13: Results: example Q2B IR1-HC @ nominal luminosity
Temp. distribution at peak location (coil detail)
inner insulation
inner coil layer
outer coil layer
interlayer insulation
outer + ground insulation
He II
Kapitza resistance

## Slide 14: Results: example Q2B IR1-HC @ nominal luminosity
Max T in cold bore
Temp. distribution at peak location (coil detail)
For the described geometry, boundary conditions and considering the peak power deposition generated by a luminosity of 5x1034 cm-2s-1 for each of the 12 magnet cross-sections, we find:
Max. T in the coil = 2.3 K
Max. T in cold mass = 2.8 K (on cold bore)
He II T gradient O(100 µK)
T gradient dominated by inner insulation, interlayer insulation and Kapitza

## Slide 15: Resulting temperature margin for MQXF magnets
Current sharing temp. MQXF @ , ,
Temperature margin Q2B IR1-HC @ nom. lum.
(scale truncated at 5 K!)
Min T margin = 4.88 K
NB: Cold bore included, dose for luminosity = 5.0x1034 cm-2s-1
Based on the assumption of a homogeneous at 1.9 K, margins for an ideal magnet
Temperature profile Q2B IR1-HC @ nom. lum.
distribution considering conduction pathways and dose-generated heat deposition

## Slide 16: Resulting temperature margin for MQXF magnets
Current sharing temp. MQXF @ , ,
Temperature margin Q2B IR1-HC @ nom. lum.
(scale truncated at 5 K!)
Min T margin = 4.88 K
Based on the assumption of a homogeneous at 1.9 K
For the described geometry, boundary conditions and considering the peak power deposition generated by a luminosity of 5x1034 cm-2s-1 for each of the 12 magnet cross-sections, we find:
Min. T margin in the coil = 4.78 K
Invariably located on the 8 turn(s) closest to the pole
The rest of the coil pack for each magnet cross-section has a temperature margin higher than 5 K

## Slide 17: Summary (I)
Robust, easily adaptable numerical toolkit has been consolidated to produce results in a timeframe that allows for parametric investigation of geometry, operational temperature, and power deposition on magnet systems cooled by stagnant, pressurized He II
The heat extraction pathways for the HL-LHC inner triplet magnets have been validated for the latest geometry, considering a steady-state power deposition at peak location for nominal operating conditions (5.0x1034 cm-2s-1, 7 TeV), at 1.9 K cold source

## Slide 18: Summary (II)
The temperature field in MQXF coil and cold-mass cross-sections has been updated w.r.t. previous assessments, considering the influence of the dose-generated power deposition for the peak position in each magnet
The maximum calculated coil temperature is 2.3 K, while the rest of the cold mass sees a localized maximum ≤ 2.8 K, located on the cold bore
Considering the calculated temperature distribution, for the design , , and cold source at 1.9 K, the minimum temperature margin is calculated to be between 4.78 K and 4.92 K
 | On coil pack | On cold mass
Maximum power density | 3.6 mW/cm3 | 6.4 mW/cm3
Maximum temperature | 2.30 K | 2.79 K
Minimum temp. margin | 4.78 K | N/A
MQXF cross-sections at peak dose, 7 TeV, 5.0x1034 cm-2s-1,1.9 K cold source

## Slide 19: Outlook
Consolidated strategy can be applied to investigate temperature distribution & margins, as well as to validate the heat extraction strategy, on other geometries including non-impregnated coil structures
Simulations of a 2D longitudinal section of the cold masses will be carried out to better evaluate the gradient along the pressurized He II region with real He passageways (8 mm holes every 50 mm)
Next major step is to move to a 3D (simplified) geometry: magnet configurations that rely on reduced He content and/or long conduction paths can profit from a 3D picture of temperature distribution

## Slide 20: Thank you for your attention!

## Slide 21: Results at peak location for IR1/HC Luminosity = 5.0 x 1034 cm-2s-1 Energy = 7 TeV
Dose map cold mass in GeV/cm3
Power deposition cold mass in mW/cm3
Power deposition (coil detail) in mW/cm3
Temperature profile cold mass in K
Temperature profile (coil detail) in K

## Slide 22
Dose maps at peak location – IR1/HC

## Slide 23
Power deposition at peak location – IR1/HC

## Slide 24
Power deposition at peak location (coil) – IR1/HC

## Slide 25
Temperature profile at peak location – IR1/HC

## Slide 26
Temperature profile at peak location (coil) – IR1/HC

## Slide 27: Results at peak location for IR5/VC Luminosity = 5.0 x 1034 cm-2s-1 Energy = 7 TeV
Dose map cold mass in GeV/cm3
Power deposition cold mass in mW/cm3
Power deposition (coil detail) in mW/cm3
Temperature profile cold mass in K
Temperature profile (coil detail) in K

## Slide 28
Dose maps at peak location – IR5/VC

## Slide 29
Power deposition at peak location – IR5/VC

## Slide 30
Power deposition at peak location (coil) – IR5/VC

## Slide 31
Temperature profile at peak location – IR5/VC

## Slide 32
Temperature profile at peak location (coil) – IR5/VC