## Slide 1: SiPM Low Power Bias Generation for Dune FD2-VD
Sergio Rescia and the BNL Team
BNL Dune FD2-VD Workshop
13 Apr 2022

## Slide 2
PoF  DC ~12 Vin  ~200 Vout
  Current PoF unit tested has ~6.7 V at RT and ~10.4 V at cold
Colpitts oscillator + Cockcroft-Walton charge pump  feasibility study
  Fairly simple and low power circuit solution capable of cryogenic operation which can generate ~200V bias using ~10-20mW or less power for SiPMbias
Challenge is to control the output voltage and provide regulation
  use varactor voltage-controlled attenuator
  control supply VDD of Colpitts oscillator
SiPMBias Generation for Dune FD2-VD

## Slide 3
CW mult.
Colpitts Oscillator
Variable
Attenuator
VHV_unfiltered
CF
RF
200MΩ
-
+
VREF
Rin
Rfb
Rdiv
VHV
needs cryogenic micropower opamp:
TLC721B (tested by NASA)
(?) TLV9101 newer version of TLC721B
(?) ADA4098-1 high voltage, VDD=50V
SiPM HV Bias Generator
Inspired by photomultiplier base HV generator

## Slide 4
with:
2 x KV1471
CVP=50pF
Ccwmult=20p
control range is +/-12%
Vcontrol=0.1V Vpp=20.07V
Vcontrol=1V Vpp=18.5V
Vcontrol=2V Vpp=17.6V
Vcontrol=3V Vpp=16.8V
Vcontrol=10V Vpp=15.6V
R1
15Meg
R2
5.6Meg
R3
5000
CFB
1µ
CACV1
0.1µ
VDD
12
C1
10n
C2
3.3n
330n
L1
C3
4.7n
M1
RJU002N06
RV1
1M
RV2
1M
CVP
50p
CACV2
0.1µ
Ccwmult
20p
Vcontrol
3V
DV1
DV2
KV1471
OUT
Colpitts Oscillator
Colpitts and Attenuator

## Slide 5
Inspired by photomultiplier base HV generator
HV Bias: Colpitts oscillator + Cockcroft-Walton charge pump
Colpitts Oscillator
Cockroft-Walton Multiplier
R1
15Meg
R2
5.6Meg
R3
5000
CFB1
1µ
CACV1
0.1µ
C2
10n
C3
3.3n
330n
L1
C4
4.7n
M1
DV1
RV1
1Meg
RV2
1Meg
CVP
CACV2
0.1µ
Rdivider1
16Meg
CFdiv
Rdivider2
500Meg
RFSiPM
1Meg
CF2
0.47µ
RSiPM
200Meg
Cpos
3p
RF
Rin
100k
S
ADA4098-1
VDD
nopamp
nHVunfiltered
VDD
VHV
VREF
6.3V
needs cryogenic micropower opamp
TLC721B (tested by NASA)
(?) TLV9101 newer version of TLC721B
(?) ADA4098-1 high voltage, VDD=50V
12V
+
+

## Slide 6
~20mV pp ripple at the output of the Cockroft-Walton
Easily filtered
Colpitts output ~20Vpp