## Slide 1: Step-up/boost DC-DC converters test summary
Eaglekumar Tarpara on behalf of BNL CE team
04/13/2022

## Slide 2: Content
X-ARAPUCA and SiPM Readout
Search for Step-up DC-DC modules
Step-up DC-DC modules tested at cryogenic temperatures
  CHVM3-12-0300PW (TDK)
  0.3US12-P0.1, 0.4US5-P0.1 (Advanced Energy)
  C10940-53, C10940-03, C11204-02 (Hamamatsu)
  AH0SP-12, Q025-5C, Q025-12 (EMCO, Xp Power)
  12SAR 250, 5SAR250, 5SM48S (PICO Electronics)
Summary

## Slide 3: Veljko’s Talk in LIDINE 2021 Light Detection In Noble Elements
Charge and Light Sensing in Noble Liquid TPCs
  https://indico.physics.ucsd.edu/event/1/contributions/103/

## Slide 4: Veljko’s Talk in LIDINE 2021 Light Detection In Noble Elements
Improve SNR with ES (Electrostatic) transformer

## Slide 5: A Possible X-ARAPUCA Readout Scheme
  160 SiPMs in 40p4s configuration, HV ~ 200 V
  4 bias resistors, 1 capacitor Cb before FE ASIC
Goal: explore HV DC-DC modules outputting ~200V at cryogenic temperatures (77K-89K)

## Slide 6: Search for DC-DC modules
Basic requirements of step-up DC-DC converters
  Output voltage range up to 200V
  Survive at cryogenic temperature as low as 77K (liquid nitrogen)
  High power efficiency when the load current is ~100 µA
  Low noise
Market survey of DC-DC modules

## Slide 7: Commercial DC-DC modules
Manufacturer | Model | Type | Input Voltage (V) | Output Voltage (V) | Typical Input Current (mA) | Maximum Output Current | Typical Ripple and Noise
TDK-Lambda | CHVM3-12-0300PW | Integrated Module | 10.8-13.2 | 0-300 | 395 | 10mA@300V | 30 mV
TI | LM3478/LM3488 | Controller | 2.97-40 | 1.26-500 |  | 1A@12V | 
TI | LM3478Q/LM3488Q | Controller | 2.97-40 | 1.26-500 |  | 3A@10V | 
TI | LM3481/LTM3481-Q1 | Controller | 2.97-48 | 1.26-500 |  | 2A@12V | 
 |  | Controller |  |  |  | 1.5A@12V | 
 |  | Controller |  |  |  | 1.25A@12V | 
TI | LM51561/LM5156 | Controller | 1.5-60 | 1.5-300 |  | 3A@12V | 
TI | LM51551/LM5155 | Controller | 1.5-45 | 1.5-300 |  | 2A@24V, 4A@5V, 2A@12V | 
TI | LM5022/LM5022Q | Controller | 6-60 | 1.25-300 |  | 0.5A@40V | 
Maxim | MAX17597 | Controller | 4.5-36 | 5-250 |  | 1A@24V | 
Maxim | MAX17499 | Controller | 9.5-24 | 1.23-400 |  |  | 
ADI | LTC3862-1 | Controller | 8.5-36 | <350 |  | 5A@48V | 
ADI | LTC3862-2 | Controller | 5.5-36 | <350 |  | 10A@50V | 
ADI |  |  |  |  |  | 2A@120V | 
ADI |  |  |  |  |  | 6A@12V | 
ADI | LT8312 | Controller | 10-38 | <400 |  | 0.375A@400V | 
ADI | LT3757/LT3757A | Controller | 2.9-40 | <350 |  | 1.5A@12V, 3A@5V, 1A@-15V, 3A@5V | 
ADI | LT3758/LT3758A | Controller | 5.5-100 | <350 |  | 1A@24V, 3A@3.3V | 
Hamamatsu | C9619-51 | Integrated Module | 12 | <2000 | 460 | 2mA | 60 mV
 | C11152-51 | Integrated Module | 12 | <1500 | 220 | 1mA | 5 mV
 | C12733-04 | Integrated Module | 10-35 | 500-1800 | 90 | 90uA | 100 mV
 | C13890-55 | Integrated Module | 11-16 | <1250 | 125 | 0.6mA | 38 mV
 | C14051-55 | Integrated Module | 11-16 | <10000 | 260 | 0.2mA | 100 mV
 | C11204-02 | Integrated Module | 5 | 20-90 | 40 | 2mA | 0.2 mV
 | C10940-03 | Integrated Module | 5 | -200/-1200 | 230 | 0.6mA | 50 mV
 | C10940-53 | Integrated Module | 5 | 200-1200 | 230 | 0.6mA | 50 mV
Advanced Energy Industries, Inc | ULTRAVOLT US SERIES | Integrated Module | 5 or 12-15V | 0-500 | 50-60 | 0.2-0.5mA | <0.01%*Vout
XP Power | A Series | Integrated Module | 5/12/24V | 0-6000 | 500mA | 5mA | <1%*Vout
 | Q Series | Integrated Module | 5/12/24V | 0-10,000 | 100mA | 1mA | <1%*Vout
 | AG Series | Integrated Module | 5/12/24V | 0-6000 | 500mA | 1mA | <1%*Vout
PICO | Series AV/SMV | Integrated Module | 5/12/15/24/28 | 0-500 |  |  | 

## Slide 8: DC-DC module testing at cold temperature
# | Module | Manufacture | R load | Vin (V) | Vout (V) at RT | Vout (V) at LN2 | Works at Cold? | Comments
1 | CHVM3-12-0300PW | TDK | 10MΩ | 12 | 200 | 0 | No | 
2 | 0.3US12-P0.1 | Advanced Energy | 10MΩ | 12 | 200 | 0 | No | 
3 | 0.4US5-P0.1 | Advanced Energy | 10MΩ | 5 | 200 | 0 | No | 
4 | C10940-53 | Hamamatsu | 10MΩ | 5 | 205 | 0 | No | 
5 | C10940-03 (negative HV) | Hamamatsu | 10MΩ | 5 | -200 | 0 | No | 
6 | C11204-02 | Hamamatsu |  | 5 | 40 | 0 | No | 
7 | AH0SP-12 | EMCO, XP Power | 10MΩ | 10 | 200 | 0 | No | 
8 | 12SAR 250 | PICO Electronics | 1MΩ | 12 | 200 | 0 | No | 
9 | 5SAR 250 | PICO Electronics | 1MΩ | 5.1 | 200 | 0 | No | 
10 | Q025-5C | EMCO, XP Power | 10MΩ | 5 | 222 | 0 | No | 
11 | 5SM48S | PICO Electronics | 10MΩ | 5 | 74.5 | 10.63 | Yes | At cold, output voltage reduced to 1.26 V with 20kΩ load Results are not matched with the University of Iowa results
 |  |  | 20kΩ | 5 | 60.5 | 1.26 |  | 
12 | Q025-12 | EMCO, XP Power | 10MΩ | 12 | 203 | 52 | Yes | Works at cold with reduced voltage ~52 V Ordered a few more modules for retesting

## Slide 9: CHVM3-12-0300PW (TDK)
Datasheet
  https://product.tdk.com/system/files/dam/doc/product/power/switching-power/dc-dc-converter/specification/chvm3_spc.pdf

## Slide 10: CHVM3-12-0300PW (Failed when T < -50C)
Temp | Vin /V | Iin /mA | Vcntl / V | Icntl /mA | HV /V
RT | 12 | 41.70 | 2.68 | 0.120 | 200.38
Can’t output HV properly when temperature drop to < -50C (note: there is temperature difference between DC-DC kernel and T sensor)
Cool down
warm up
With 10MΩ load

## Slide 11: 0.3US12-P0.1 (Advanced Energy)
Datasheet
  https://www.advancedenergy.com/products/high-voltage-products/high-voltage-power-supplies/micro-size-high-voltage-dc-to-dc-modules/us-series/
Temp | Vin /V | Iin /mA | Vcntl / V | Icntl /mA | HV /V
RT | 12 | 7.58 | 1.67 | 0 | 200.65
note: REF = 2.494V, MON = 1.67V
Can’t output HV properly when temperature drop to < -50C
Case metal shorts to pin#2 (0V)
With 10MΩ load
0.4US5-P0.1 is also failed at LN2

## Slide 12: C10940-53 (Hamamatsu)
Datasheet
  https://www.hamamatsu.com/content/dam/hamamatsu-photonics/sites/documents/99_SALES_LIBRARY/etd/C10940_TACC1069E.pdf
Temp | Vin /V | Iin /mA | Vcntl / V | Icntl /mA | HV /V
RT | 5 | 11.49 | 0.208 | 0 | 205.08
Can’t output HV when it submerged in LN2, however it survive when temperature is higher than -170C.
Note: Ripple RMS ~10mV after RC filter
With 10MΩ load

## Slide 13: C10940-53 (Hamamatsu)
Place it in the deep Dewar
  Sufficient cooldown time to ensure the inner and surface has the same temperature
  Power is off
    no power until the temperature is stable for ~30 minutes
Temperature °C | Vin / V | Iin /mA | Vout /V | 
RT | 5V | 11.5mA | 205V | 
-160 | 5V | ~20mA | 210V | 
-170 | 5V | 2.6 | 0.09 | 
-170 | 5.2V | 20 | 210 | 
-172 | 5.2V | 3 | 0.1 | 
-172 | 5.5 | 20 | 212 | 
-180 | 6 V | 2.8 | 0.1 | 
-181 | 6.5V | 3.2 | 0.1 | 
in LN2 | 7~10V | 3.6~11mA | 0.1~0.2 | 
In LN2 | 11V | > 1A | 0.2V | damaged
When T < -100C, the output jumps to > 250V and then return to ~200V
C10940-03 (negative HV) and C11204-02 are also failed at LN2 temperature

## Slide 14: AH0SP-12 (Xp Power)
Datasheet
  https://www.xppower.com/portals/0/pdfs/SF_A_Series.pdf
Output is 0V when submerged in LN2.
Temp (C) | i/p Voltage (V) | i/p Current (mA) | o/p Voltage (V) | o/p AC ripple (mV)
+14 | 3.88 | 11.76 | 199.8 | 0.94
-40.2 | 3.88 | 11.76 | 199.9 | 0.8
-45 | 3.88 | 31.75 | 183.72 | 
-77 | 3.88 (4.4) | 31.75 (10.76) | 178.2 (199.9) | 
-95.5 | 4.4 (4.9) | 12.68 (10.8) | 180 (200) | 
-120 | 4.9 (5.35) | 13.68 (10.68) | 187.2 (199.9) | 
-139 | 5.35 (6.7) | 12.62 (13.9) | 156.4 (200) | 
-176 | 6.7 (10.3) | 12.46 (11.07) | 177 (207.5) | 
LN2 | 10.3 | 6.62 | 0 V | 
With 10MΩ load

## Slide 15: 12SAR 250 (PICO Electronics)
Datasheet
  https://www.picoelectronics.com/node/69108
With 1MΩ load

## Slide 16: 12SAR 250 (PICO Electronics)
Run 1
At -150 C, the output voltage is gradually increased to ~236 V, then suddenly reduces to 0V
Temp (C) | i/p Voltage (V) | i/p Current (mA) | o/p Voltage (V) | o/p AC ripple (mV)
+24 | 12 | 25.6 | 200.6 | 3.5
-52 | 12 | 25.6 | 199.3 | 4.2
-116 | 12 | 28.8 | 199.2 | 
-150 | 12 | 35.2 | 220 | 
 | 12 | 42.2 | 230 | 
 | 12 | 77.2 | 234 | 
 | 12 | 11.5 | 0 | After few seconds
Run 2
Temp (C) | i/p Voltage (V) | i/p Current (mA) | o/p Voltage (V) | o/p AC ripple (mV)
+22 | 12 | 22.4 | 200 | 3.8
-80 | 12 | 23 | 199 | 3.5
-151 | 12 | 36.3 | 215 | 3.6
 | 12 | 39.8 | 230 | 
 | 12 | 81.9 | 236 | 
 | 12 | 9.0 | 0 | After few seconds
5SAR250 is also failed at LN2 temperature

## Slide 17: Q025-5C (Xp Power -EMCO)
Datasheet
  https://www.xppower.com/portals/0/pdfs/SF_Q_Series.pdf
Temp (C) | i/p Voltage (V) (Control Voltage (V)) | i/p Current (mA) | o/p Voltage (V) | Comments
+25 | 5 V (2 V) | 22 | 222 | 
-75 | 5 V (2 V) | 30.7 | 207 | 
-135 | 5 V (2 V) | 27.3 | 202 | 
-153 | 5 V (3.5 V) | 44 | 220 | 
 |  |  | 112 | Decreased after few seconds, then constant at 112 V
LN2 | 5 V (3.5 V) | 54 | 112 | 
 |  |  | 0 | Decreased to 0 V after few seconds
At LN2, the output voltage is decreased to 0V
With 10MΩ load

## Slide 18: 5SM48S (PICO Electronics)
Datasheet
  https://www.picoelectronics.com/node/13270
Temp (C) | i/p Voltage (V) (Control Voltage (V)) | i/p Current (mA) | o/p Voltage (V)
+25 | 5 | 74.5 | 133.75
-90 | 5 | 83 | 133
-137 | 5 | 83.2 | 128
 |  |  | 88
-160 | 5 | 63 | 77
 |  |  | 51
LN2 | 5 | 54 | 10.63
 | 6 | 76 | 14.2
 | 7 | 99 | 17.8
 | 10 | 172 | 33.4
 | 12 | 251 | 54.2
At LN2, the output voltage is constant at 54 V
10 MΩ load
Vin=1V, Vout= 4V
Vin=5V, Vout=54V
@LN2
With 10MΩ load

## Slide 19: 5SM48S (PICO Electronics)
At LN2, results are not consistent with the results presented by the University of Iowa
Possible reasons:
  Test setup difference?
  Since PICO Electronics is a small company, different batch modules may have different performances at cold?
With 20kΩ load
Vin=5V, Vout= 60.3 V
Vin=5V, Vout=70V and unstable after few seconds
@RT
University of Iowa results:
https://indico.fnal.gov/event/53080/
@LN2
Vin=5V, Vout=1.26 constant
 | Temp (C) | i/p Voltage (V) (Control Voltage (V)) | i/p Current (mA) | o/p Voltage (V) | o/p AC ripple (mV)
BNL | RT | 5 | 94.1 | 60.5 | 141
 |  | 5 | 94 | 70 | 5000 (very noisy after few seconds)
Uni.of Iowa | RT | 5 |  | 54.9 | 
BNL | LN2 | 5 | 94.5 | 1.26 | 0.15
BNL | LN2 | 5.25 | 45 | 1.59 | 
Uni.of Iowa | LN2 | 5.25 |  | 43.4 | 
@RT
@LN2
20s

## Slide 20: Q025-12 (Xp Power -EMCO)
Datasheet
  https://www.xppower.com/portals/0/pdfs/SF_Q_Series.pdf
At LN2, the output voltage is constant at ~52 V
Temp (C) | i/p Voltage (V) (Control Voltage (V)) | i/p Current (mA) | o/p Voltage (V) | o/p AC ripple (mV)
+25 | 9 | 61 | 203.24 | 0.53
-95 | 9 | 91 | 200.64 | 0.5
-115 | 9 | 17.5 | 195.4 | 0.32
-150 | 9 | 13 | 196.88 | 0.4
 | 9.2 | 13.5 | 201.16 | 0.3
-187 | 9.2 | 12 | 198.1 | 0.3
 |  | 2 | 37.11, After few seconds | 
 | 20 | 9.7 | 125 | 
LN2 | 12 (maximum recommended input voltage) |  | ~52 | 
 | 20 | 9.7 | 129 | 
Vin=9V, Vout= ~37 V
@LN2
Vin=12V, Vout= ~56 V
@LN2
Vin=5V, Vout= ~5 V
With 10MΩ load

## Slide 21: Summary
A step-up DC-DC modules working at cryogenic temperature (77K-89K) is crucial to implement SiPM cold readout scheme
  Especially when PoF is presented for DUNE FD2-VD photon detector
Search and test of step-up DC-DC modules being carried out at BNL
  Tested 12 different (from 5 manufacturers) HV DC-DC modules at RT and cryogenic (as low as LN2) temperatures
  Most of the devices are failed at LN2 temperature
    Commercial DC-DC modules may have used transistors that don’t work at LN2 temperatures, such as bipolar junction transistors (BJTs).
  5SM48S (Pico Electronics) can’t reproduce test results reported with the different test setup
  Q025-12 (EMCO, XP Power) works at a cold with reduced output voltage, still needs to investigate further

## Slide 22: Back up slides

## Slide 23: 0.4US5-P0.1
Datasheet
  https://www.advancedenergy.com/products/high-voltage-products/high-voltage-power-supplies/micro-size-high-voltage-dc-to-dc-modules/us-series/
Temp | Vin /V | Iin /mA | Vcntl / V | Icntl /mA | HV /V
RT | 5 | 6.81 | 1.255 | 0 | 200.27
note: REF = 2.492V, MON = 1.255V
Case metal is open to pin#2 (0V). It should short to pin#2 according to datasheet
Can’t output HV properly when temperature drop to < -150C
With 10MΩ load

## Slide 24: C10940-03 (negative HV)
Datasheet
  https://www.hamamatsu.com/content/dam/hamamatsu-photonics/sites/documents/99_SALES_LIBRARY/etd/C10940_TACC1069E.pdf
Temp | Vin /V | Iin /mA | Vcntl / V | Icntl /mA | HV /V
RT | 5 | 11.39 | 0.208 | 0 | -200.33
Can’t output HV when it submerged in LN2, however it survive when temperature is higher than -170C.
Note: Ripple RMS ~10mV after RC filter
With 10MΩ load

## Slide 25: C11204-02
Datasheet
  https://www.hamamatsu.com/content/dam/hamamatsu-photonics/sites/documents/99_SALES_LIBRARY/ssd/c11204-02_kacc1242e.pdf
Can’t output HV properly when temperature is lower than -60C.
HV outputs 40V by default

## Slide 26: 5SAR 250 (PICO Electronics)
Datasheet
  https://www.picoelectronics.com/node/69108
Output load is constant 1 MOhm.
Temp (C) | i/p Voltage (V) (Control Voltage (V)) | i/p Current (mA) | o/p Voltage (V) | o/p AC ripple (mV)
+25 | 5.1 (2.3) | 43.9 | 202.1 | 4.2
-53 | 5.1 (2.4) | 49.8 | 195.8 | 4.4
-80 | 5.1 (2.4) | 28.8 | 205 | 4.5
-93 | 5.1 (2.4) | 9.4 | 242 | 5.9
 | 5.1 (1.8) | 9.4 | 201.3 | 
-116 | 5.1 (1.8) | 87.1 | 205 | 4.1
-154 | 5.1 (1.8) | 2 | 0 | 
At <-93C, the output voltage is gradually increased
At <-150C, the output voltage is decreased to 0V
With 1MΩ load