## Slide 1: FD2-VD Discharge Effects on Cathode and X-ARAPUCA Modules
Sergio Rescia, Veljko Radeka, Bo Yu
and the BNL Team
BNL Dune FD2-VD Workshop
13 Apr 2022

## Slide 2: FD2 High Voltage System Components
TPC sensitive volume: 60m x 13m x 13.5m
The cathode plane: 60m x 13.5m
The field cage is 13m tall (6.5m double sided drift). Each field cage column (with own resistive divider chain) is ~ 3m (3.4m) wide. The resistance between nodes is 2.5Gohm.
The anodes (CRPs) are at the top and bottom of the cryostat.
The nominal cathode voltage is about -300kV.
60m
13m
13.5m
HV Feedthrough
Field cage
Field cage
Field cage
Cathode
HV Extender

## Slide 3: FD2 High Voltage System Schematic Diagram
The total capacitance of a profile near the center the field cage is about
40 pF/m, or 120pF over the 3m width of the field cage column.
There are 48 FC columns along the periphery of the cathode array. 2x20 columns are 3 m wide; 2x4 columns (at the cryostat ends) are 3.4 m wide.
There are about 192 FC modules , each 3m (3.4m) wide and 3m high.
not to scale

## Slide 4: Cathode Module
There are 4x20=80 cathode modules, each 3.4m x 3m x 5cm
4 X-Arapuca modules in each cathode module (~25 % of the cathode light sensitive)
Conductive wire meshes covering the X-Arapuca modules
Perforated resistive sheets (4Mohm/square) covering the rest of the frame openings
3m
Cathode “strip”
0.4m
3.4m
60cm
60cm
electronics
Strips for analysis

## Slide 5
Field Cage discharge from HV~300kV to zero; time scale 10 ns
Transient propagation along resistive HV bus is only diffusive; time scale 10-100 ms
Transient propagation on the cathode; there are three time scales: a) Capacitive coupling FC-cathode – 10 ns; same time scale as “spark” b) cathode R-C diffusive – 0.1 ms; c) entire cathode-HV bus diffusive -- ~ 100 ms
Discharge Transient: time scale
cath strip
13.5m
3.4m
cath strip
cath strip
cath strip
cath strip
cath strip
cath strip
CKA
C cathode-anode
CFK
C FC - cathode
(FC)
HV Bus
FC0
3m

## Slide 6
Illustration of capacitive coupling among FC-cathode-anode by weighting field lines from the cathode with respect to FC and anode (top half shown)
field cage (0V)
cathode (1V)
Anode (0V)
field cage (0V)
CFK
CKA
CFK dominate near FC
in the middle only CKA

## Slide 9
FC discharge model (voltage simulating discharge on FC0)
with Lser=600nH
No Lser; “step” slowed down to ~10ns to match the rise time of the case with Lser on FC0
Lser
RF1
50Meg
CFC1
7.8p
CHVF1
1n
RF2
10Meg
VHV
RFC1
1.25G
UFC1
ERZV20D182$3SP2$cryo
CFC2
174p
600n
Rshort
0.1
SWshort
Vcontrol
CFC0
7.8p
HV
nFC0
ncontrol
nFC1
DISCHARGE HAPPENS QUICKLY
DETAILS OF DISCHARGE DO NOT AFFECT RESULTS
600nH is the minimum.
More realistic ~several uH
Risetime ~tens of ns
Charge Q≈ tr x Ipeak

## Slide 10
FC Discharge Effect on Resistive Cathode: Resistive Cathode Equivalent Circuit
32 Cathode Strips (42 cm wide, ½ X-Arapuca)
Field Cage Transient “driven” from FC0
(worst case)
Cathode
“strip” R
Add a note of CK1FCtotal
RF1
50Meg
CHVF1
1n
RF2
10Meg
VHV
ERZV20D182$3SP2$cryo
Lshort
600n
Rshort
0.1
Sshort
Vcontrol
RK1
560k
Rk2
560k
CKA1
0.34p
CKA2
0.86p
CK1FCt
96p
CK2FCt
24p
Vdisch_FC0
HV
nFC0
ncontrol
K1
K2
107 FC profiles
CFC1
7.8p
RFC1
1.25G
UFC1
CFC2
174p
CFC0
7.8p
nFC1
Add box & transparent bkgd

## Slide 11
RK1
R0
CKA1
0.3p
RK2
CKA2
0.9p
RK3
CKA3 1.4p
RK4
CKA4
1.8pF
RK5
CKA5
2.3p
RK6
CKA6
2.7p
CKA7
3.0p
CFK1
CFK2
CFK3
CFK4
CFK5
CFK6
CFK7
Vdischarge
K1
K2
K3
K4
K5
K6
K7
nFC0
nFC0
nFC0
nFC0
nFC0
nFC0
nFC0
Current in XARAPUCA Shield caused by FC-cathode-anode capacitances
Simulates 2 cathode strips with maximum transient current in the shield of X-ARAPUCA ( in the 2nd row from the HV bus).
96p
24p
10.8p
5.5p
3.1p
1.9p
1.2p
nFC0

## Slide 12
Summary of Voltages on Cathode (log time 100 ms)
V(k1)
V(k2)
V(k3)
V(k4)
V(k5)
100ns
1µs
10µs
100µs
1ms
10ms
100ms
-300KV
-270KV
-240KV
-210KV
-180KV
-150KV
-120KV
-90KV
-60KV
-30KV
0KV
V(k1)
V(k2)
V(k3)
V(k4)
V(k5)
R-C diffusion on cathode
R-C diffusion along HV bus
Capacitive transient from FC to cathode strips

## Slide 13
Summary of Voltages on Cathode (25ms)
0.0µs
2.5µs
5.0µs
7.5µs
10.0µs
12.5µs
15.0µs
17.5µs
20.0µs
22.5µs
25.0µs
V(k1)
V(k2)
V(k3)
V(k4)
V(k5)
V(k6)
V(k7)
-300KV
-270KV
-240KV
-210KV
-180KV
-150KV
-120KV
-90KV
-60KV
-30KV
0KV
30KV
V(k1)
V(k2)
V(k3)
V(k4)
V(k5)
V(k6)
V(k7)

## Slide 14
Summary of Voltages on Cathode (1us)
V(k1)
V(k2)
V(k3)
V(k4)
V(k5)
V(k6)
V(k7)
0.0µs
0.1µs
0.2µs
0.3µs
0.4µs
0.5µs
0.6µs
0.7µs
0.8µs
0.9µs
1.0µs
-300KV
-270KV
-240KV
-210KV
-180KV
-150KV
-120KV
-90KV
-60KV
-30KV
0KV
30KV
V(k1)
V(k2)
V(k3)
V(k4)
V(k5)
V(k6)
V(k7)

## Slide 15
Potential Difference between Cathode Strips (1us)
V(k1)-V(k2)
V(k4)-V(k5)
V(k2)-V(k3)
V(k6)-V(k7)
V(k3)-V(k4)
Max ≃50kV difference between strip 4 and 5
0.0µs
0.1µs
0.2µs
0.3µs
0.4µs
0.5µs
0.6µs
0.7µs
0.8µs
0.9µs
1.0µs
-5KV
0KV
5KV
10KV
15KV
20KV
25KV
30KV
35KV
40KV
45KV
50KV
55KV
V(K1,K2)
V(K2,K3)
V(K3,K4)
V(K4,K5)
V(K6,K7)
Note: it’s the CHARGE and current that matters for possible damage to XARAPUCA

## Slide 18
Potential difference (gradient) over the width of one X-ARAPUCA module (84cm) [V] (charge difference is small)

## Slide 19
Current through X-ARAPUCA Shield (linear scales)
Displacement Current I(CKA3)+I(CKA4) scaled to X-ARAPUCA
Area Charge ~ 0.8 µC
This is for 10ns discharge: for slower discharge,
max current would be reduced

## Slide 20
Current through XARAPUCA Shield (log-log scales)
Displacement Current I(CKA3)+I(CKA4) scaled to X-ARAPUCA Area
Diffusion current is very low.

## Slide 22
Discharge Simulation: Charge Capacitively Coupled to X-ARAPUCA
cath strip
13.5m
3.4m
cath strip
cath strip
cath strip
cath strip
cath strip
cath strip
CKA
C cathode-anode
CFK
C FC - cathode
(FC)
HV Bus
FC0
3m

## Slide 23: Shielding Effectiveness: Reflection + Absorption of Thin Shield in LAr
Redrawn from from: H.W. Ott
Ar thin shield t<<d
Ar thick shield t>>d
[dB]
A tot

## Slide 24
Risk to X-ARAPUCA is best measured by the discharge charge capacitively coupled to its shield, and thus it is entirely determined by the capacitances among field cage, cathode and anode
Discharge at any single HV bus segment may create ~100 kV potential transient on the cathode but with very high source impedance of a few pFs. Average current through the shield is negligible, but there may be an up to ~ 20 A spike due to capacitance to the anode CKA ; the charge in the spike is less than 0.5 µC.
Risk mitigation (assuming uniform distribution of X-ARAPUCAs): * X-ARAPUCA in the cathode module connected to the bus should have independent POF and fiber readout * X-ARAPUCAs in the cathode modules in the center (6 m x 54 m, 36 modules) less at risk (farther away: smaller charge coupled capacitively). Electrical connection of several X-ARAPUCAs could be considered
Next Step: design and test of X-ARAPUCA Faraday cage shield and optically transparent grid to withstand a charge of ~1 µC (to provide some margin) over <50 ns discharge duration
Conclusions:

## Slide 25
Supplemental Slides

## Slide 26: Maxwell Matrix
Add how Maxwell matrix is calculated
Some “representative” values
Drawing of electrodes
Cut and paste some portion of Maxwell matrix
Maxwell matrix: partial capacitances => model the coupling of electrodes

## Slide 27
FD2-VD Geometry used for Maxwell Matrix Calculation (Bo Yu)

## Slide 28
FD2-VD Geometry used for Maxwell Matrix Calculation (Bo Yu): detail

## Slide 29
Maxwell Matrix Capacitance FC profiles to Cathode strips: K1 to K10

## Slide 30: Maxwell Matrix Capacitance FC profiles to Cathode strips: K2 to K10
Dropping K1
(zoomed in)

## Slide 31: Maxwell Matrix
Maxwell capacitance (F/m) | HV Bus | F0 | C1 | C2 | C3 | C4 | C5 | C6 | C7 | C8 | C9 | C10 | C11 | C12 | C13 | C14 | C15 | C16 | C17 | C18 | C19 | C20
F1 | - 23.6E-15 | - 15.0E-12 | - 3.8E-12 | - 89.8E-15 | - 19.6E-15 | - 7.3E-15 | - 3.5E-15 | - 1.9E-15 | - 1.2E-15 | - 763.9E-18 | - 523.4E-18 | - 372.6E-18 | - 273.2E-18 | - 205.0E-18 | - 156.8E-18 | - 121.7E-18 | - 95.7E-18 | - 75.9E-18 | - 60.7E-18 | - 48.9E-18 | - 39.6E-18 | - 32.1E-18
F2 | - 8.3E-15 | - 3.2E-12 | - 3.1E-12 | - 172.9E-15 | - 39.0E-15 | - 14.6E-15 | - 7.0E-15 | - 3.9E-15 | - 2.4E-15 | - 1.5E-15 | - 1.1E-15 | - 750.3E-18 | - 550.3E-18 | - 413.1E-18 | - 316.0E-18 | - 245.3E-18 | - 192.8E-18 | - 153.1E-18 | - 122.5E-18 | - 98.6E-18 | - 79.8E-18 | - 64.8E-18
F3 | - 3.2E-15 | - 1.3E-12 | - 2.2E-12 | - 235.7E-15 | - 56.4E-15 | - 21.4E-15 | - 10.3E-15 | - 5.7E-15 | - 3.5E-15 | - 2.3E-15 | - 1.6E-15 | - 1.1E-15 | - 817.0E-18 | - 613.4E-18 | - 469.3E-18 | - 364.5E-18 | - 286.5E-18 | - 227.5E-18 | - 182.0E-18 | - 146.6E-18 | - 118.6E-18 | - 96.4E-18
F4 | - 1.5E-15 | - 676.1E-15 | - 1.6E-12 | - 278.3E-15 | - 71.8E-15 | - 27.8E-15 | - 13.5E-15 | - 7.5E-15 | - 4.6E-15 | - 3.0E-15 | - 2.1E-15 | - 1.5E-15 | - 1.1E-15 | - 812.8E-18 | - 622.1E-18 | - 483.2E-18 | - 379.9E-18 | - 301.7E-18 | - 241.4E-18 | - 194.4E-18 | - 157.4E-18 | - 127.8E-18
F5 | - 796.8E-18 | - 406.3E-15 | - 1.2E-12 | - 301.8E-15 | - 84.9E-15 | - 33.8E-15 | - 16.6E-15 | - 9.3E-15 | - 5.7E-15 | - 3.7E-15 | - 2.6E-15 | - 1.8E-15 | - 1.3E-15 | - 1.0E-15 | - 774.0E-18 | - 601.4E-18 | - 473.0E-18 | - 375.6E-18 | - 300.7E-18 | - 242.1E-18 | - 196.0E-18 | - 159.3E-18
F6 | - 476.4E-18 | - 264.4E-15 | - 874.8E-15 | - 309.1E-15 | - 95.5E-15 | - 39.2E-15 | - 19.5E-15 | - 11.0E-15 | - 6.8E-15 | - 4.4E-15 | - 3.1E-15 | - 2.2E-15 | - 1.6E-15 | - 1.2E-15 | - 924.9E-18 | - 718.9E-18 | - 565.5E-18 | - 449.2E-18 | - 359.6E-18 | - 289.7E-18 | - 234.6E-18 | - 190.6E-18
F7 | - 306.4E-18 | - 181.2E-15 | - 669.2E-15 | - 304.5E-15 | - 103.6E-15 | - 43.9E-15 | - 22.2E-15 | - 12.6E-15 | - 7.8E-15 | - 5.1E-15 | - 3.5E-15 | - 2.5E-15 | - 1.9E-15 | - 1.4E-15 | - 1.1E-15 | - 835.5E-18 | - 657.5E-18 | - 522.4E-18 | - 418.3E-18 | - 337.0E-18 | - 272.9E-18 | - 221.7E-18
F8 | - 208.2E-18 | - 128.6E-15 | - 519.9E-15 | - 291.7E-15 | - 109.2E-15 | - 48.0E-15 | - 24.6E-15 | - 14.1E-15 | - 8.8E-15 | - 5.8E-15 | - 4.0E-15 | - 2.9E-15 | - 2.1E-15 | - 1.6E-15 | - 1.2E-15 | - 951.0E-18 | - 748.6E-18 | - 595.0E-18 | - 476.5E-18 | - 384.0E-18 | - 311.0E-18 | - 252.8E-18
F9 | - 147.5E-18 | - 93.7E-15 | - 409.5E-15 | - 274.0E-15 | - 112.6E-15 | - 51.4E-15 | - 26.8E-15 | - 15.5E-15 | - 9.7E-15 | - 6.4E-15 | - 4.5E-15 | - 3.2E-15 | - 2.4E-15 | - 1.8E-15 | - 1.4E-15 | - 1.1E-15 | - 838.8E-18 | - 666.9E-18 | - 534.3E-18 | - 430.7E-18 | - 348.8E-18 | - 283.5E-18
F10 | - 108.1E-18 | - 69.5E-15 | - 326.8E-15 | - 253.8E-15 | - 114.1E-15 | - 54.2E-15 | - 28.8E-15 | - 16.9E-15 | - 10.6E-15 | - 7.1E-15 | - 4.9E-15 | - 3.5E-15 | - 2.6E-15 | - 2.0E-15 | - 1.5E-15 | - 1.2E-15 | - 928.2E-18 | - 738.2E-18 | - 591.6E-18 | - 477.0E-18 | - 386.4E-18 | - 314.1E-18
F11 | - 81.3E-18 | - 52.3E-15 | - 263.7E-15 | - 232.7E-15 | - 113.8E-15 | - 56.3E-15 | - 30.6E-15 | - 18.1E-15 | - 11.5E-15 | - 7.7E-15 | - 5.3E-15 | - 3.8E-15 | - 2.8E-15 | - 2.2E-15 | - 1.7E-15 | - 1.3E-15 | - 1.0E-15 | - 808.3E-18 | - 648.0E-18 | - 522.6E-18 | - 423.5E-18 | - 344.3E-18
F12 | - 62.6E-18 | - 39.8E-15 | - 215.1E-15 | - 211.8E-15 | - 112.2E-15 | - 57.8E-15 | - 32.0E-15 | - 19.2E-15 | - 12.2E-15 | - 8.2E-15 | - 5.8E-15 | - 4.2E-15 | - 3.1E-15 | - 2.3E-15 | - 1.8E-15 | - 1.4E-15 | - 1.1E-15 | - 877.1E-18 | - 703.4E-18 | - 567.4E-18 | - 459.9E-18 | - 374.0E-18
F13 | - 49.1E-18 | - 30.6E-15 | - 177.6E-15 | - 192.2E-15 | - 109.7E-15 | - 58.8E-15 | - 33.3E-15 | - 20.2E-15 | - 13.0E-15 | - 8.8E-15 | - 6.2E-15 | - 4.5E-15 | - 3.3E-15 | - 2.5E-15 | - 1.9E-15 | - 1.5E-15 | - 1.2E-15 | - 946.5E-18 | - 759.4E-18 | - 612.7E-18 | - 496.8E-18 | - 404.1E-18
F14 | - 39.1E-18 | - 23.6E-15 | - 147.7E-15 | - 173.7E-15 | - 106.2E-15 | - 59.2E-15 | - 34.3E-15 | - 21.1E-15 | - 13.7E-15 | - 9.3E-15 | - 6.5E-15 | - 4.7E-15 | - 3.5E-15 | - 2.7E-15 | - 2.1E-15 | - 1.6E-15 | - 1.3E-15 | - 1.0E-15 | - 813.3E-18 | - 656.5E-18 | - 532.4E-18 | - 433.1E-18
F15 | - 31.6E-18 | - 18.4E-15 | - 123.9E-15 | - 156.6E-15 | - 102.0E-15 | - 59.1E-15 | - 35.0E-15 | - 21.8E-15 | - 14.3E-15 | - 9.7E-15 | - 6.9E-15 | - 5.0E-15 | - 3.7E-15 | - 2.8E-15 | - 2.2E-15 | - 1.7E-15 | - 1.4E-15 | - 1.1E-15 | - 866.0E-18 | - 699.2E-18 | - 567.2E-18 | - 461.6E-18
F16 | - 25.9E-18 | - 14.4E-15 | - 105.0E-15 | - 141.4E-15 | - 97.7E-15 | - 58.8E-15 | - 35.6E-15 | - 22.5E-15 | - 14.8E-15 | - 10.2E-15 | - 7.2E-15 | - 5.3E-15 | - 3.9E-15 | - 3.0E-15 | - 2.3E-15 | - 1.8E-15 | - 1.4E-15 | - 1.1E-15 | - 919.4E-18 | - 742.7E-18 | - 602.7E-18 | - 490.6E-18
F17 | - 21.4E-18 | - 11.3E-15 | - 89.5E-15 | - 127.5E-15 | - 93.1E-15 | - 58.1E-15 | - 36.0E-15 | - 23.0E-15 | - 15.3E-15 | - 10.6E-15 | - 7.5E-15 | - 5.5E-15 | - 4.1E-15 | - 3.2E-15 | - 2.4E-15 | - 1.9E-15 | - 1.5E-15 | - 1.2E-15 | - 971.0E-18 | - 784.6E-18 | - 636.9E-18 | - 518.6E-18
F18 | - 17.9E-18 | - 8.9E-15 | - 76.8E-15 | - 114.9E-15 | - 88.2E-15 | - 57.1E-15 | - 36.1E-15 | - 23.5E-15 | - 15.8E-15 | - 11.0E-15 | - 7.8E-15 | - 5.8E-15 | - 4.3E-15 | - 3.3E-15 | - 2.6E-15 | - 2.0E-15 | - 1.6E-15 | - 1.3E-15 | - 1.0E-15 | - 825.2E-18 | - 670.1E-18 | - 545.7E-18
F19 | - 15.1E-18 | - 7.1E-15 | - 66.5E-15 | - 103.9E-15 | - 83.6E-15 | - 55.9E-15 | - 36.2E-15 | - 23.8E-15 | - 16.2E-15 | - 11.3E-15 | - 8.1E-15 | - 6.0E-15 | - 4.5E-15 | - 3.4E-15 | - 2.7E-15 | - 2.1E-15 | - 1.7E-15 | - 1.3E-15 | - 1.1E-15 | - 866.8E-18 | - 704.1E-18 | - 573.6E-18
F20 | - 12.9E-18 | - 5.7E-15 | - 57.8E-15 | - 93.9E-15 | - 78.9E-15 | - 54.5E-15 | - 36.1E-15 | - 24.1E-15 | - 16.5E-15 | - 11.6E-15 | - 8.4E-15 | - 6.2E-15 | - 4.7E-15 | - 3.6E-15 | - 2.8E-15 | - 2.2E-15 | - 1.7E-15 | - 1.4E-15 | - 1.1E-15 | - 906.3E-18 | - 736.5E-18 | - 600.2E-18
F30 | - 3.6E-18 | - 800.6E-18 | - 18.4E-15 | - 37.6E-15 | - 42.0E-15 | - 37.3E-15 | - 29.8E-15 | - 22.8E-15 | - 17.2E-15 | - 13.0E-15 | - 9.9E-15 | - 7.6E-15 | - 5.9E-15 | - 4.6E-15 | - 3.7E-15 | - 2.9E-15 | - 2.3E-15 | - 1.9E-15 | - 1.5E-15 | - 1.2E-15 | - 1.0E-15 | - 834.6E-18
F40 | - 1.5E-18 | - 222.1E-18 | - 7.9E-15 | - 17.8E-15 | - 22.8E-15 | - 23.4E-15 | - 21.4E-15 | - 18.3E-15 | - 15.1E-15 | - 12.2E-15 | - 9.8E-15 | - 7.9E-15 | - 6.3E-15 | - 5.1E-15 | - 4.1E-15 | - 3.3E-15 | - 2.7E-15 | - 2.2E-15 | - 1.8E-15 | - 1.5E-15 | - 1.2E-15 | - 998.8E-18
F50 | - 744.2E-21 | - 100.5E-18 | - 4.1E-15 | - 9.6E-15 | - 13.2E-15 | - 14.8E-15 | - 14.7E-15 | - 13.6E-15 | - 12.1E-15 | - 10.4E-15 | - 8.7E-15 | - 7.3E-15 | - 6.1E-15 | - 5.0E-15 | - 4.1E-15 | - 3.4E-15 | - 2.8E-15 | - 2.3E-15 | - 1.9E-15 | - 1.6E-15 | - 1.3E-15 | - 1.1E-15
F60 | - 423.5E-21 | - 55.9E-18 | - 2.3E-15 | - 5.6E-15 | - 8.1E-15 | - 9.6E-15 | - 10.1E-15 | - 9.9E-15 | - 9.2E-15 | - 8.3E-15 | - 7.3E-15 | - 6.3E-15 | - 5.4E-15 | - 4.6E-15 | - 3.9E-15 | - 3.3E-15 | - 2.7E-15 | - 2.3E-15 | - 1.9E-15 | - 1.6E-15 | - 1.3E-15 | - 1.1E-15
F70 | - 258.6E-21 | - 34.0E-18 | - 1.4E-15 | - 3.5E-15 | - 5.2E-15 | - 6.3E-15 | - 6.9E-15 | - 7.1E-15 | - 6.9E-15 | - 6.4E-15 | - 5.8E-15 | - 5.2E-15 | - 4.6E-15 | - 4.0E-15 | - 3.4E-15 | - 2.9E-15 | - 2.5E-15 | - 2.1E-15 | - 1.8E-15 | - 1.5E-15 | - 1.2E-15 | - 1.0E-15
F80 | - 163.9E-21 | - 21.5E-18 | - 910.3E-18 | - 2.3E-15 | - 3.4E-15 | - 4.2E-15 | - 4.8E-15 | - 5.0E-15 | - 5.0E-15 | - 4.8E-15 | - 4.5E-15 | - 4.1E-15 | - 3.6E-15 | - 3.2E-15 | - 2.8E-15 | - 2.4E-15 | - 2.1E-15 | - 1.8E-15 | - 1.5E-15 | - 1.3E-15 | - 1.1E-15 | - 909.8E-18
F90 | - 104.3E-21 | - 13.7E-18 | - 580.2E-18 | - 1.4E-15 | - 2.2E-15 | - 2.8E-15 | - 3.2E-15 | - 3.4E-15 | - 3.5E-15 | - 3.4E-15 | - 3.2E-15 | - 3.0E-15 | - 2.7E-15 | - 2.4E-15 | - 2.2E-15 | - 1.9E-15 | - 1.6E-15 | - 1.4E-15 | - 1.2E-15 | - 1.0E-15 | - 871.6E-18 | - 735.4E-18
F100 | - 64.3E-21 | - 8.4E-18 | - 358.2E-18 | - 894.9E-18 | - 1.4E-15 | - 1.8E-15 | - 2.0E-15 | - 2.2E-15 | - 2.3E-15 | - 2.3E-15 | - 2.2E-15 | - 2.0E-15 | - 1.9E-15 | - 1.7E-15 | - 1.5E-15 | - 1.3E-15 | - 1.2E-15 | - 1.0E-15 | - 867.4E-18 | - 741.6E-18 | - 630.8E-18 | - 533.9E-18
F101 | - 61.2E-21 | - 8.0E-18 | - 341.1E-18 | - 852.3E-18 | - 1.3E-15 | - 1.7E-15 | - 1.9E-15 | - 2.1E-15 | - 2.2E-15 | - 2.2E-15 | - 2.1E-15 | - 2.0E-15 | - 1.8E-15 | - 1.6E-15 | - 1.5E-15 | - 1.3E-15 | - 1.1E-15 | - 970.8E-18 | - 835.4E-18 | - 714.5E-18 | - 607.9E-18 | - 514.7E-18
F102 | - 58.5E-21 | - 7.7E-18 | - 325.8E-18 | - 814.3E-18 | - 1.2E-15 | - 1.6E-15 | - 1.9E-15 | - 2.0E-15 | - 2.1E-15 | - 2.1E-15 | - 2.0E-15 | - 1.9E-15 | - 1.7E-15 | - 1.6E-15 | - 1.4E-15 | - 1.2E-15 | - 1.1E-15 | - 937.1E-18 | - 806.8E-18 | - 690.2E-18 | - 587.4E-18 | - 497.5E-18
F103 | - 56.1E-21 | - 7.4E-18 | - 312.4E-18 | - 781.1E-18 | - 1.2E-15 | - 1.5E-15 | - 1.8E-15 | - 1.9E-15 | - 2.0E-15 | - 2.0E-15 | - 1.9E-15 | - 1.8E-15 | - 1.7E-15 | - 1.5E-15 | - 1.4E-15 | - 1.2E-15 | - 1.0E-15 | - 907.7E-18 | - 781.7E-18 | - 669.0E-18 | - 569.6E-18 | - 482.4E-18
F104 | - 54.4E-21 | - 7.1E-18 | - 302.9E-18 | - 757.6E-18 | - 1.2E-15 | - 1.5E-15 | - 1.7E-15 | - 1.9E-15 | - 1.9E-15 | - 1.9E-15 | - 1.9E-15 | - 1.8E-15 | - 1.6E-15 | - 1.5E-15 | - 1.3E-15 | - 1.2E-15 | - 1.0E-15 | - 888.6E-18 | - 765.5E-18 | - 655.4E-18 | - 558.1E-18 | - 472.8E-18
F105 | - 53.9E-21 | - 7.1E-18 | - 300.4E-18 | - 751.5E-18 | - 1.2E-15 | - 1.5E-15 | - 1.7E-15 | - 1.9E-15 | - 1.9E-15 | - 1.9E-15 | - 1.9E-15 | - 1.8E-15 | - 1.6E-15 | - 1.5E-15 | - 1.3E-15 | - 1.2E-15 | - 1.0E-15 | - 889.3E-18 | - 766.4E-18 | - 656.3E-18 | - 559.0E-18 | - 473.7E-18
F106 | - 57.1E-21 | - 7.5E-18 | - 318.0E-18 | - 795.7E-18 | - 1.2E-15 | - 1.6E-15 | - 1.8E-15 | - 2.0E-15 | - 2.1E-15 | - 2.1E-15 | - 2.0E-15 | - 1.9E-15 | - 1.7E-15 | - 1.6E-15 | - 1.4E-15 | - 1.2E-15 | - 1.1E-15 | - 950.1E-18 | - 819.0E-18 | - 701.6E-18 | - 597.7E-18 | - 506.6E-18
F107 | - 80.2E-21 | - 10.5E-18 | - 446.9E-18 | - 1.1E-15 | - 1.7E-15 | - 2.2E-15 | - 2.6E-15 | - 2.8E-15 | - 2.9E-15 | - 2.9E-15 | - 2.8E-15 | - 2.7E-15 | - 2.5E-15 | - 2.2E-15 | - 2.0E-15 | - 1.8E-15 | - 1.6E-15 | - 1.3E-15 | - 1.2E-15 | - 996.3E-18 | - 849.1E-18 | - 719.9E-18
Sum{F1-F20) (F/m) |  |  | - 16.0E-12 | - 4.1E-12 | - 1.8E-12 | - 917.2E-15 | - 518.1E-15 | - 315.7E-15 | - 204.2E-15 | - 138.5E-15 | - 97.6E-15 | - 70.8E-15 | - 52.7E-15 | - 40.0E-15 | - 30.8E-15 | - 24.1E-15 | - 19.0E-15 | - 15.2E-15 | - 12.2E-15 | - 9.8E-15 | - 8.0E-15 | - 6.5E-15
CFK (F) |  |  | - 96.0E-12 | - 24.4E-12 | - 10.8E-12 | - 5.5E-12 | - 3.1E-12 | - 1.9E-12 | - 1.2E-12 | - 831.1E-15 | - 585.4E-15 | - 425.0E-15 | - 316.2E-15 | - 239.9E-15 | - 185.0E-15 | - 144.6E-15 | - 114.2E-15 | - 91.0E-15 | - 73.1E-15 | - 59.0E-15 | - 47.9E-15 | - 38.9E-15
Total Capacitance from Field Cage profiles FC1-20 to Kathode strip Ci Multiply by 6 (x 3m x 2 top & bottom FC in parallel) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 32
Summary of Voltages on Cathode (100ms)
V(k1)
V(k2)
V(k3)
V(k4)
V(k5)
0ms
10ms
20ms
30ms
40ms
50ms
60ms
70ms
80ms
90ms
100ms
-300KV
-270KV
-240KV
-210KV
-180KV
-150KV
-120KV
-90KV
-60KV
-30KV
0KV
V(k1)
V(k2)
V(k3)
V(k4)
V(k5)

## Slide 33
Interpolation zero, first, second order

## Slide 34: Shielding Effectiveness: Reflection + Absorption in Air
Redrawn from from: H.W. Ott
Ar thin shield t<<d
Ar thick shield t>>d
[dB]
A tot