## Slide 1: X-ARAPUCA HV Discharge Tests
Eric Raguzin, Veljko Radeka, Sergio Rescia
4/13/2021

## Slide 2
cath strip
13.5m
3.4m
cath strip
cath strip
cath strip
cath strip
cath strip
cath strip
CKA
C cathode-anode
CFK
C FC - cathode
(FC)
HV Bus
FC0
3m
Discharge Simulation: Charge Capacitively Coupled to X-ARAPUCA

## Slide 3
LV, HV power and data links are delivered to one module through fiber and then connected to one or two others via copper.
There’s risk that a HV discharge to one module could also affect other modules through this connection.
A solution would be the inclusion of a common mode inductance (“balun”) to attenuate potential HV discharge current. Its effectiveness must be evaluated.
Note that this can be avoided with “Power over Fiber” connections – although with higher cost.
Resistive
cathode sheets
Grounded
wire mesh
Grounded C-channel
ARAPUCAs with common electrical connections

## Slide 4: Testing Overview
BAV99 diodes – part of the cold electronics design to attenuate ESD
Twinax cable with shielding to be used for electrical connection
Break in cable for balun with common winding core for both power conductors and shield – essence of “common mode choke”
Receiving box with oscilloscope connection to measure magnitude of attenuated current
No shield connection to box
Shield connection to box
Shared common core

## Slide 5
Physical Implementation

## Slide 6: Bench Setup
HV Pulser applies voltage/current across shield of each “module”, simulating a discharge
Discharge path runs through BAV99 diodes, shielded twinax cable, common mode choke. Attenuated signal read out on the scope.
Enclosure allows safe testing, interlock will switch off exposed HV when opened
Test boxes will be covered and function as complete Faraday cages with penetrating feedthroughs properly connected

## Slide 7: HV Pulser Characterization
50 ohm out, 50 ohm terminated
Scope is in high impedance mode
Set to 1/10th Full Scale (nominal FS is 450 V)
Peak is ~42V, first pulse is ~2 ns FWHM
2 ns FWHM

## Slide 8: Measurements
With low impedance HV pulser output, we can emulate expected current pulses
The common mode choke will be swapped out with different coils
Externally clamped ferrite beads will be tested as well
Oscilloscope will read out attenuated signal seen by second X-ARAPUCA module
Ensure that discharge will not affect electronics in second module
Best performing coils and beads will characterized in LN2

## Slide 9: Backup Slides

## Slide 10: Closer look
Board with ground connected to shield, red PCBs with BAV99 diodes
Middle box to be filled with different coils to characterize effectiveness of common mode attenuation

## Slide 11: Cable
BNC Twinax uses RG 108
Rated up to 1kV
Standardized connectors and feedthroughs