## Slide 1: Stato sensori e maschere
7/4/22 INFN Bologna

## Slide 2: Modello Camera in simulazione
Camera da 1024 canali
  Usata in tutte le ultime simulazioni
  ~ 180 x 180 x 22mm
  ~500 Fori quadrati da 2.71mm con bordo 0.2mm
  Spessore fronte 0.1mm
Numerose varianti con fori diversi, pattern diversi, sensori diversi
  https://baltig.infn.it/dune/sand-optical/geometry

## Slide 3: Sensore
Sensore 32x32 pixel
Dati performance come Hamamatsu S14160-3050
  https://www.hamamatsu.com/content/dam/hamamatsu-photonics/sites/documents/99_SALES_LIBRARY/ssd/s14160_s14161_series_kapd1064e.pdf

## Slide 4: Detector Response
The goal is to perform a detailed simulation of the response of a SiPM sensor matrix and DAQ, including SiPM internal noise and electronics effects.
This tool can be used to perform optimization studies considering different SiPM models or ASICS.
An example parameter file:
https://baltig.infn.it/dune/sand-optical/detector-response-gpu/-/blob/master/config/config1.xml

## Slide 5: SiPM waveform simulation
Input from GEANT4
  list of simulated photon hit positions and times on the sensor surface
Each photon is assigned to the corresponding matrix SiPM (pixel)
Matrix borders and dead area between pixel is considered
An output waveform is simulated for every pixel
  Subsequent photons are summed into the waveform
  Can choose waveform length here. Longer is more GPU expensive
Intermediate output (not saved)
  Full "analog" waveform (floating point, very high sample rate)

## Slide 6: SiPM waveform simulation examples
SiPM characteristics and noise effect included:
1 p.e. gaussian amplitude distribution
PDE: fixed value or depending on photon wavelength (wip)
Single photon time resolution
noise: dark count rate, afterpulses, crosstalk, white and rf noise
threshold
threshold

## Slide 7: Electronics simulation
Simulation of multiple ASIC types implemented so far:
Charge integrator ADC + leading edge TDC (TRIROC-like, used with warm demonstrator)
Multiple TDCs for time-over-threshold (ALCOR) [wip]
Simple peak sensing [wip]...
Included effects:
  Analog bandwidth [wip]
  Amplifier gain and saturation
  Quantization error (ADC resolution)
  TDC time resolution
Output format: DRDF (binary png-like) and List-of-hits (for Sand reco)

## Slide 8: Actual prototypes
Warm demonstrator
  8x8 channels, 1mm pitch S13615
  17x17 hole mask
  Warm readout with TRIROC
Test results:
  SiPM and ASIC work OK
  TRIROC demo DAQ board is poor
  Can reconstruct one bright point source, struggles with two
  Survived LN2 bath
Cold demonstrator [wip]
  16x16 channels, 3mm pitch S14160 like in simulation
  Readout with 8xALCOR
  Expect 34x34 mask ~ 10 cm wide
Status:
  Waiting for PCB
  Firmware in progress
  Mechanics tbd

## Slide 9: Backup