## Slide 1: Writing ProtoDUNE RAW MC Files to art.hdf5

## Slide 2: Introduction
The code lives in /dune/app/users/barnali/hdf5_APAIO_testing/srcs/dunetpc/dune/APAIO/APAIORdWriter_module.cc
APAIO directory was initially made to write binary files and to read those binary files back in an artROOT files
Working with larsoft_v09_38_00
Will migrate them to the new GitHub repos

## Slide 3: The MC Data-Model
The writer module writes the output to make an art.hdf5 file with the following data structure .
GROUP "APA_0" {
DATASET "ChannelHeader_0" {
DATATYPE H5T_COMPOUND {
H5T_STD_I32BE "Chan";
H5T_IEEE_F32BE "Pedestal";
H5T_IEEE_F32BE "Sigma";
H5T_STD_I32BE "nADC";
H5T_STD_I16BE "Compression";
}
DATASET "ChannelID_0" {
DATATYPE H5T_STD_U16LE
DATASPACE SIMPLE { ( 6000 ) / ( 6000 ) }
DATA {
Writes MetaData
Writes Data
Header Info will be replicated nChannels * nTriggerRecords times per APA.
Channel Data will also be replicated nChannels * nTriggerRecords times per APA.

## Slide 4: The Way DAQ Models their Data
GROUP "TriggerRecord00028" {
GROUP "TPC" {
GROUP "APA000" {
DATASET "Link00" {
DATATYPE H5T_STD_I8LE
DATASPACE SIMPLE { ( 4640080, 1 ) / ( 4640080, 1 ) }
}
DATASET "Link01" {
DATATYPE H5T_STD_I8LE
DATASPACE SIMPLE { ( 4640080, 1 ) / ( 4640080, 1 ) }
}
…………………
DATASET "TriggerRecordHeader" {
DATATYPE H5T_STD_I8LE
DATASPACE SIMPLE { ( 368, 1 ) / ( 368, 1 ) }
}
}

## Slide 5: Why Different Models ?
We are not formatting the data generated in the MC to look as much like what is produced online.
There is no need to have the same data format for data and MC as long as there is a lossless map between them.
MC groups the data by APA. That way searching through the trigger record for all the channels in an APA will be quicker and easier.
All we need is a separate tool to read each kind of file format/data format in the existing tools to accommodate all different kinds of data.

## Slide 6
artHDF5 file
The input file  /dune/data/users/trj/pdsp_data/np04_raw_run005177_0004_dl1_decode_gen.root
It reads one event out of an old decoded ProtoDUNE-SP data file with Raw::RawDigits in it from 6 APAs and writes out 1 art.h5 file.
The output file  dump_binary.h5
The size of the output file to write 1 event  191M

## Slide 7
Dumping artHDF5 file
DATASET "ChannelID_2560" {
DATATYPE H5T_STD_I16LE
DATASPACE SIMPLE { ( 6000 ) / ( 6000 ) }
DATA {
(0): 2271, 2274, 2274, 2275, 2272, 2272, 2271, 2269, 2271, 2270,
(10): 2271, 2269, 2270, 2272, 2275, 2276, 2275, 2275, 2275, 2272,
(20): 2271, 2271, 2269, 2269, 2267, 2270, 2271, 2275, 2275, 2275,
(30): 2275, 2273, 2271, 2269, 2271, 2272, 2275, 2277, 2276, 2274,
(40): 2271, 2269, 2269, 2270, 2271, 2274, 2279, 2283, 2284, 2283,
(50): 2278, 2279, 2280, 2281, 2282, 2279, 2274, 2271, 2272, 2275,
---------------------------------------------------
---------------------------------------------------
6000 ADC values are written here.
They are signed 16-bit integers.
GROUP "APA_1" {
DATASET "ChannelHeader_2560" {
DATATYPE H5T_COMPOUND {
H5T_STD_I32BE "Chan";
H5T_IEEE_F32BE "Pedestal";
H5T_IEEE_F32BE "Sigma";
H5T_STD_I32BE "nADC";
H5T_STD_I16BE "Compression";
}
DATASPACE SIMPLE { ( 1 ) / ( 1 ) }
DATA {
(0): {
2560,
2305,
8.49856,
6000,
0
}
}
}