## Slide 1: Recent Accelerator Performance and Shutdown plans
Phil Adamson
Fermilab Accelerator Division

## Slide 2: Introduction
Tevatron shut down at the end of last FY
  Impact celebrated yesterday
Talks later this afternoon
  Muon Accelerator Program
    Yagmur Torun
  FNAL Test Beam
    Aria Soha
  ASTA
    Mike Church

## Slide 3: Accelerator Overview

## Slide 4: Accelerator Overview
Linac:
  NTF, MTA
Booster
  BNB (MiniBooNE)
Main Injector/Recycler
  NuMI (MINOS, Minerva)
  SY120
    Test Beams, SeaQuest
Muon Rings
    Ex-pbar source

## Slide 5: NuMI Performance
Recall NuMI target problems from last year
Water cooling lines for target redesigned
  Target ran until shutdown with no problems

## Slide 6: FY11: Annus Horribilis
Got 2.2E20 in FY11, thanks to heroic efforts from target folks (and delay to future projects)
New target NT07 installed at end of FY11
  Ran without problems until shutdown
(NT04)
NT05
NT06
NT01
NT02

## Slide 7: Main Injector
After Tevatron off, re-adjusted slip-stacking to fulfill request from NuMI with minimum losses
  Beam loss per proton accelerated reduced by almost a factor of 2
  ALARA
Retune after Tevatron off
Normalized beam loss (µJ/proton)

## Slide 8: SY120
Testbeam typically runs protons per spill
SeaQuest started running in March
  Ultimately wants 2 orders of magnitude more
  Can’t afford 2 orders of magnitude more beam loss
  Installed/installing instrumentation

## Slide 9: Proton Source
Steady year-on-year improvement
  Lots of small gains
Need Proton Improvement Plan for future
  See later in talk
BNB (MiniBooNE) good, steady performance

## Slide 10: Shutdown 2012

## Slide 11: Increasing beam power
Move slip-stacking to recycler
11 batch -> 12 batch
Increase Main Injector ramp rate (204 GeV/s -> 240 GeV/s)
330 (380) -> 700kW with only ~10% increase in per-pulse intensity
Main Injector
Recycler
Red: MI momentum
Green: Beam current

## Slide 12: Accelerator and NuMI Upgrades
Recycler Ring, RR
  New injection line into RR
  New extraction line from RR
  New 53 MHz RF system
  Instrumentation Upgrades
  New abort kickers
  Decommissioning of pbar components
Main Injector
  Two 53 MHz cavities
  Quad Power Supply Upgrade
  Low Level RF System
NuMI
  Change to medium energy n beam configuration (new target, horn, configuration)
  Cooling & power supply upgrades

## Slide 13: Big Picture
Crew 1
Crew 2
Crew 3
Crew4
Crew 5
Crew 6
Staging
NuMI Crew

## Slide 14
New MI8 line to recycler

## Slide 15: Future Proton Needs

## Slide 16: Proton Improvement Plan
Cockcroft Walton
Proton source is 40 years old
  Must run for at least 15 more years to support lab physics program
Need upgrades to permit higher rep rate for intensity frontier
Identify weaknesses and remedy
  Cockcroft-Waltons
    (2009 I- off for ~ 1 year for repair)
  Solution – RFQ Based Injector
    Install this shutdown

## Slide 17: Proton Improvement Plan
Linac
  Linac Dump Repair
  Vacuum Upgrades
  BPM Upgrade
  Klystron Maintenance
  Low Energy Maintenance
  LE PLC Upgrade
Booster
  Solid State Upgrade
  Booster Cavity Refurb.
  Gradient Magnet Moves
  Beam Absorber Install
  LCW Upgrade
  Possible Shielding Changes
  Booster RF cavity tuners need cooling upgrade to permit 15 Hz operation

## Slide 18: Summary
Accelerators have had a good year
“11-month” shutdown has begun
  Lots of work to do to upgrade complex to meet challenges of the intensity frontier
    ANU (double NuMI beam power)
    PIP (double+ proton source output)
    SeaQuest (2 orders of magnitude increase in slow spill from MI)
We are working hard to meet these challenges
Expect a report on startup / commissioning next year