## Slide 1: NEW ISO 330-1 GeV DFD lattice: CW to +/- 0.5%
C. Johnstone
Particle Accelerator Corporation
FFAG meeting
4/11/2012

## Slide 2: Isochronous 330 – 1000 MeV Layout
  Ring layout and half cell plotted (intermediate energy plotted: injection begins ~5.5 m radius)

## Slide 3: Isochronous 330 – 1000 MeV Machine Tunes
  Ring (left) and cell (right) tunes (vertical and horizontal close to 90 degrees); ring tune stable to +/-0.05 (2 rad)

## Slide 4: Isochronous 330 – 1000 MeV footprint and isochronous properties
  Average radius (left) :5.5 – 7.2 m (inj to ext); deviation in percent from isochronous (right). Note transition ~1200 MeV/c (585 MeV)

## Slide 5: Isochronous 330 – 1000 MeV Apertures
  Orbits in F (left) and orbits in D (right) in radial distance from injection

## Slide 6: Isochronous 330 – 1000 MeV Magnet lengths
  Half lengths of F and D – Note that SC D magnet (3.8T extraction field) is only 0.4 m long and is basically rectangular – can be made completely rectangular. F is almost a sector magnet.

## Slide 7: Isochronous 330 – 1000 MeV Magnetic Field Profiles
  F (left) and D (right) : D is almost a linear gradient

## Slide 8: Isochronous 330-1000 MeV NS FFAG
CW operation with ….
To +/- 0.05%
Six 2m straights for RF, injection, extraction
DFD layout : long straight at min horizontal beam size
Will require max RF cavities for low-loss operation
Need to develop 3D field map from COSY tools
RF cavity conceptual design
Upstream Booster lattice is next and needs to be matched to 1 GeV machine.

## Slide 9: Isochronous 330-1000 MeV NS FFAG Machine Table
Ring |  | 
Particle | H+ | 
Injection energy | 330 MeV | 
Extraction energy | 1 GeV | 
Injection B.rho | Alternating gradients | 
Extraction B.rho |  | 
Injection radius | 5.50 m | 
Extraction radius | 7.15 m | 
Variable extraction radius | Not needed | 
Degree of isochronicity | 0.05% preliminary | 
Geometrical acceptance |  | 
Dynamical acceptance | ≥ 400  mm-mr | 
Injection method | H- Stripping – CW injection | 
Extraction method | Field change/septum/single –turn resonance? | 
Transition gamma | 585 MeV | 

## Slide 10: Isochronous 330-1000 MeV NS FFAG Machine Table
Beam |  | 
Injected emittance, normalized | ≥ 200  mm-mr (TBD from space charge and losses) | 
Extracted emittance, normalized | ≥ 200  mm-mr | 
Injected intensity |  | 
Extracted intensity | 7-10MW | 
# ppb |  | 
Momentum spread | What can we capture | 
RF structure of injected beam | Min RF: 5.8 MHz | 
Lattice |  | 
Accelerator type | NS-FFAG | 
Lattice type | DFD | 
Number of cells | 6 | 
Number of straight sections | 6 | 
Straight section length, long | 2 m | 
Straight section length, short | 0.70 – 0.50 m (inj. to ext.) | 
Number of magnets | 2 per cell | 
Packing factor |  | 
Horizontal tune radial-dependence | See graph | 
Vertical tune radial-dependence | See graph | 

## Slide 11: Isochronous 330-1000 MeV NS FFAG Machine Table
Magnet, Warm | 
Field index, F type | 
Field index, D type | 
Wedge angles, F | 
Wedge angles, D | 
I/O fringe field r-dependence, F | 
I/O fringe field r-dependence, D | 
Sector angle, F | Edge crossing varies
Sector angle, D | 
Bend angle, F | 0.523 / 0.657 rad
Bend angle, D | 0.000 / -0.134
Radii on min/max orbits, F | 
Radii on min/max orbits, D | 
Magnetic field on R_min/max, F | 1.5 / 1.8 T
Magnetic field on R_max/min, D | 0.002 / -3.8T
Gap on R_max/min, F | 1-2”
Gap on R_max/min, D | 1-2”
Field profile, F | See graph
Field profile, D | See graph
Fringe fields, F | To be calculated
Fringe fields, D | “

## Slide 12: Isochronous 330-1000 MeV NS FFAG Machine Table
RF system |  | 
Number of cavities | 6 (3 straights) | 
RF gap shape | Straight | 
RF gap length |  | 
Cavity tilt |  | 
RF voltage |  | 
Energy gain per turn | > 4 MeV/turn - as large as possible | 
Harmonic number |  | 
RF wave shape | sinusoidal |