## Slide 1
Status of CM Assembly Infrastructure at CEA
PIP-II Technical Workshop - WG#1 HB650 Cryomodule Assembly
J. Drant A. Raut
S. Berry A. Moreau

## Slide 2: Status of LB650 CM Assembly
General workflow of workstations
Geographical location of the assembly workstations in CEA infrastructure
Overview of the main steps of each workstation
A detailed assembly step example
The use of mock-ups
The use of robot assistance for flange cleaning
Assembly tooling

## Slide 3: Status of LB650 CM Assembly
General workflow of workstations
Geographical location of the assembly workstations in CEA infrastructure
Overview of the main steps of each workstation
A detailed assembly step example
The use of mock-ups
The use of robot assistance for flange cleaning
Assembly tooling

## Slide 4: General workflow of workstations
CAP
Clean room elements assembly preparation
BLA
Beam Line Assembly
WAS/PRE
Washing of the elements in BELIMED
Preparation of the elements before entering the clean room
ABE
Assembly of the beam line equipments
SPA
Strongback Preparation Area
COS
Cold mass on strongback
CRY
Cryostating of the cold mass inside the vacuum vessel
Clean room
CLO
Vacuum vessel closure
BUN
Bunker cryomodule test
EXP
Preparation for shipment
Notes: WAS : WAShing of elements
PRE : PREparation of elements before clean room
CAP : in Clean room Assembly Preparation
BLA : Beam Line Assembly
ABE : Assembly of Beam line Equipments
SPA : Strongback Preparation Area
COS : Coldmass On Strongback
CRY : CRYostating
CLO : Closure of cryomodule
EXP : EXPedition

## Slide 5: Geographical location of the assembly workstations
General view of the layout of the various assembly workstations based on the layout of the ESS project
Workstation LAV/PREP
Workstation CAP
Workstation BLA
Workstation ABE
Workstation CLO
Workstation SPA
Workstation COS
Workstation CRY
Waiting area for Workstation BUN
Workstation EXP
Notes: WAS : WAShing of elements
PRE : PREparation of elements before clean room
CAP : in Clean room Assembly Preparation
BLA : Beam Line Assembly
ABE : Assembly of Beam line Equipments
SPA : Strongback Preparation Area
COS : Coldmass On Strongback
CRY : CRYostating
CLO : Closure of cryomodule
EXP : EXPedition

## Slide 6
1,15
1,35
15,00
SPA
CRY
CLO
ABE
COS
Cryomodule
Waiting
Area
Detailed view of the layout of the various assembly stations within the assembly hall, based on the layout of the ESS project
TEST & SHIPPING
(BUN & EXP)
CLEAN ROOM
(WAS/PRE/CAP/BLA)
Geographical location of the assembly workstations
South to North rail
(46m) for the beam line
East to west rails (15m)
Strongback and vacuum vessel
Notes: WAS : WAShing of elements
PRE : PREparation of elements before clean room
CAP : in Clean room Assembly Preparation
BLA : Beam Line Assembly
ABE : Assembly of Beam line Equipments
SPA : Strongback Preparation Area
COS : Coldmass On Strongback
CRY : CRYostating
CLO : Closure of cryomodule
EXP : EXPedition

## Slide 7: Status of LB650 CM Assembly
General workflow of workstations
Geographical location of the assembly workstations in CEA infrastructure
Overview of the main steps of each workstation
A detailed assembly step example
The use of mock-ups
The use of robot assistance for flange cleaning
Assembly tooling
Notes: Adapt the assembly step workflow with design modification, HB650 REX, mockup assemblies

## Slide 8: Workstation WAS/PRE
Reception and QC of components (cavities, couplers, bellows,…)
A - PRE
Plugs mounted
Preparation of components before washing steps (installation, mounting of plugs…)
1 - PRE
Alignment and setting of cavities posts and clean room assembly tooling
2 - PRE
Cleaning of cavities, bellows, couplers manifold and beam pipe end
1 - WAS
Cleaning of cavities posts, tooling
2 - WAS
Cleaning of all clean room parts (valves, screws, …)
3 - WAS
Pictures from ESS

## Slide 9: Workstation CAP
Cleaning of cavities, bellows, couplers manifold and beam pipe ends
1 - WAS
Cleaning of cavities posts, tooling
2 - WAS
Cleaning of all clean room parts (valves, screws, …)
3 - WAS
Transfer and installation of a cavity on posts
3 - CAP
Cavity alignment settings
4 - CAP
Leak test of the pumping group connection and the cavity by spraying and slow venting
5 - CAP
Transfer of the coupler manifold to the coupler test station
1 - CAP
Leak test of the pumping group connection and RGA of the coupler manifold and slow venting
2 - CAP

## Slide 10: Workstation BLA
Leak test of the pumping group connection and the cavity by spraying
5 - CAP
Leak test of the pumping group connection and RGA of the coupler manifold
2 - CAP
Cleaning the holes of the cavity coupler flange
2 - BLA
Coupler manifold disconnection and mounting on coupler tooling + pre-positioning of coupler/cavity
1 - BLA
Cavity/coupler final connection and installation of holding coupler tooling
3 - BLA
Leak test of the connection and slow venting
4 - BLA
Repetitions of previous steps to obtain 4 aligned leak tight cavities/couplers
5 - BLA

## Slide 11: Workstation BLA
Assembly of extremity devices (ion pum, valves, flushing system…) on DS gate valve
7 - BLA
Setting up beam pipe ends on posts
6 - BLA
DS gate valve/ DS beam pipe end assembly
9 - BLA
Leak check of extremity devices/DS gate valve/ DS beam pipe end connections and slow venting
10 - BLA
Assembly of flushing system on US gate valve
11 - BLA
Burst disk system first RAV/ DS beam pipe end connection
8 - BLA
US gate valve/ US beam pipe end assembly
12 - BLA
Leak check of flushing device/US gate valve/ US beam pipe end connections and slow venting
13 - BLA

## Slide 12: Workstation BLA
Cavity 3/Bellow/Cavity 4 connection
15 - BLA
Cavity 4/beam pipe end connection
14 - BLA
Cavity 1/Bellow/Cavity 2 connection
17 - BLA
beam pipe end/Cavity 1 connection with flushing
18 - BLA
Coupler/coupler and coupler/transitions lengths settings
19 - BLA
Cavity 2/Bellow/Cavity 3 connection
16 - BLA
Cavity string leak check and RGA
20 - BLA
Holdpoint before transferring the cavity string to ABE workstation
21 - BLA

## Slide 13: Workstation ABE
Cavity string transfer in ABE workstation
1 - ABE
Preparation of the cavity string (bellows protections...)
2 - ABE
Alignment of the cavity string
3 - ABE
Preparation of the diphasic tubes sections for welding
4 - ABE
Welding of instrumentations hoses on 3rd diphasic tube section and routing of extension cables inside
5 - ABE
Positioning and welding of diphasic tubes on cavity string and level tube cap + Internal and external visual inspection of the welds
6 - ABE
Routing of cables into diphasic tubes and connection with extension cables + electrical control sensors
10 - ABE
Lifting of cavity string and tooling to maintaining cooling line installation
7 - ABE
Positioning and welding of the cooling line on cavity string + external visual inspection of the welds
8 - ABE
Leak test of the welds of the helium circuitry welded by spraying then by overpressure of helium and sniffing
9 - ABE

## Slide 14: Workstation ABE
Installation of on-helium tanks probes and electric testing of them
11 - ABE
Installation of the MLI on the cold mass
12 - ABE
Preparation of tuners assembly (pre-assembly of sections, assembly of piezos, limit switches,...)
13 - ABE
Tuners mechanical assembly with motors on cavity string under RF control and electrical tests on tuner operation
15 - ABE
Installation of magnetic shields
16 - ABE
Assembly of thermal straps for beam pipe ends, couplers and tuner motors
17 - ABE
Installation without settings of the invar bars on diphasic tube lugs
18 - ABE
Installation of RF cables on cavities
14 - ABE
Hold point before transfer to SPA workstation
19 - ABE

## Slide 15: Workstation SPA
Transfer from vacuum vessel to SPA workstation
1 - SPA
Mounting the vacuum vessel on the adjustment tool on rails
3 - SPA
Adjustment of the reference height of the studs
5 - SPA
Levelling and alignment of the vacuum vessel
4 - SPA
Installation of the strongback sections on studs and alignment of each section
7 - SPA
Assembly of studs/housings on stud/rails interface tooling
6 - SPA
Assembly of the 4 sections of the strongback and beam pipe end tooling then leveling
8 - SPA
Insertion of the strongback into the vacuum vessel and placing the studs to reference height
9 - SPA
Mounting the magnetic shield on the vacuum vessel
2 - SPA

## Slide 16: Workstation SPA
Final assembly of the strongback conical plates and setting of the beam pipe end tooling
10 - SPA
Removal of the strongback from the vacuum vessel and drilling of the conical plates to receive the positioning pins
11 - SPA
Assembly of the lower part of the magnetic shield and the lowest part of MLI on strongback
12 - SPA
Installation of G11 posts equipped with Cernox on the strongback with electrical testing
13 - SPA
Lower thermal shield assembly with 50K line
14 - SPA
Assembly of cavity posts on G11 posts and 5K line supports
16 - SPA
Hold point before transfer to COS workstation
17 - SPA
Installation of 5K line
15 - SPA

## Slide 17: Workstation COS
Displacement of the cold mass above the strongback
1 - COS
Complete control and alignment of the cavity train
2 - COS
Positioning of the cold mass on SB (height and longitudinal positioning)
3 - COS
Assembly of the C-Shape elements on the cavities
4 - COS
Disassembly of bellows rigidifiers and transitions support bars then setting the Invar bars
7 - COS
Assembly of the G-10 cryo lines support and installation of JT and 2K pumping lines
8 - COS
Alignment and alignment check with C-block adjustment
6 - COS
Installation of the means of thermalization of cables and parts (thermal blocs/straps connections)
9 - COS
Installation of HBCAM sights
10 - COS
Assembly of the upper thermal shield elements on cold mass
11 - COS
Thermal sensor mounting on thermal shield and electrical test
12 - COS
Assembly of the 30-layer MLI on the upper thermal shield
13 - COS
Hold point before the CRY workstation
14 - COS

## Slide 18: Workstation CRY
Insertion of strongback with cold mass in vacuum vessel
1 - CRY
Positioning of the cold mass in the vacuum vessel (Adjustment of the studs + tightening of the locking nut)
2 - CRY
Pre-stressing of the strongback via studs (vacuum deformation, thermal shrinkage)
3 - CRY
Side heat shield/MLI/magnetic shield assembly
5 - CRY
Assembly of the vessel endcaps / HBCAM windows / gate valves protections
6 - CRY
Position control of cold mass in vacuum vessel by HBCAM
7 - CRY
Studs vacuum cover assembly
8 - CRY
Hold point before transfer to CLO station
9 - CRY
Couplers warm parts assembly
4 - CRY

## Slide 19: Workstation CRY
Assembly/welding of the relief line (tubes/bellows) + Cernox & Platinium
1 - CLO
Assembly of 5K inlet & outlet bayonets valves kits on 5K hoses
2 - CLO
Assembly of 35K-50K inlet & outlet bayonets valves kits on hoses
3 - CLO
Assembly of the 2K pumping bayonet valve kit (line+valve)
4 - CLO
Assembling the CD cryo bayonet valve kit on hoses
5 - CLO
Assembly of the Cryo JT bayonet valve kit on hoses
6 - CLO
Weldment of heat exchanger, pumping line straight tube/bellows and connection of the 2 elements
7 - CLO
Leak test of the welds of the helium circuitry welded by spraying then by overpressure of helium with sniffing Radiography of CD valve welds
8 - CLO
Lateral side port MLI and thermal shield assembly
9 - CLO
Thermal shield assembly on top port + Instrumentation hoses retainer mounting
10 - CLO
Assembly of the lateral MLI on top port
11 - CLO
Magnetic shield assembly on top port
12 - CLO
Assembling the top port on the vacuum vessel
13 - CLO

## Slide 20: Workstation CRY
Thermal shield/ MLI/magnetic shield assembly on flanges of side port and top port
14 - CLO
Top port/side port flange assembly
15 - CLO
Assembly of solid, pumping flanges and instrumentation flanges (with magnetic shield trapdoors)
16 - CLO
Assembly of the relief valve of the vacuum vessel
18 - CLO
Top port instrumentation flange assembly + pressure probes + relief line flange assembly
17 - CLO
Vacuuming of the vessel
19 - CLO
Vacuum vessel leak check by spraying
20 - CLO
Pressurization of the thermal shield 50K, 5K, 2K lines
21 - CLO
Leak check by surveying helium presence in insulating vacuum
22 - CLO
Beam line burst Disc final assembly
23 - CLO
Vacuuming of the cavities string
24 - CLO
Helium filling of vacuum vessel and leak check of the string + final RGA
25 - CLO
Purge of the helium from the vacuum vessel + vacuuming of the vessel
26 - CLO
Holdpoint before test phase
27 - CLO

## Slide 21: Workstation BUN
At this point in the assembly workflow, only the waveguide assembly is planned within the test site

## Slide 22: Workstation EXP
Disassembly of the wave guides and warm part of the coupler
1 - EXP
Installation of bumpers to maintain the cold part of the couplers
2 - EXP
Removal of top port instrumentation ports, relief line flange, top port flange and the top port
3 - EXP
Removal of the thermal, magnetic and MLI shields from the top port
4 - EXP
Disassembly of the heat exchanger and relief line
5 - EXP
Mounting of the plugs on the relief line/pumping line/flexible
6 - EXP
Re-assembly of the top port flange and instrumentation ports on the vacuum vessel
7 - EXP
Assembly of spring interfaces for the transport
8 - EXP
Assembly of the transport structure for shipping + installation of the vessel inside
9 - EXP
Filling of insulating vacuum of the vacuum vessel with nitrogen
10 - EXP
Extension of beam line pressure gauges, temperature gauges, accelerometers and shock sensors to instrumentation box
11 - EXP
Hold final point before shipping
12 - EXP
Notes: Adapt the assembly step workflow with design modification, HB650 REX, mockup assemblies

## Slide 23: Status of LB650 CM Assembly
General workflow of workstations
Geographical location of the assembly workstations in CEA infrastructure
Overview of the main steps of each workstation
A detailed assembly step example
The use of mock-ups
The use of robot assistance for flange cleaning
Assembly tooling

## Slide 24: More detailed assembly step example
Opening of the nitrogen flushing on the cavity angle valve n-1
Connection of the flushing hose to the cavity angle valve n-1
Preparation of the cleaned and checked consumables (screws, tools)
Assembly of the bellows assembly tool on the cavity post n-1
Clean the whole flange with IPA
Unscrew the 4 yellow screws, clean and check the 4 holes
Place 4 clean screws/nuts in the 4 cleaned holes
Unscrew all the screws except the 4 yellow screws/nuts
Mounting of 2 centering devices at 180° on each of the 2 bellows flanges
Adjustment of the parallelism of the 2 bellows flanges
Rough adjustment of the bellows tie rods (to avoid too much movement when adjusting the rotating flange)
Placement of the bellows in its assembly tooling
Alignment of the bellows with the cavity flange n-1 and n
Removing the bellows from its tooling
Removal of the centering pins
Cleaning and checking the inter-cavity bellows
Blowing with particle control of each hole of the cavity flange n and n-1
Re-installation of the bellows on its tooling without modifying the settings of the tooling
Cleaning and checking of the aluminium bellows/cavity seal
Placement of the aluminium gasket in the test flange by ovalizing it
Placement of the ovalized aluminium gasket on the open fixed flange of the bellows (critical operation: new gloves, hands at the bottom of the flange...)
Removal of the remaining screws and opening of the n-1 cavity flange by removing the remaining n nut screws while holding the flange against the cavity (2 operators)
Visual inspection of the cavity opening
Installation of n diametrically opposed screws + washers + nuts (frictionless entry)
Installation of the other screws and tightening to the star torque
Backing up of the cavity n-1
Removal of the bellows positioning tooling (checking the slight lowering of the bellows due to gravity)
Assembly of the third tie rods
Cleaning and checking of the bellows/cavity aluminium seal
Placement of the aluminium gasket in the test flange by ovalizing it
Placement of the ovalized aluminium gasket on the rotating flange of the bellows (critical operation: new gloves, hands at the bottom of the flange...)
Removal of the remaining screws and opening of the cavity n flange by removing the remaining n nut screws while maintaining the flange against the cavity (2 operators)
Visual inspection of the cavity opening
Installation of n diametrically opposed screws + washers + nuts (frictionless entry)
Installation of the other screws and tightening to the star torque
Place the bottom tie rods between the cavity posts n-1 and n
Replace the tie rods of the bellows without stress on the bellows (maintain the adjustment)
Cavity n-1/Bellow/Cavity n connection with flushing
Each assembly steps detailed in previous slides can be detailed in smaller steps
The objective is to create the detailed procedure for the assembly
Notes: Continue writing the detailed workflow (adding details, images) to converge on the start of writing the procedures

## Slide 25: Status of LB650 CM Assembly
General workflow of workstations
Geographical location of the assembly workstations in CEA infrastructure
Overview of the main steps of each workstation
A detailed assembly step example
The use of mock-ups
The use of robot assistance for flange cleaning
Assembly tooling

## Slide 26: Use of mock-ups
To validate some critical assembly steps, the use of mock-ups objects appears useful.
  The use of mock-ups will make it possible to test the mountability and usability of tools with objects whose interfaces are representative of real objects
  This process has been used on several projects (IFMIF, ESS, …)
For the PIP-II LB650 cryomodule, some assembly tests with mock-ups have been identified :

## Slide 27: Status of LB650 CM Assembly
General workflow of workstations
Geographical location of the assembly workstations in CEA infrastructure
Overview of the main steps of each workstation
A detailed assembly step example
The use of mock-ups
The use of robot assistance for flange cleaning
Assembly tooling

## Slide 28: Flange Cleaning Procedure : Robot Assistance
A current R&D project aims at developing the use of robot assistance during flange cleaning phases
All flange/holes cleaning steps could be realized with a robot assistance
A pre-cleaning step is realized with lint free cloth
The robot is equipped with Ionized nitrogen blower and a particle counter
The cleaning process is carried out until the targeted cleanliness criterion is validated
Slow implantation in ESS clean room production workflow
Flange cleaning procedure can be used in LB650 clean room assembly workflow with the ESS experience

## Slide 29: Status of LB650 CM Assembly
General workflow of workstations
Geographical location of the assembly workstations in CEA infrastructure
Overview of the main steps of each workstation
A detailed assembly step example
The use of mock-ups
The use of robot assistance for flange cleaning
Assembly tooling

## Slide 30: Assembly tooling
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low
Clean room posts leveling tooling
Aluminium

## Slide 31: Assembly tooling
Cavity/beam pipe end/gate valve posts
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 32: Assembly tooling
Beam pipe end length adjusting tooling
PTFE
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 33: Assembly tooling
Cavity in clean room roll & pitch adjusting tooling
Aluminium
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 34: Assembly tooling
Coupler-coupler distance tooling
Aluminium
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 35: Assembly tooling
Cavity handling cart in clean room
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 36: Assembly tooling
Beam pipe end handling cart in clean room
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 37: Assembly tooling
Alignment tooling for cavity/coupler connection
Aluminium
Stainless steel
HDPE
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 38: Assembly tooling
Alignment tooling for cavity/bellow/cavity connection
Bellow/cavity alignment tooling with locating pins (like HB650 clean room process)
Stainless steel
HDPE
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 39: Assembly tooling
Support tooling for couplers
Aluminium
Stainless Steel
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 40: Assembly tooling
Support and adjustment tooling for strongback
Use of an extra set of housings+studs on tooling to limit the disassembly steps
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low

## Slide 41: Assembly tooling
Support and adjustment tooling for the vacuum vessel
Some tooling for the assembly steps are designed or in design finalization.
They are inspired by previous CEA projects (XFEL, ESS,…) and the experience from PIP-II pCM HB650
Aluminum/Polymers is favored over stainless steel for parts that will be handled regularly or on which the stresses remain low
Notes: Continue the tooling design (lifting tooling,…)

## Slide 42: Thanks for your attention