## Slide 1
Risk Analysis of Cryogenic Distribution Systems
Maciej Chorowski / Wroclaw Univ. of Science and Technology
PIP-II Technical Workshop
07/13/2022

## Slide 2
Outline
Why the Risk Analysis of Cryogenic Distribution System is recommended.
Metodology proposed by WUST
Risk analysis examples – LHC, ESS distribution systems
Conclusions

## Slide 3
Outline
Why the Risk Analysis of Cryogenic Distribution System is recommended.
Metodology proposed by WUST
RAMI approach
Risk analysis examples – LHC, ESS distribution systems
Conclusions

## Slide 4: Properties of cryogenic liquids
Cryog-en | M [g] | TN [K] | 1 [kg/m3] | 2 [kg/m3] | 3 [kg/m3] | TC [K] | PC [MPa] | HV [kJ/kg] | V2 / V1 ---- | V3 / V1 ----
He | 4,003 | 4,2 | 124,9 | 16,91 | 0,178 | 5,2 | 0,229 | 20,3 | 7,4 | 701
H2 | 2,01 | 20,3 | 70,81 | 1,34 | 0,089 | 33,04 | 1,29 | 446,0 | 52,8 | 788
Ne | 20,18 | 27,17 | 1207 | 9,58 | 0,90 | 44,5 | 2,73 | 85,8 | 126,0 | 1341
N2 | 28,01 | 77,3 | 808 | 4,62 | 1,25 | 126,2 | 3,39 | 199,0 | 175,0 | 646
O2 | 32,00 | 90,2 | 1140 | 4,47 | 1,43 | 154,6 | 5,04 | 213,0 | 255,0 | 797
CH4 | 32,00 | 111,6 | 423 | 1,82 | 0,717 | 190,5 | 4,60 | 510,0 | 232,0 | 590

## Slide 5: Energy release potential of liquid cryogens
Consider vessel containing volume V of liquid cryogen at saturation (Tsat) and atmospheric pressure, environment at Ta
  What is the energy release potential of that liquid?
  How much damage can be done by releasing it to the environment?
Technical answer depends upon the details of the process, but… thermodynamics can set upper boundaries to answer these questions
  Cooling of equipment (thermal energy): first principle
  Mechanical damage (mechanical energy): second principle
Tsat
Ta
Heat
Mechanical
V
Environment
Courteasy Ph. Lebrun

## Slide 6: Cooling of equipment: thermal energy
Heat needed to vaporize mass m of liquid and warm resulting vapour up to temperature T
Q(T) = m Lv + m Cp (T-Tsat)
  Case 1: 1000 liter (125.2 kg) liquid helium at 4.2 K, 1 bar Lv = 20.8 kJ/kg Cp ≈ 5.2 kJ/kg.K
  Case 2: 1000 liter (806.6 kg) liquid nitrogen at 77.2 K, 1 bar Lv = 199.3 kJ/kg Cp ≈ 1.05 kJ/kg.K
First principle of thermodynamics (energy conservation): Q is drawn from the environment of the fluid, where it will cool mass M of equipment from Ta down to temperature T Q(T) = M [h(Ta)-h(T)] h(T) enthalpy of material
  Applications: 1 ton of iron 10 tons of iron
Courteasy Ph. Lebrun

## Slide 8: Mechanical energy release
Upper bound set by 2nd principle of thermodynamics (Carnot)
Mechanical energy W
  extracted from heat Q at T
  by Carnot engine rejecting at Ta
  W = Q (Ta/T – 1)
Consider only heat of vaporization at Tsat W = m Lv (Ta/Tsat – 1)
  Case 1: 1000 liter liquid He at 4.2 K (Ta/Tsat – 1) ≈ 68 W ≈ 177 MJ (~ 65 kg TNT)
  Case 2: 1000 liter liquid N2 at 77.2 K (Ta/Tsat – 1) ≈ 2.76 W ≈ 443 MJ (~ 163 kg TNT)
Real process
  efficiency < Carnot
  also include specific heat of vapour
  see examples later
Tsat
Ta= 290 K
Heat Q+W
Mechanical W
V
Environment
Carnot engine
Heat Q
Courteasy Ph. Lebrun

## Slide 9
Outline
Why the Risk Analysis of Cryogenic Distribution System is recommended.
Metodology proposed by WUST
RAMI approach
Risk analysis examples – LHC, ESS distribution systems
Conclusions

## Slide 10: Risk Analysis – aim and scope of the task
Identification of all risks for personnel, equipment and environement caused by the failure of Cryogenic Distribution System and that can not be avoided by design.
Classification of all failures to determine worst case scenario – based on RAMI approach
Risk analysis gives possible causes and consequences, event scenarios and repair schedules of all recognized system failure modes.

## Slide 11
Each cryogenic node - component of the machine like transfer line, pipe, vessel, heat exchanger, cryostat can be treated as a separate helium enclosure, characterized by the amount and thermodynamic parameters of enclosed helium.
Cryogenic node – a single element of the cryogenic system
Risk analysis of Cryogenic Distribution Systems

## Slide 12: Possible failures of cryogenic node followed by the cryogen discharge
Mechanical break of warm vacuum vessel
Fast degradation of vacuum insulation with air
Intensive heat flow to the cryogen
Magnet quench (optionally)
Pressure increase of the cryogen
Opening of the safety valve
Cryogen discharge through the safety valve
Mechanical break of cold vessel
Fast degradation of vacuum insulation with cryogen
Intensive heat flow to the cryogen
Magnet quench (optionally)
Pressure increase of the cryogen and in the vacuum space
Opening of the rupture disk and/or safety valve
Cryogen discharges through the rupture disk and/or safety valve
qm
p
qm

## Slide 13: Categorization of the failures
The failures are categorized according to the criticality rate of the failure:
failure occurence rate
(based on probability data)
severity rate to the machine
(based on the helium flow and the failure location)
severity rate to the personnel
(based on oxygen deficiency hazard)
M. Chorowski, J. Fydrych, M. Grabowski, Risk Analysis of the ITER cryodistribution system, Technical Report WUT-IO_TR_015-1010

## Slide 14: Risk assessment – RAMI approach
Criticality rate of the failure
failure occurence rate
(based on probability data)
severity rate to the machine
(based on estimated time to restart experiment)
severity rate to the personnel
(based on oxygen deficiency hazard)

## Slide 15: Failure criticality rate

## Slide 16: Failure criticality rate
Cumulative failure rate, CFR |  |  | OCC
 | CFR | < 0.0005 | 1
0.0005 ≤ | CFR | < 0.005 | 2
0.005 ≤ | CFR | < 0.05 | 3
0.05 ≤ | CFR | < 0.5 | 4
0.5 ≤ | CFR | < 5 | 5
5 ≤ | CFR |  | 6

## Slide 17: Occurance rate OCC
Defect | Failure rate
Cold weld ruture | 5.2610-5 m-1year -1
Cold pipe leakage | 5.2610-6 m-1year -1
Cold pipe rupture | 4.3810-5 m-1year -1
Cold bellows rupture | 8.7610-5 year -1
Vacuum jacket rupture | 8.7710-3 year -1
Electrical joint failure | 1.210-1 year -1
Capilary break | 2.010-8 year -1
Warm line leakage | 8.810-7 year -1
Probabilities of defect occurrence (failure rates) of the most common defects:
T. Peterson, Helium and nitrogen ODH analysis for ICB Engineering Laboratory, Fermilab, 1991
M. Chorowski, J. Fydrych, M. Grabowski, Risk Analysis of the ITER cryodistribution system, Technical Report WUT-IO_TR_015-1010

## Slide 18: Failure criticality rate
Cumulative failure rate, CFR |  |  | OCC
 | CFR | < 0.0005 | 1
0.0005 ≤ | CFR | < 0.005 | 2
0.005 ≤ | CFR | < 0.05 | 3
0.05 ≤ | CFR | < 0.5 | 4
0.5 ≤ | CFR | < 5 | 5
5 ≤ | CFR |  | 6
 | Helium at ambient temperature | Helium at low temperature | 
 | HRL, WRL, quench line | Auxiliary system (DFB, QRL) | LHC
Maximum mass flow rate, kg/s | SEVM | SEVM | SEVM
Leakage | 1 | 1 | 1
1 – 15 | 1 | 2 | 2
15.1 – 20 | 3 | 4 | 4
more than 20 | 4 | 5 | 6

## Slide 19: Failure criticality rate
Cumulative failure rate, CFR |  |  | OCC
 | CFR | < 0.0005 | 1
0.0005 ≤ | CFR | < 0.005 | 2
0.005 ≤ | CFR | < 0.05 | 3
0.05 ≤ | CFR | < 0.5 | 4
0.5 ≤ | CFR | < 5 | 5
5 ≤ | CFR |  | 6
Oxygen concentration, % | SEVP
21 – 18 | 1
18 – 15 | 2
15 – 12 | 3
12 – 10 | 4
10 – 6 | 5
6 – 0 | 6
 | Helium at ambient temperature | Helium at low temperature | 
 | HRL, WRL, quench line | Auxiliary system (DFB, QRL) | LHC
Maximum mass flow rate, kg/s | SEVM | SEVM | SEVM
Leakage | 1 | 1 | 1
1 – 15 | 1 | 2 | 2
15.1 – 20 | 3 | 4 | 4
more than 20 | 4 | 5 | 6

## Slide 20: The criticality matrix – basis for decisions mitigating the risk
System in design phase
System under operation
A – The personnel access restrictions
B1/B2 – The changes possible in the machine design phase
C1/C2 – The changes possible in the machine consolidation phase

## Slide 21
Outline
Why the Risk Analysis of Cryogenic Distribution System is recommended.
Metodology proposed by WUST
Risk analysis examples – ESS distribution system
Conclusions

## Slide 22: ESS Linac CDS – function and layout
Endbox
Cryogenic
Transfer
Line (65 m)
Splitting
box
Cryogenic
Transfer Line
Linac Cryogenic Distribution System
Cryogenic Distribution Line (255 m, 30 valve boxes)
Cryogenic Distribution Line (55 m, 13 valve boxes)
13 branch cryolines
CDS for the elliptical linac
(Polish in-kind, WUST)
CDS for the spoke linac
(French in-kind, CNRS)
Cryogenic Distribution Line
with 30 valve boxes
Cryogenic Distribution Line
with 13 valve boxes
Auxiliary process lines
30 branch cryolines

## Slide 23: 3D model of the Valve Box for CDS-EL

## Slide 24: Identification of the CDS’s nodes

## Slide 25: Identification of the CDS’s nodes
Cryogenic Transfer Line incl. Splitting Box – F1

## Slide 26: Identification of the CDS’s nodes
Cryogenic Distribution Line incl. End Box – F2

## Slide 27: Identification of the CDS’s nodes
Valve Box – F3

## Slide 28: Identification of the CDS’s nodes
Auxiliary Lines – F4

## Slide 29: Cryogenic failure modes identification
No. | Cryogenic failure mode
1. | Air flow to insulation vacuum
2. | Helium flow to insulation vacuum
3. | Air flow to sub-atmospheric helium
4. | Pressurized He flow to sub-atmospheric helium
5. | Helium flow to environment
6. | Air flow to sub-atmospheric line
7. | He flow to sub-atmospheric line

## Slide 30: Recognized failures of the CTL

## Slide 31: Conclusions of the ESS cryogenic distribution system risk analysis
17 different failure modes of the CDS have been recognized, analyzed and classified
Based on RAMI approach worst case scenarios have been identified for both operation and cool down modes.

## Slide 32
Outline
Why the Risk Analysis of Cryogenic Distribution System is recommended.
Metodology proposed by WUST
Risk analysis examples – LHC cryogenic system
Conclusions

## Slide 34: Cryogenic node – simplest element of the cryogenic system – basis for the risk analysis
Each component of the machine like pipe, vessel, heat exchanger, and cryostat can been treated as separate helium enclosure, characterized by the amount and thermodynamic parameters of helium.

## Slide 35: Possible failures of cryogenic node followed by the cryogen discharge
Mechanical break of warm vacuum vessel
Fast degradation of vacuum insulation with air
Intensive heat flow to the cryogen
Magnet quench (optionally)
Pressure increase of the cryogen
Opening of the safety valve
Cryogen discharge through the safety valve
Mechanical break of cold vessel
Fast degradation of vacuum insulation with cryogen
Intensive heat flow to the cryogen
Magnet quench (optionally)
Pressure increase of the cryogen and in the vacuum space
Opening of the rupture disk and/or safety valve
Cryogen discharges through the rupture disk and/or safety valve
qm
p
qm
In LHC – to header D
In LHC – to header D

## Slide 36: Possible failure modes of the LHC cryogenic system
1 Air flow to insulation vacuum
2 Helium flow to the insulation vacuum
3 Air flow to the sub-atmospheric helium
4 Helium flow to environment
5 Air flow to beam vacuum
6 Helium flow to beam vacuum
7 Pressurised helium flow to sub-atmospheric helium
8 Energy release to cold mass helium due to magnet quench
9 Energy release to cold mass helium due to electrical arc
LHC Project Note 177

## Slide 37
LHC Project Note 177
(resulting from
5 cm2 hole)

## Slide 38: Risk analysis – worst case scenario analysed – full break of jumper connection

## Slide 39: Can the helium discharge be avoided? Geneva, 19 September 2008:
„Investigations at CERN following a large helium leak into sector 3-4 of the Large Hadron Collider (LHC) tunnel have indicated that the most likely cause of the incident was a faulty electrical connection between two of the accelerator’s magnets. Before a full understanding of the incident can be established, however, the sector has to be brought to room temperature and the magnets involved opened up for inspection. This will take three to four weeks. Full details of this investigation will be made available once it is complete”.

## Slide 40: Not foreseen in PRA: pressurization of the vacuum space

## Slide 41: Damage caused by the pressurization of the vacuum space

## Slide 42: Preliminary Risk Analysis update
Redefinition of Maximum Credible Incident with respect to He flow to cryostat insulation vacuum – full cut of interconnecting pipes
Development of mathematical model
Modeling of the 19. Sept. 08 incident
Modeling of the MCI (Maximum Credible Event)
  original SV scheme
  temporary SV scheme
  final SV scheme
Analysis of the pressure rise in the LHC tunnel following the helium significant discharge
Conclusions

## Slide 43: Preliminary Risk Analysis update: STEP 1: Redefinition of Maximum Credible Incident with respect to He flow to cryostat insulation vacuum – full cut of interconnecting pipes
Interconnection pipe | PRA (LHC PN 177) cm2 | 19. Sept. 08 , cm2 | MCI, cm2
Bus-bar piping | 5 | 2 x 32 | 6 x 32
Line E | 0 | 2 x 50 | 2 x 50
Line C via Line C’ | 0 | 1.8 | 2 x 1.8
080919 incident
A limiting factor which has to be taken into account is the available free cross-section for
longitudinal flow in the magnet cold-mass lamination, limited to about 60 cm2. Therefore,
even in the case when breaches appearing in the interconnection are larger than 2 x 60 cm2,
the magnet laminations will limit the total effective opening to 120 cm2.

## Slide 44: Preliminary Risk Analysis update: STEP 2 –Development of mathematical model
Vacuum vessel
Thermal shield
Cold mass
Holes 2x32cm2 @ t=0s
Holes 2x30cm2 @ t=22s
2xSV
pset=1.07bar
3xQV
pset=17bar
qRateQuecnch – heat transfer to Cold Mass helium from quenched magnets
qRateArc – heat transfer to helium from electrical arc
qRate01 – heat transfer to Vacuum helium form Vacuum Vessel
qRate21 – heat transfer to Vacuum helium form Aluminum Shield
qRate13 – heat transfer to Cold Mass helium from Vacuum helium
Thermodynamic model input:

## Slide 45: Magnet quench heat transfer to cold mass helium – data from String experiments
M. Chorowski, P. Lebrun, L. Serio, R. van Weelderen - Thermohydraulics of Quenches and Helium Recovery in the LHC Magnet Strings - LHC Project Report 154
Data have been scaled according to the equation

## Slide 46: Electrical arc heat transfer to helium – data from 19. Sept. 08 incident
A Perin - “LHC Project Report 1168 - Annex F: Estimation of the mass flow of helium out of the cold masses and of the pressure evolution in the cryostat of sub-sector 23-25 „
Data for Iarc=8.7kA:
Conservative scaling with the current:

## Slide 47: Gas helium heat transfer - convection heat transfer
Heat transfer from Vacuum Vessel to Vacuum helium – QRate01
Heat transfer from Aluminum Shield to Vacuum helium – QRate21
Heat transfer from Vacuum helium to Cold Mass helium – QRate13
Cold Mass
TAl
Tvv=300K
Tv
Al.. Shield
Vacuum Vessel
QRate13
Tc
QRate21
QRate01
Tc, Tv – helium temperature in Cold Mass, Vacuum
TAl, Tvv –temperature of Vacuum Vessel, Aluminum Shield
Ac, AAl, Avv – area of Cold Mass, Aluminum Shield, Vacuum Vessel

## Slide 48: Model tuning – the only parameter to tune the model was the natural convection heat transfer coefficient
Evolution of the helium temperature and pressure in Cold Mass
Measured and calculated data for 080919 LHC failure
pCM=16bar

## Slide 49: Modelling of 19. Sept. 08 incident
Sequence of events
19. Sept. 08 Incident | 
Time | Event
t=0 | M3 pipe break, hole area: 2x32 cm2 caused by Electrical arc at I=8.7kA
t=5s | Quench of 4 magnets for I=8.7kA
t=22s | pipe break, hole area: 2x30 cm2

## Slide 50: Maximum Credible Incident analysis
Sequence of events – comparison with 19. Sept. inc.
19 Sept. 08 incident | 
Time | Event
t=0 | M3 pipe break, hole area: 2x32 cm2 caused by Electrical arc at I=8.7kA
t=5s | Quench of 4 magnets for I=8.7kA
t=22s | pipe break, hole area: 2x30 cm2
MCI | 
Time | Event
t=0 | Pipe break with total area of the holes: 6x32 cm2 = 192 cm2 but Cold Mass free flow area is 60cm2 and Quench of all (16) magnets at I=13.1kA caused by Electrical arc at I=13.1kA

## Slide 51: Model validation: 19. Sept. 08 incident modeling results vs. measured data
Measured and calculated data for the 19. Sept. 08 incident (LHC Project Report 1168 )
Modeling results
CERN data
WUT calculations

## Slide 52: Vacuum vessel safety valves (SV) schemes
Prior to
19.Sept. 08 incident SV scheme
Final SV scheme
Temporary SV scheme

## Slide 53: Modeling results for redefinedMCI with temporary SV scheme
Helium mass flow thought holes, SV and QV valves

## Slide 54: Modeling results for redefined MCI with final SV scheme
Helium mass flow thought holes, SV and QV valves

## Slide 55: Helium propagation, tunnel pressurization and ODH
During the incident the amount of about 6 ton of helium has been released into the LHC tunnel in the way that can be classified as a physical phenomenon with a high rate volume production.

## Slide 56: The observed oxygen concentration decrease was in good agreement with a small scale modelling of the helium discharge to the LHC tunnel mock-up
0
5
10
15
20
0
0.2
0.4
0.6
0.8
1
180
200
220
240
260
280
300
0
0.2
0.4
0.6
0.8
1
O
2
concentration, %
Temperature, K
h / D
h / D
Test set-up
build and operated at WUT
Visualisation results
LHe
Air
LHe
Measurement results

## Slide 57: As well as with a full scale modelling of the helium discharge to the LHC tunnel mock-up
Cold helium propagation
in the LHC tunnel
Large scale
experiment at CERN

## Slide 58: Conclusions
Risk analysis for PIP II Cryogenic Distribution System is recommended
The analysis should be based on WUST experience with other similar systems (ESS, XFEL, LHC, ITER), the metodology takes into account both physics and RAMI approach
The cheapest intervention is during the design phase