## Slide 1
DVB design
Pawel Duda / Wroclaw University of Science and Technolog
PIP-II Technical Workshop
13/07/2022

## Slide 2
Outline
CDS overview
DVB overview
  PID diagram
  process pipes design
  thermal shield design
  vacuum vessel and external supports design

## Slide 3
CDS overview
Cryogenic distribution system

## Slide 4
DVB overview
Cold Box
Connection
3m high
7.8m long with a Cold Box connection
5m without a CB connection
1.5m in diameter
ITL Connection

## Slide 5
DVB overview
Fixed Support
Sliding Support
Warm Manifold
Main process lines
HTTS Return (80K; 20 bara)
HTTS Supply (40K; 20 bara)
LTTS Return (9K; 20 bara)
4.5 K Supply (4.5K; 20 bara)
2 K Return (3.8K; 4.1 bara)
Cooldown Return (80K; 20 bara)

## Slide 6
DVB PID diagram
Process
valves
Warm He supply
to CDS
Main process lines
HTTS Return (80K; 20 bara)
HTTS Supply (40K; 20 bara)
LTTS Return (9K; 20 bara)
4.5 K Supply (4.5K; 20 bara)
2 K Return (3.8K; 4.1 bara)
Cooldown Return (80K; 20 bara)
Cooldown valves
Flow meter

## Slide 7
Process pipes design
Main process lines
HTTS Return (80K; 20 bara)
HTTS Supply (40K; 20 bara)
LTTS Return (9K; 20 bara)
4.5 K Supply (4.5K; 20 bara)
2 K Return (3.8K; 4.1 bara)
Cooldown Return (80K; 20 bara)
Process pipes are covered with 10 layers of MLI at layer density of ≤ 20/cm

## Slide 8
Process pipes design – 2K Return frame
Teflon plate on horizontal surfaces
Fixed connection between frame and 2K Return
Support for the flow meter

## Slide 9
Process pipes design - shape compensation
Fixed Support
Fixed Support
Fixed Support
Fixed Support
„0” point
Movement
Compensation arm

## Slide 10
Process pipes design – TS cooling loop
Main process lines
HTTS Return (80K; 20 bara)
HTTS Supply (40K; 20 bara)
LTTS Return (9K; 20 bara)
4.5 K Supply (4.5K; 20 bara)
2 K Return (3.8K; 4.1 bara)
Cooldown Return (80K; 20 bara)

## Slide 11
Thermal shield design
Main Part:
aluminium 1050 sheet
wall thickness of 10 mm
Pipe Parts:
aluminium 1050 pipe segments
diameter of 700 mm and 560 mm
wall thickness of 5 mm
The shield is covered with 40 layers of MLI at layer density of ≤ 20/cm

## Slide 12
Thermal shield design

## Slide 13
Thermal shield design
Possibility of movement -

## Slide 14
Thermal shield design

## Slide 15
Thermal shield design – thermalization method

## Slide 16
  Vacuum vessel and external supports design
Welding point for warm manifolds frame

## Slide 17
  Vacuum vessel and external supports design
The adjustability of the external supports for mounting will be not less than ± 10 mm in all planes.

## Slide 18
  Vacuum vessel and external supports design
The fixed support need to be anchored to the platform using 4 anchor bolts per leg with the size of M16

## Slide 19
  Vacuum vessel and external supports design
slide in the x-y plane
each bracket should be anchored to the platform using 4 bolts in size of M8 to fix its z-position
5mm
+/- 20mm
Teflon plates
Bracket for support
Bracket for support
Bracket for teflon plates