## Slide 1: DAPHNE Changes
T Shaw
1 JULY 2022
V2a

## Slide 2: PDT006A Recommendations
Sheet 10
PDT006A DC/DC converter recommendations ->
Not sure where current values came from
Milano group requests:
For +5.5A(voltage) U43
Lower output to +5V by changing R351 to 2.7Kohm
Change Rtune from 100 ohm to 270 ohm
Change Ctune from 10nF to 2200pF

## Slide 3: PDT006A Recommendations
Sheet 10
PDT006A DC/DC converter recommendations ->
Not sure where current values came from
For +5A(voltage) U42
Change Rtune from 100 ohm to 270 ohm
Change Ctune from 10nF to 2200pF
For +3.3V U39
Change Rtune from 100 ohm to 180 ohm
Change Ctune from 10nF to 3300pF
Do we want to change anything else – multiple DC/DC converters on that page?

## Slide 4: PDT006A Recommendations
Do we want to do anything with low voltage digital rails?
Sheet 10
PDT006A DC/DC converter recommendations ->
Not sure where current values came from
For +1.8V U36
Change Rtune from 100 ohm to 180 ohm
Change Ctune from 10nF to 4700pF
Adjust Co?
For +1.0V U33
Change Rtune from 100 ohm to 180 ohm
Change Ctune from 10nF to 3300pF
Adjust Co?

## Slide 5: TPS7A9201 layout – U17, U19, U35, U37, U40, U44 sheet 10
We are NOT currently following recommendation for 10nF capacitor placement - FIX

## Slide 6: MAX38908 – U 15 sheet 10

## Slide 7: LT3571
Tie Sync to GND?

## Slide 8: SiPM Bias filter
Sheet 2 (x5)
Change R217 from 49.9ohm to 1Kohm
Change R186 from 33nF to 1uF (200 WVDC)
Sheet 2 (x5)
For Bias, split 2Kohm resistor and add DNS 1uF (200 VDC) capacitor to ground at mid point.
Mark as DNS in schematic

## Slide 9: Trim Voltage filtering near analog Mux
Sheet 2 (x5)
Put in filter circuit which allows for selection of Patch 1,2,or 3
For Trim. Need to decide before sending to assembler.
Sheet 3 (x5)
Add power supply filter to Trim op amp – BOTH power rails V+ and V-
100nF capacitor
22uH Ferrite
IHLP2020CZER220M11 L inductor SMT Fixed Inductors Commercial Low DCR Series 22uH 1.9A 270mΩ 20%

## Slide 10: DC blocking Capacitors
Sheet 2 (x5)
Change 10nF capacitors to 100nF
  Suggest selecting 200DCWV

## Slide 11: Other
Sheet 8
  Two Dual transmit SFP+ packages changed to four 10GBASE-SR SFP+ 850nm transceivers
  Looks like above included in 28 JUNE schematic. Need to verify new FPGA connections as well.

## Slide 12: Other
Sheet 6
  Check open pin 9 on SFP package J3 – should be grounded
Sheet 2
  For xfmr chip, R116-R123 should be DNS - OK
  Also, R124-R131 should be changed from 49.9 ohms to 100 ohms
Sheet 10
  Verify L10 footprint fixed
Sheet 6
  Does X1 output need 49.9ohm termination at load?
  Verify X5 output clock termination at load.
Sheet 11
  J23 pin 3 is a “TX_Disable” pin, it is noted as TX enabled. Correctly connected to GND. (Text only correction)

## Slide 13: Other
Sheet 10
  Verify cell shape of U15 MAX38908 (analog voltage for AFE) – also verify layout has no choke points for current

## Slide 14: Optional GND connections
Sheet 5
  Change R72 from 0 to 100 ohms for consistent GND to AGND connections

## Slide 15: Chassis Fab
Need to make this priority as soon as all connector placements locked in.
No connector shell or mating connector should make electrical/conductive contact with the chassis other than LVDC input – J12 (Sheet 10)