## Slide 1: MAP HTS Magnet Workshop Welcome
M.A. Palmer
MAP Director
May 30, 2012

## Slide 2: Welcome
First, thanks to all of you for coming. We’re looking forward to a productive two days…
Our goal for this workshop is to review the status of the conductors that will enable the construction of very high field accelerator magnets…
In our effort to demonstrate the feasibility of a neutrino factory or TeV-scale muon collider, the Muon Accelerator Program represents the high energy physics effort most critically tied to capabilities in this area.

## Slide 3: Technical Challenges - Cooling
Some components beyond state-of-art:
  Very high field HTS solenoids (30-40 T)
  High gradient RF cavities operating in multi-Tesla fields
Development of a cooling channel design to reduce the 6D phase space by a factor of O(106) → luminosity of O(1034) cm-2 s-1
R. Palmer
Emittance Reduction via Ionization Cooling for an Energy Frontier Muon Collider
The program is targeting critical magnet and cooling cell demonstrations on the 3-5 year timescale!

## Slide 4: Muon Collider Magnet Needs
Accelerator systems for a muon collider require magnets beyond the current state of the art
  Very high fields
  Operation in high radiation environments
  Very high current densities
  Good mechanical stability of conductor
Application | Field (T) on Beam Axis | Current Density Required | Field Quality Required | Stored Energy
Pion Capture | 15-20 | Low | Low | High
6D Cooling | ≤20 | High | Low | Moderate
Late 6D Cooling | ≤25 | High | Low | Moderate
Final Cooling | 30-40 | Moderate | Low | High
Collider Ring Interaction Region Magnets | ≥12 | Moderate | High | High
Collider Ring Dipoles | ≥10 | Moderate | High | High
High Temperature Superconductors can meet these needs – but their development requires support!

## Slide 5: Recent MAP-related HTS Efforts
Progress towards a demonstration of a final stage cooling solenoid:
Demonstrated 15+ T (16+ T on coil)
  ~25 mm insert HTS solenoid
  BNL/PBL YBCO Design
  Highest field ever in HTS-only solenoid (by ~1.5×)
Preparing for a test with HTS insert in NC solenoid at NHFML a >30 T
BSCCO-2212 Cable -
Transport measurements show that FNAL cable attains 105% Jc of that of the single-strand
Multi-strand cable utilizing chemically compatible alloy and oxide layer to minimize cracks

## Slide 6: Goals and Structure I
Goals
  Identify the critical path R&D issues that will impact our ability to carry out critical feasibility demonstrations on the 3-5 year
  Assess how we can best direct constrained resources to facilitate the critical path R&D
  At the same time, assess what needs to be done for the long-term needs for the entire program (and for HEP needs more generally)
  a Provide inputs to our program planning
Talks
  For this very compact workshop, we need to target the critical R&D issues
  a We need to know what does and doesn’t work
  While there has been a great deal of excellent R&D over the last several years, we need your help to stay focused primarily on the items that can determine our path forward.
  Please try to stay within your allotted times…

## Slide 7: Goals and Structure II
Discussions
  30 minutes at the conclusion of each session
  Will attempt to sum up our conclusions for each conductor at the end of the talks tomorrow morning
    R&D Tasks and Priorities
    Resources required
    Risk factors
Advisory Panel
  Tasked with looking at these issues from a programmatic view
  Will provide an evaluation specifically directed at MAP needs for the next 2-3 years and beyond
Particularly in the context of MAP 3-5 year needs

## Slide 8: Some Practical Issues
Please upload your talks to the Indico site or put on the USB sticks that Tengming and Vito are passing around
Any questions about arrangements, just find
  Tengming
  Vito
  Elaine
  Myself