## Slide 1: PDS DQM Discussion
David Christian
Fermilab
July 26, 2022

## Slide 2: PDS Data
Raw data is 14-bit ADC values (sample rate = 62.5 MHz = 1/16ns)
  Integers 0 - 16383
16 14-bit values are packed into 7 32-bit words in the data frame transmitted to FELIX
Response to an impulse of light is a negative going pulse with a fast (<100ns) rise time. The pulse returns to zero in ~1 microsecond. There is a slower overshoot that returns to zero in ~6 us more.
The current plan is for “self-triggered” readout
  A waveform snippet will be read out for each “hit” over threshold
  Currently 320 samples are included in the snippet (5120 ns); this will likely increase to 512 or 1024.
  The waveform snippet will include samples before the hit (likely 32 or 64)
We would also like to be able to read out untriggered (streaming) data for debugging purposes, but this has not yet been agreed with the DAQ group
I don’t know who will write the unpacking routine
  PDS Consortium needs to provide unpacking

## Slide 3: What should be monitored? (first thoughts)
Histogram of hit channels (hit frequency/dark count rate)
Pedestal (from the first n samples of each record)
Individual hit display (waveform snippet)
Histogram of integrated charge
  Need to identify pulses & integrate area in each pulse
  PDS group to supply algorithm (deconvolution & integration)
Extreme values?
FFTs (average of n FFTs?)
  Value will depend on the number of samples
  Bin width in frequency = 31.25 MHz divided by (# of samples)/2
Time distribution of hits (histogram)?
  Per channel
  Per APA?

## Slide 4: PDS To Do
Unpacking routine
Hit finding/integration
Sample data (real or simulated)
  Cold box data?
  Data from supercell test in LN2?