## Slide 1: Analysis on Bandpass Calibration for Tianlai Cylinder
Jixia Li
NAOC
2022/8/29

## Slide 2: Bandpass Calibration
Smooth frequency is important for foreground removal.
180322 data
144 frequency points (For Tianlai cylinder: observed in 576 frequency points, i.e. 4 points averaged).
Randomly choose some pixels in the sky map, as shown in top left figure.

## Slide 3: Bandpass Calibration
Smooth frequency is important for foreground removal.
180322 data
144 frequency points (For Tianlai cylinder: observed in 576 frequency points, i.e. 4 points averaged).
Spectrum of randomly chosen sky pixels – blank sky
(Left and right for different frequency channels)
Rapid fluctuations vs frequency!
Randomly choose some pixels in the sky map, as shown in top left figure.

## Slide 4: Bandpass Calibration
Spectrum of bright source sky pixels
(Left and right for different frequency channels)
Smooth frequency is important for foreground removal.
180322 data
144 frequency points (For Tianlai cylinder: observed in 576 frequency points, i.e. 4 points averaged).
Choose some pixels in the sky map containing bright sources, as shown in the left figure.
Rapid fluctuations over frequency!
Virgo A
Cyg A
Cas A
Blank sky
Taurus A

## Slide 5: Bandpass Calibration
Spectrum of bright source sky pixels
(Left and right for different frequency channels)
Smooth frequency is important for foreground removal.
180322 data
144 frequency points (For Tianlai cylinder: observed in 576 frequency points, i.e. 4 points averaged).
Choose some pixels in the sky map containing Cyg A, as shown in the left figure.
Cyg A
Rapid fluctuations over frequency!

## Slide 6: Bandpass Calibration
Calibration:
  : time, : frequency, : a pair of antennas forming a baseline.
  : complex gain, varying over time.
  : complex frequency-dependent gain (bandpass).
Bandpass calibration: a process of measuring and correcting the frequency-dependent part of the gains, .
No single process of bandpass calibration in tlpipe, incorporated into calibration.
  Thought to be calibrated after point source calibration (i.e. flat spectrum expected), but the fact is not.

## Slide 7: Calibrator information
Source | Flux (Jy) | Zenith Angle (degree) | Data (YYMMDD) | Transit Time (UTC+8h) | Sun contamination
Cyg A | 2980 | South 3.4 | 160927 | 09/27 21:25:46 | No
 |  |  | 170821 | 08/21 23:52:13 | No
 |  |  | 171209 | 12/09 16:35:47 | Yes
 |  |  | 180322 | 03/23 09:50:49 | Yes
Cas A | 2861 | North 14.7 | 160927 | 09/28 00:49:19 | No
 |  |  | 170821 | 08/22 03:15:47 | No
 |  |  | 171209 | 12/08 20:03:22 | No
 |  |  | 180322 | 03/23 13:14:24 | Yes
Virgo A | 353 | South 31.8 | 171209 | 12/10 09:08:39 | No
Taurus A | ~1000 | South 22.15 | 171209 | 12/11 02:09:43 | No
Low sensitivity limited bright sources

## Slide 8: Bandpass – Amplitude over Time
Step:
1. Find transit peak time;
2. Choose 5 integration time;
  ~ 20 seconds.
3. Calculate amplitude of ;
4. Average over frequency;
5. Normalize to 1;
6. Repeat days and baselines.
Cylinder naming convention
South
West
North

## Slide 9: Bandpass – Amplitude over Time
Step:
1. Find transit peak time;
2. Choose 5 integration time;
  ~ 20 seconds.
3. Calculate amplitude of ;
4. Average over frequency;
5. Normalize to 1;
6. Repeat days and baselines.
171209, Cas A, A1Y-B2Y

## Slide 10: Bandpass – Amplitude vs Frequency
171209, Cas A, A1Y-B2Y
Step:
1. Find transit peak time;
2. Choose 5 integration time;
  ~ 20 seconds.
3. Calculate amplitude of ;
4. Average over peak time;
5. Normalize to 1;
6. Repeat days and baselines.

## Slide 11: Bandpass – Amplitude vs Frequency (more results)
171209_CasA_A10X-B13X
171209_CygA_A10X-B13X
171209_CasA_B21Y-C25Y
171209_CygA_B21Y-C25Y
Conclusion 2:
Sun contamination is serious.
Use data when bright sources transit at night.
Conclusion 1:
Bandpass is stable over days.
Can average bandpass over days.

## Slide 12: Bandpass Analysis on Sources
171209_B11X_C33X
171209_B21Y_C25Y
171209_A1Y_B2Y
171209_A10X_B13X
Cas A, Taurus A
Inconsistent bandpass
Src. | Z.A. | Sun
Cas A | N14.7 | No
Tau A | S22.15 | No
Cyg A | S3.4 | Yes
Vir A | S31.8 | Yes
Sources of different declinations results in different bandpasses?
Is Taurus A too faint?

## Slide 13: Bandpass Analysis on Sources
160927_B11X_C25X
160927_A15Y_C17Y
160927_A1Y_B2Y
160927_A10X_B13X
Cas A, Cyg A
Inconsistent bandpass
Src. | Z.A. | Sun
Cas A | N14.7 | No
Cyg A | S3.4 | No
Conclusion 3:
Sources of different declinations results in different bandpasses.

## Slide 14: Bandpass Analysis on Time
Each curve is an averaged bandpass in its days’ observation.
Conclusion 4:
Bandpass is not stable over 3 weeks.

## Slide 15: Conclusions/problems for Bandpass Calibration
Bright sources  Not enough, but BP is stable over days  Average over days’ observation, but not weeks.
Sun contamination is serious  only use night transit sources.
Bandpasses are different for sources at different declinations  How to obtain bandpasses?
Next work:
Bandpasses vs declinations:
  Drone experiment?
  EM simulation?
Analysis on phase.

## Slide 16: Conclusions/problems for Bandpass Calibration
Bright sources  Not enough, but BP is stable over days  Average over days’ observation, but not weeks.
Sun contamination is serious  only use night transit sources.
Bandpasses are different for sources at different declinations  How to obtain bandpasses?
Next work:
Bandpasses vs declinations:
  Drone experiment?
  EM simulation?
Analysis on phase.
Thank you!