## Slide 1: MQXFA05 SG Data during Endurance Test, by 05/31/2022
L. Garcia Fajardo, D. Cheng, P. Ferracin, G. Vallone
08/15/2022
LBNL

## Slide 2: MQXFA05 SG Gauges Layout
Only HBM gauges are installed.
Shell gauges --- three axial locations:
  Shell gauges (T & Z): on shell 2, 4, & 7
Coil gauges (T & Z): on the axial location of 3989 mm (RE) from LE.
Rod stations are located on the RE
  Each station is full bridge with four individual gauges.
LE
RE
MID
Shell 2
Shell 4
Shell 7
Coil Stations
Coil Stations
RE axial plate assembly
Rod Stations

## Slide 3: Data Processing Chronology for MQXFA05
02/17/22  First readings
03/21/22 – 03/29/22  1st Cooldown
03/30/22 – 03/31/22  Ramp to 16230 A- Hold 30 min - ramp down to 200 A @20A/s - ramp up@20A/s to 16230 A for 5 min - ramp down to 200A@100A/s -Ramp up to 16230 A@20A/s hold for 60 min- ramp down to 0A.
03/31/22  Manual Trips 1 and 2
04/03/22 – 04/12/22  1st Warmup
04/25/22 – 04/27/22  2nd Cooldown
04/28/22  Spontaneous quench
04/29/22  30 min hold at 16230A (+/- 20A/s), 5 min hold at 16230A (+30 A/s, -100 A/s), 60 min hold at 16230A (+/- 20A/s), Manual Trip 3
05/02/22  Manual Trips 4 and 5
05/03/22  Manual Trips 6 and 7
05/04/22  Manual Trips 8 and 9
05/05/22  Manual Trips 10 and 11
05/06/22  Manual Trips 12 and 13
05/09/22  Manual Trips 14 and 15
05/10/22  Manual Trips 16 and 17
05/11/22  Manual Trips 18 and 19
05/12/22  Manual Trips 20 and 21
05/13/22  Manual Trips 22 and 23
05/16/22  Manual Trips 24 and 25
05/17/22  Manual Trips 26 and 27
05/18/22  Manual Trips 28 and 29
05/19/22  Manual Trips 30 and 31
05/20/22  Manual Trips 32, 33 and 34
05/21/22  Manual Trips 35 and 36
05/23/22  Manual Trips 37, 38 and 39
05/24/22  Manual Trip 40, 60 min hold at 16230A - Manual Trip No.41
05/25/22  30 min hold at 16230A - 4.5 K, 30 min hold at 16530A
05/26/22 to 05/31/22  2nd Warmup

## Slide 4: History plots (The magnet behavior shows repeatability during the endurance test)

## Slide 5: Coils’ axial strain. History plots
Magnet test
Magnet endurance test
Missing temperature and SG data in the 3rd thermal cycle

## Slide 6: Coils’ azimuthal strain. History plots
Strange behavior of CQ4 during temperature changes (see individual plots)
Magnet test
Magnet endurance test

## Slide 7: Coils’ axial stress. History plots
Magnet test
Magnet endurance test

## Slide 8: Coils’ azimuthal stress. History plots
CQ4 is the coil with the lowest prestress
Magnet test
Magnet endurance test

## Slide 9: Shell02 azimuthal stress. History plots
Shells don’t show signs of plastic deformation
Magnet test
Magnet endurance test

## Slide 10: Shell04 stress. History plots
Magnet test
Magnet endurance test

## Slide 11: Shell07 stress. History plots
Magnet test
Magnet endurance test

## Slide 12: Rods’ strain. History plots
The rods don’t appear to be losing preload (even though these are the rods with lower yield strength)
Magnet test
Magnet endurance test

## Slide 13: Rods’ stress. History plots
Magnet test
Magnet endurance test

## Slide 14: Coil azimuthal strain during temperature changes

## Slide 15: CQ4 azimuthal strain during temperature changes (test)
1st thermal cycle
2nd thermal cycle
Missing temperature and SG data for the 3rd thermal cycle
We saw a similar issue (even worse) with CQ4 in MQXFA11

## Slide 16: CQ4 azimuthal strain during temperature changes (endurance test)
1st thermal cycle
2nd thermal cycle

## Slide 17: First ramp (no quench or manual trip) in MQXFA05 during the test and the endurance test Ramp-up and ramp-down are averaged

## Slide 18: Coil stress increase during powering (ramps-up and down averaged) Comparison with previous magnets
MQXFA05 (test)
Ramp to 16.46 kA
Av. delta stress: 102 MPa
MQXFA05 (endurance test)
Ramp to 16.14 kA
Av. delta stress: 105 MPa

## Slide 19: Appendix

## Slide 20: E.M. Effect is Apparent on Coils and Shell 7 (this example is for magnet 5 but applies to all)
Despite not yet fully processing the files, the gauge readings of the coils and the shell 7 appear to be noisy during current ramps
Similar effects have been observed in earlier magnets
The noise on the signals is most likely from the dI/dt.
LP Filter
Cutoff frequency:0.25 Hz
Clean signal
Clean signal
Noisy signal
(note the different scale from Shells 02 and 04 plots)
Noisy signal

## Slide 21: Reference: MQXFA03 Coil Azimuthal --- over I2
LP Filter
Cutoff frequency:0.25 Hz
C204
C110
C111
C204 ramp up
C204 ramp down
C110 & 111 ramp up
C110 & 111 ramp down
The readings of this part may the combination of actual SG and inductive components
Combined the ramp up and ramp down data, the three coils actually behave identically.
The readings of the “turn around” part are likely to be combined with inductive components;
The “up-warp” on the curves of C110 & 111 may be not mechanical. It is “bended” by the field.
Inorm = 16.47 kA

## Slide 22: MQXFA04 Coil Strain --- over I2
The exact same behavior as seen in MQXFA03 (next slide).
From what we have learned from MQXFA03, there is no issue in the 10 kA ramp tests.
Inorm = 16.47 kA