## Slide 1
A Brief Overview of artdaq
The artdaq Developers
ICARUS DAQ Workshop
9 November 2022

## Slide 2: artdaq System Layout (Full)
artdaq organizes the DAQ system into “layers”, with each process in each layer sending data to each process in following layers. BoardReaders communicate with readout hardware, EventBuilders construct full events from BoardReader “Fragments”, and EVBs, DataLoggers and Dispatchers provide art environments for running experiment-specific filtering, data writing, and analysis tasks.
Routing Manager
Routing Manager
Routing Manager
Hardware
Board
Reader
Data Logger
Event
Builder
Dispatcher
Online Monitor
Hardware
Board
Reader
Data Logger
Event Builder
Online Monitor
Hardware
Board
Reader

## Slide 3: artdaq System Layout (ICARUS)
In ICARUS DAQ, the EventBuilder art processes handle writing data to file and communicate directly with the Dispatcher. RoutingManagers are not used.
Hardware
Board
Reader
Event
Builder
Dispatcher
Online Monitor
Hardware
Board
Reader
Event Builder
Online Monitor
Hardware
Board
Reader

## Slide 4: Design of artdaq - Transfers
Host 2
Host 1
Transfer plugins are used to transport Fragments between artdaq layers. artdaq provides Shared Memory, TCPSocket and Autodetect transfers
Each Transfer is a point-to-point link, between two “ranks” in the artdaq system
DataSenderManager gets information from the applicable RoutingManager to determine the destination for a given Fragment’s Sequence ID
  If RoutingManagers are not used, Fragments are sent round-robin
DataSender Manager
DataSender Manager
DataReceiver Manager
DataReceiver Manager
Shared Memory Transfer Plugin 0-2
Autodetect Transfer Plugin 1-3 (Shmem)
Auto Transfer Plugin 1-2 (TCP)
TCP Transfer Plugin 0-3
Rank 2
Rank 0
Rank 1
Rank 3

## Slide 5: Board Reader
User-defined Fragment Generator reads hardware and creates Fragments. CommandableFragmentGenerator (CFG) packages those fragments based on Data Request Mode. BoardReaderCore calls CFG::getNext function to retrieve Fragments, then calls DataSenderManager’s (DSM) sendFragment method to send them on to EventBuilders.
HW
BoardReaderCore
To EBs
CommandableFragmentGenerator
Data Sender Manager
Fragment Generator

## Slide 6: Commandable Fragment Generator
CommandableFragmentGenerator uses up to four threads for data-taking, hardware status checking, request reception and request processing. If threads are not used, calls to getNext_ and checkHW_ occur synchronously in getNext (no underscore) method.
getNext_
Fragment Buffer
Requests
Receive Requests
Apply Requests
getMonitoringDataLoop
checkHWStatus_
Fragments Output
Notes: ApplyRequests uses one of several modes (Buffer, Window, Single, Sequence, …) to match data from the buffer and send to output

## Slide 7: Event Builder/Data Logger (DataReceiverCore)
DataReceiverManager (DRM) runs a thread for each source. It reads the Fragment header and sends it to SharedMemoryEventManager (SMEM) to get the location in shared memory where the data should be placed. The Transfer Plugin is then instructed to receive data to that location. Once all Fragments for an event have been received, the Shared Memory Reader reads the event into art. The shared memory has an event-based structure, with a dual-semaphore system to synchronize access.
DataReceiverCore
Data Receiver Manager
Transfer Plugins (one per source)
art Processes
Shared Memory
Shared Memory Event Manager
Shared Memory Reader (RawInput)
artdaq art Modules
Output Plugin(s)
Fragment Header
Fragment Header
Fragment Header
Data Location
Data Location
Fragment Data
RawEvent
Request
Sender

## Slide 8: artdaq art Process
RootDAQOut
(DataLogger to Disk)
art reads from the shared memory using the SharedMemoryEventReceiver. RawInput uses the SharedMemoryReader to translate the artdaq::RawEvent objects received using SMER to art::Event objects.
Events are fed into the provided art job, and sent to the configured outputs. art is configured at initialize by the EventBuilder and DataLogger, and when the register_monitor command is received in the Dispatcher (using the art job specification contained in that command).
RawInput (Shared Memory Reader)
Shared Memory Event Receiver
artdaq art Modules
RootNetOutput
(EventBuilder to DataLogger or DataLogger to Dispatcher)
RootDAQOut
(DataLogger to Disk, Can use SelectEvents to separate into streams)
TransferOutput
(Dispatcher to Online Monitor)
art::Event
Artdaq::RawEvent
Shared Memory
Transfer Plugin
Data Sender Manager

## Slide 9: Dispatcher and Online Monitors
The Dispatcher is similar to the EventBuilder and DataLogger, except that one art process is run per Online Monitor. When the Online Monitor registers itself with the Dispatcher (during the construction of the TransferInput art source), it sends the job description for the art process on the Dispatcher.
DataReceiverCore
Data Receiver Manager
Transfer Plugins (one per source)
art Processes
Shared Memory
Shared Memory Event Manager
Shared Memory Reader (RawInput)
artdaq art Modules
Transfer Output
Fragment Header
Fragment Header
Fragment Header
Data Location
Data Location
Fragment Data
Raw Event
Online Monitors
Transfer Input
artdaq art Modules

## Slide 10: Message Logging and Metrics
artdaq uses TRACE and art’s MessageFacility for message logging and a custom metric interface for run-time metric reporting.
Designed to be a “fire-and-forget” system with minimal impact on operations
TRACE is a high-speed memory-based messaging interface
  Messages can be enabled and disabled at run-time
MessageFacility supports a plugin-based output
  artdaq provides a MessageFacility viewer for displaying messages
Metric data is aggregated on a dedicated thread
  Metric Plugins handle sending metrics to various metric reporting services
Notes: TRACE decided what to send to MessageFacility.

## Slide 11: Configuring artdaq
artdaq inherits the FHiCL configuration language from art
Each component of artdaq is individually configurable, though “sensible defaults” are used wherever possible
Many run-time configuration variables are handled by the DAQInterface run control
Complete documents are stored in the data files and in the “run_records” directory managed by DAQInterface
Some key FHiCL Parameters:
  max_fragment_size_words
  fragment_id
  request_mode
  request_windows_are_unique
  art_analyzer_count
  expected_fragments_per_event (DAQInterface book-kept)
  art_command_line (useful for debugging, can run art in GDB)

## Slide 12: Configuring artdaq
Example Configurations:
  https://github.com/art-daq/artdaq_daqinterface/tree/develop/simple_test_config
“Demo” Config
  https://github.com/art-daq/artdaq_daqinterface/blob/develop/simple_test_config/demo/component01.fcl
  https://github.com/art-daq/artdaq_daqinterface/blob/develop/simple_test_config/demo/EventBuilder1.fcl
  https://github.com/art-daq/artdaq_daqinterface/blob/develop/simple_test_config/demo/DataLogger1.fcl
  https://github.com/art-daq/artdaq_daqinterface/blob/develop/simple_test_config/demo/Dispatcher1.fcl

## Slide 13: DAQInterface
DAQInterface is a Python package which handles the tasks of configuring artdaq for a runtime environment and managing the artdaq processes throughout their lifetime
It performs a large amount of “FHiCL book-keeping” to ensure that Transfer Plugins are correctly configured to find their endpoints, and that log and output file names are specified in the desired data directories
It starts the artdaq processes using SSH, and communicates with them over XMLRPC
  It sends state transmission commands and checks the status, both to ensure that commands execute within a certain time-frame and to detect when artdaq processes exit abnormally
It also maintains the “run record”, which includes metadata about where the artdaq processes were run and the fully-resolved configuration documents

## Slide 14: artdaq Plugins
artdaq supports plugins for performing various tasks within the DAQ, including
  Data readout from hardware (FragmentGenerators)
  Metric reporting
  Message routing (See artdaq_mfextensions for examples of custom message routers)
  Data transfers
  Analysis and filtering (artdaq art Modules, which differ from standard art modules in that they should try to be self-contained (e.g., not use external database services if possible) and performant)
  Command and Control (XMLRPC is the only current plugin of this type)
  Routing Policies (FIFO, Round Robin, others)

## Slide 15: Further Reading
Wiki documentation is available on the artdaq Github repositories:
  https://github.com/art-daq/artdaq/wiki
  https://github.com/art-daq/artdaq_demo/wiki
  Migrated from Redmine wikis, some formatting and link errors may remain
Doxygen Source Code Browser
  https://artdaq.fnal.gov/Doxygen/index.html
  Services login required