## Slide 1
Raul Campos and Alex Chen
1 December 2022
PIP-II BTL Vacuum Systems
BTL Workshop

## Slide 2: Outline
Vacuum Systems Scope
Vacuum Systems Performance Requirements
Current BTL Vacuum Design Status
Vacuum System Interfaces
Summary and Path Forward

## Slide 3
Material Requirements: | Beam Transfer Line | Beam Absorber Line
Ion Pump | 53 (45 l/s) | 11 (200 l/s)
Ion pump controller | 53 | 11
Connectors & 100m cable | 106 | 22
Ion gauge | 14 | 8
Pirani gauge | 7 | 4
Gauge controller | 4 | 3
Pirani gauge cables (50-200m) | 7 | 4
Ion gauge cables(50-200m) | 7 | 4
SS beam tube, 2" dia, | 250 | 40
Cutting, welding | 1 | -
SS beam tube, 6" dia | - | 5
2" Tee's | 53 | -
6" Tee | - | 11
2" Crosses | 7 | -
Hardware + adaptor w/ cover, clamp, bellows | - | -
Inline valve for isolation | 5 | -
Pumpout port w AMV | 7 | 3
Portable pumping cart | 2 | -
Titanium Windows | - | 2
Ion pumps are located at each quadrupole:
49 regular quads
+2 (large aperture)
+6 (end of line quads)
57 TOTAL
-4 (in Absorber line)
53 (in BTL)
Vacuum Scope
Management, design, procurement, fabrication, and testing of all vacuum systems in all sections of the linac, transfer line, absorber line, and in PIP2IT including its transition to the cryomodule test stand.
Preliminary design BTL Deliverables (includes BAL, and Booster injection):

## Slide 4: Critical Requirements - Performance Requirements Physics Requirements Document is the basis; Team Center #ED0010228
 | Ion Source | LEBT | RFQ | MEBT | MEBT-DS | CMs* | Warm Units** | Trans. Section | BTL
Pressure (torr) | <10-2*** | <5x10-7 | <5x10-7 | <5x10-7 | <1x10-9 | <10-10 | <1x10-9 | <5x10-8 | <5x10-8
Leak check sensitivity (mbar-l/s) | 2x10-9 | 2x10-9 | 2x10-9 | 2x10-9 | 2x10-10 | 2x10-10 | 2x10-10 | 2x10-10 | 2x10-10
Vacuum seals joints | Metal gasket or elastomer, CF or KF |  |  |  | CF only: metal gasket only | CF only: metal gasket only |  | Weld or Metal gasket | Weld or Metal gasket
Parts cleaning | UHV procedure |  |  |  |  |  |  |  | 
Gauging | Ion gauge |  |  |  |  | CC gauge |  | Ion gauge | 
Low Particulate practice | No | No | No | No | Yes | Yes | Yes | Yes | No
Controllers | Equipped with RS485 to communicate with control system via a PLC |  |  |  |  |  |  |  | 
* Anticipated pressure value when CM is cold
**Warm units adjacent to CMs
***Operational pressure
Interface with Booster
Booster-style vacuum joins (O-rings)
Metal gaskets for instrumentation or serviceable devices, or welded joints (between magnets, less risk of leak)

## Slide 5: Current Design Status
Final design of Vacuum subsystems in progress, PDR completed in Oct 2021
  Developed P&ID for Vacuum system with pumps and gauges, with input from ED0010216 PIP-II Parameters PRD
  Performed initial vacuum pressure calculations and defined pump capacity
  Defined specifications for BTL magnets vacuum chambers
  Developed vacuum physical interface between BTL and Booster injection

## Slide 6: Vacuum Layout For Linac-BTL-BAL-Absorber-Booster
  We understand basic configuration and segmentation based on ED0010216 PIP-II Parameters PRD and initial CAD model
  Initial configuration and placement of gate valves and ion pumps has been defined roughly based on operation needs. Final locations need to be defined based on final lattice and CAD model
Section1(GV1-GV4): 26 Ion pumps; 3 gauge/pump port
Section2(GV4-GV5: 27 ion pumps; 4 gauge/pump port
Section3(GV2-Dump): 2 Ion pumps; 1 gauge/pump port
Section4(GV3-Dump): 6 Ion pumps; 2 gauge/pump port
GV1: gate valve at down stream of fast close valve, as beginning of BTL
GV2: branch for straight ahead Dump(5kW)
GV3: branch for beam dump (50kW)
GV4: divides BTL into two vacuum segments for operation/maintenance
GV5: separate from Booster vacuum
GV1
GV2
GV3
GV4
GV5

## Slide 7: Ion Pump Capacity
Vacuum pumping uses typical ion pumps
  Assuming 45 L/s Ion Pumps, distributed roughly 7m apart following quadrupoles
  Assumed 2in beamtubes for typical sections. We need to update pumping and calculations where larger aperture is needed
  Calculations based on 4 different outgassing assumptions
    Blue line is the achieved pressure after a few weeks of pump down
    Dash line assumes a loss of an ion pump – allows for reliable operation in case of failure
  We will need to simulate non typical sections (i.e. near collimators) and verify initial assumptions to verify pump capacity selection
Chart: Pressure Profile of Half Cell in BTL w 20 l/s effective pumping at midpoint
< 5E-8 Torr requirement

## Slide 8: BTL/BAL P&ID
P&ID TC F10159450 developed with initial lattice, final P&ID will use latest lattice information
  Valves are included in P&ID and need to be added to ED0010216 PIP-II Parameters PRD
  We need to develop 3D model with detailed vacuum systems

## Slide 9: BTL Vacuum Interfaces
  BTL Vacuum Interfaces outlined in Vacuum ISD ED0016361. Interface details and reference drawings and documents need to be added to ISD for BTL interfaces
    For other Vacuum subsystems, we have used Not-to-Exceed Envelopes and interface drawings to develop vacuum designs and CAD models
    We need to work with interfacing systems to detail:
      Vacuum spool sizes
      Ion pump locations – until now we have followed quads locations to define spool size and ion pump locations
      If there are locations of limited space, can ion pumps be installed on instrumentation vacuum chambers?

## Slide 10: Transition from Linac to BTL
Low-particulate vacuum
field connections
Conventional UHV
FAV
We have initial understanding of transition interface but need additional details on design and interface of systems such as
  Downstream of CMs design and integration
  RF Separators Interface

## Slide 11: BTL Magnets Interface
Vacuum systems has worked with Magnets WBS to define magnets vacuum chambers materials and surface finish requirements
BTL magnets define beampipe size and shape
Working with Margents WBS as magnets designs advance, especially switcher magnets
Charge #1b

## Slide 12: Beam Instrumentation Interface
In general, we adapt the vacuum system spools to instrumentation physical interfaces (flange size)
In case there is space limitation, we need to work with instrumentation to see if ion pumps can be installed on wire scanners vacuum chambers

## Slide 13: BTL Collimators Interface
We are working closely with Collimators team
Pump capacity and location to be verified based on vacuum calculations and proximity to collimators vacuum chamber

## Slide 14: Booster Interface
Vacuum interfaces with Booster Injection:
  BTL vacuum connection with Booster injection to use Booster-style flanges
  Ion pumps capacity is 600 L/sec (same as Booster) and quantity is 2 or 3 (depending on outgassing)
    We are working with booster injection team to verify outgassing increase due to increased temperature or beam loss
Vacuum interface with Booster:
Gate valve will separate BTL from Booster Vacuum

## Slide 15: Beam Absorber Line
Beam Absorber line basic interfaces identified. Interface details need to be defined:
Vacuum windows
  Who is designing the window
  Physical interfaces
  Operating conditions
Beampipe
  Size requirement, 2in diameter or a different size

## Slide 16: BTL/BAL Installation
We need location of devices and relative distances for final design of vacuum systems
  NTE envelopes and interface drawings, Integrated CAD models
We are a stakeholder for the integration of the 3D model and NTE envelopes but need to understand who will lead the integration efforts
Design interfaces that we’ll need to work out:
  Interfaces with structural supports for ion pumps and beamtubes
  Vacuum Joints and Interconnections - Vacuum will define magnet vacuum chambers connections to beamtubes based on experience and review with stakeholders
  Hand-off and deliverables requirements (to address installation issues)

## Slide 17: Summary and Path Forward
  Continue working with stakeholders to define interfaces with Vacuum
  Verification of vacuum loads and pump capacity:
    Booster ORBUMP magnets outgassing
    BTL collimators vacuum calculations based on pump distances
    BTL magnets vacuum chambers QC
  Develop 3D CAD model of vacuum systems integrated with the Full CAD model
    Need CAD model designs of all devices and their position on beamline. Preliminary designs from interfacing systems will help vacuum get started with CAD model
    Need interface drawings/NTE envelopes for final design of vacuum systems